## Slide 1
Key Topic 7 Settlement
ESR treatment during SCED Failures (RTCTF assigned)
Austin Rosel
ERCOT
BESTF Meeting
11/15/2019

## Slide 2: Emergency Settlement Under RTC
This presentation is in regards to ESR settlement under RTC in the event the ESR needs to “hold” the last issued SCED Base Point due to a SCED failure, or an ESR is issued an Emergency Base Point (EBP) due to an emergency condition or watch.
This is in response to an assignment from the October 30, 2019 RTCTF meeting.

## Slide 3: Emergency Settlement Under RTC
Settlement for held Base Points and EBPs under RTC.
  Resources are considered for additional compensation if the RTSPP is less than the price on the Resource’s Energy Offer Curve (capped by the MOC) at the “held” or Emergency Base Point.
  The AS price and award for the Resource will be extended and considered in the AS Imbalance Settlement until new awards and prices are created in a subsequent SCED run.

## Slide 4: RTCTF Issues to BESTF
Two issues were brought up at the RTC Task Force meeting and assigned to BESTF.
If an ESR is losing charge will they be overcompensated in the Emergency Energy Settlement?
If, during a long SCED an ESR loses the ability to supply the awarded AS are they being overcompensated for awarded AS?

## Slide 5: Issue 1
An ESR will not be overcompensated in the emergency energy settlement if they lose charge and are not able to generate at the held base point.
  The QSE is not compensated for the price difference at the issued Base Point. The quantity used in the emergency settlement calculation is the minimum of he Average Base Point and the Real-Time Metered Generation.
  This is how it works today for all Resources.

## Slide 6: Issue 2
An ESR could be overcompensated in the Ancillary Service Imbalance Settlement if an Ancillary Service award is held through a long SCED and the ESR is not able to provide the Awarded AS for the entire duration of the SCED.
This could be true for any Resource, not just an ESR.

## Slide 7: Issue 2
Should we develop a mechanism to reduce or claw-back Real-Time Ancillary Service Payments to Resources that are having AS awards held?
A possible solution is to use telemetered AS capability, and to reduce payments for RTM AS awards for any lost capacity.
Others?

## Slide 8: Issue 2
Issues:
  Relies on telemetery during a period when there are system issues.
  Could double count capability if the Resource is able to provide more than one type of AS
    The resource may keep some revenues that should be clawed back, or
    Would require developing splitting rules that would rely on ratios or something similar.
  Increased impact for initial development and subsequent system changes for a rare occurrence.

## Slide 9: Issue 2
 | Occurrence Count |  |  | Long SCED duration (in minutes) |  | 
Year | Long SCED Count | Price Correction Count due to long SCED | EBP offset count for long SCED | Maximum duration | Average duration | Minimum duration
2010 | 5 |  | 1 | 36.1 | 19.6 | 12.3
2011 | 28 | 12 | 6 | 120.6 | 27.0 | 10.2
2012 | 5 | 3 |  | 44.2 | 24.6 | 11.8
2013 | 3 | 3 | 1 | 47.7 | 38.1 | 29.3
2014 | 9 | 8 | 2 | 83.8 | 30.6 | 10.1
2015 | 10 | 2 | 2 | 79.5 | 19.4 | 7.7
2016 | 14 | 4 | 2 | 82.9 | 16.7 | 7.7
2017 | 5 | 2 |  | 17.0 | 10.5 | 7.9
2018 | 9 | 5 |  | 27.6 | 13.1 | 7.7
2019 | 2 |  |  | 13.5 | 13.4 | 13.3
Total | 90 | 39 | 14 | 120.6 | 22.1 | 7.7
Long SCED interval history

## Slide 10: Emergency Settlement Under RTC for ESR
Settlement for held Base Points and EBPs under RTC.
  ESRs are considered for additional compensation if the RTSPP is less than the price on the ESRs Energy Offer Curve (capped by the MOC) at the “held” or Emergency Base Point.
  The AS price and award for the ESR will be extended and considered in the AS Imbalance Settlement until new awards and prices are created in a subsequent SCED run.

## Slide 11: Questions?