## Slide 1
ESR Modeling in RUC and COP Submittals
David Maggio
October 18, 2019

## Slide 2: Acronyms
Ancillary Service (AS)
Current Operating Plan (COP)
Energy Storage Resource (ESR)
Fast Responding Regulation Up Service (FRRS-Up)
High Ancillary Service Limit (HASL)
High Sustained Limit (HSL)
Reliability Unit Commitment (RUC)
Security-Constrained Economic Dispatch (SCED)
State-of-Charge (SOC)

## Slide 3: Ability of RUC to Commit ESRs
In the existing RUC construct, Resources that can start very quickly (e.g., within a SCED-interval) are not generally committed through the Day-Ahead or Hourly RUC processes.
  Any recommendations from the RUC optimization would be deferred by the Operator.
  The decision on whether or not to start the Resource can effectively be made in real-time.
In the near-term, when RUC will not be designed to directly consider SOC in dispatch, are changes to the RUC optimization to view/treat ESRs differently needed?
  If not, there may be cases in which “OFF” ESRs are recommended for commitment. This would provide some indication of need.
  However, any recommendations would be deferred by the Operators.
  Will ESRs typically have a COP status of “OFF”?

## Slide 4: Modeling for ESR Dispatch in the RUC Optimization
In the near-term, not planning to have RUC consider SOC when dispatching ESRs across the RUC study period.
  This is something that would be revisited for RUC and other forward study tools as ESR penetration in the ERCOT market increases
Instead, ESRs would simply be modeled in the same way that Generation Resources are today.
  Capacity reserved for AS (e.g., capacity above the HASL) is effectively unavailable for solving transmission congestion and meeting load forecast through energy dispatch.
  Capacity below the HASL for an online ESRs can be used for energy dispatch.
Potential to use existing COP elements to reflect duration limitations for the Resource, as applicable

## Slide 5: Using COP HSLs to Reflect Duration Limitations
At a minimum, COP HSLs will need to be greater than or equal to combined amount of AS being provided by the Resource
  Under the “combination model” structure, this requirement would be specific to the Generator or Load Resource side of the Resource (i.e., the COP HSL of Generator only has to be greater than or equal to the AS being provided by the “Generator” side of the ESR).
For cases in which the ESR is not carrying AS or has additional energy that they are planning to provide to the market, thinking through the ramifications of different options:
  HSL always at the rated amount (presumably based on the inverter rating)
  HSL always set equal to the AS responsibility amount (i.e., no additional capacity available to RUC for energy dispatch)
  QSEs use HSLs to reflect duration limitations

## Slide 6: Using COP HSLs to Reflect Duration Limitations
Options 1 and 2 are the more extreme options and obvious flaws.
  Option 1 ignores duration limitations and will tend to underestimate the system needs for other Resources, creating concerns for situational awareness.
  Option 2 is conservative and would tend to lead to unwarranted commitment recommendations by RUC. May work in interim, when ESR penetration is lower, ESRs are typically shorter duration, and ESRs mostly provide AS.
What could Option 3 look like?
  Illustration of the “Generator” side COP for a 100MWh ESR with an inverter rated at 25 MW. The ESR is not planning to provide AS.
Chart: Hour
HSL | 0 | 0 | 0 | 0 | 0 | 25 | 25 | 25 | 25 | 0 | 0 | 0 | 0 | 0 | 25 | 25 | 25 | 25 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 7: Using COP HSLs to Reflect Duration Limitations
Option 3 would then get slightly more complicated from there.
  Illustration of the “Generator” side COP for a 100MWh ESR with an inverter rated at 25 MW. The ESR is planning to provide 15 MW of FRRS-Up all day and able to provide additional energy for dispatch
Chart: Hour
HSL | 15 | 15 | 15 | 15 | 15 | 25 | 25 | 25 | 25 | 15 | 15 | 15 | 15 | 15 | 25 | 25 | 25 | 25 | 15 | 15 | 15 | 15 | 15 | 15
HASL | 0 | 0 | 0 | 0 | 0 | 10 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 10 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 8: Next Steps
We’re largely looking for feedback at this point.
Ability of RUC to commit ESRs
  May be covered by existing processes in the near-term
Modeling for ESR dispatch in the RUC optimization
  Until RUC is updated to consider SOC, have treatment be in line with current Generation Resource treatment.
  In the longer-term, RUC will be updated to consider SOC.
Using COP HSLs to reflect duration limitations
  Option 3 appears to be a beneficial option. Should option 3 be applied soon with ERCOT updating the Business Practice Manual for COP expectations?
  Are there are alternative short-term proposals (E.g., that perhaps don’t use COP HSLs)?

## Slide 9: Questions