## Slide 1
Negative AS Self-Arrangement in RTC
Alfredo Moreno
December 3, 2019

## Slide 2: Negative Self-Arrangement of AS in DAM
Protocols 4.4.7.1.1(3)
  For compliance purposes, a QSE may not submit a negative Self-Arranged Ancillary Service Quantity in the DAM that is greater in magnitude than the absolute value of the net sales of its Ancillary Service Trades per Ancillary Service.
Purpose:
  Allow the selling QSE in an AS trade an avenue for having DAM procure the AS on their behalf, when they know prior to DAM they will be unable to provide AS previously sold in a bilateral trade.
    Essentially it functions as a price-taking AS bid.
    Allows QSE to avoid the illiquid SASM process in today’s market.

## Slide 3: Negative Self-Arrangement of AS in DAM
Example of negative self-arrangement use in today’s DAM:
  QSE B(buyer) and QSE S(seller) confirm a trade for AS
  QSE B self-arranges the AS
  QSE S discovers they will be unable to provide the AS for the trade prior to DAM
  QSE S negative self-arranges the AS
  The self-arrangements balance out and DAM procures the correct amount of AS
What if the behavioral rules fail?
    QSE B doesn’t self-arrange
    QSE B doesn’t enter the trade
    QSE S negative self-arranges more than net trades, etc.
  => DAM procures more than the AS plan

## Slide 4: Negative Self-Arrangement of AS in RTC
How would this work with the ASDCs in RTC?
Because the procurement is no longer a fixed quantity, to make the negative self-arrangement essentially a price-taking bid, it would shift the ASDC to the right.
It can also result in over-procuring a service, in the case of an erroneous negative self-arrangement.

## Slide 5: Example 1 : ASO curve intersects higher on Shifted ASDC
Chart: AS Demand Curve with 200 MW Negative Self-Arranged AS
| 0 | 1800 | 1858 | 2198 | 2538 | 2543 | 2548 | 2553 | 2558 | 2560.5 | 2563
RRS DC | 9000 | 9000 | 6500 | 5500 | 4500 | 2250 | 1000 | 500 | 400 | 300 | 250
RRS Offer Curve | 1 | 50 | 100 | 200 | 275 | 425 | 800 | 1050 | 1340 | 1800 | 2350
Self Arranged RRS | 0 | 0
Shifted RRS DC | 9000 | 9000 | 6500 | 5500 | 4500 | 2250 | 1000 | 500 | 400 | 300 | 250
$1018.21/MWh
Normal ASDC Price
$2014.52/MWh
Shifted ASDC Price

## Slide 6: Example 2 : ASO curve short of Shifted ASDC
Chart: AS Demand Curve with 200 MW Negative Self-Arranged AS
| 0 | 1800 | 1858 | 2198 | 2538 | 2543 | 2548 | 2553 | 2558 | 2560.5 | 2563
RRS DC | 9000 | 9000 | 6500 | 5500 | 4500 | 2250 | 1000 | 500 | 400 | 300 | 250
RRS Offer Curve | 1 | 50 | 100 | 200 | 275 | 425 | 800 | 1050
Self Arranged RRS | 0 | 0
Shifted RRS DC | 9000 | 9000 | 6500 | 5500 | 4500 | 2250 | 1000 | 500 | 400 | 300 | 250
$1018.21/MWh
Normal ASDC Price
$5002.94/MWh
Shifted ASDC Price

## Slide 7: Discussion:
How to handle negative Self-AS once DAM has ASDCs rather than fixed AS plan procurement:
  Shift the DAM ASDC when needed, such that the negative self-arrangement is “price-taking”
    Affects clearing price
    In this case, the DAM ASDC and the RT ASDC would be out of alignment
  Remove negative Self-AS as an option
    Simplifies implementation, DAM and RT stay in alignment, and AS shortages can be handled in the RT AS Imbalance
  Other?