## Slide 1
KTC 7 Item 6
ESR Reliability Instructions and Associated Settlement
David Maggio
BESTF
December 6, 2019

## Slide 2: Introduction
With the KTC language that already has consensus and other discussions at BESTF, the expectation is that ESRs will not be committed through the current DRUC/HRUC processes.
  Because of the very short lead-times, expect that commitment recommendations for ESRs can be deferred in the RUC process by the ERCOT Operator
  Don’t typically expect ESRs to have an “OFF” status, particularly in the COP. When would an ESR be “off-line but available for commitment in the DAM and RUC”?
However, there may be rare circumstances in which ERCOT will have to give reliability instructions to ESRs to operate at a certain level when they are physically able to do so.
With that potential condition, would like to discuss current thoughts on the mechanisms for those instructions, as well as, any associated Settlement for those cases.

## Slide 3: Methods for issuing reliability directives
With the very short lead-times, expectation is that any instructions to ESRs would occur in the Operating Hour based real-time system conditions and telemetry for the Resource.
In the case where the ESR is on-line and available but the issue is not being resolved through typical SCED dispatch, the ESR dispatch would be modified through HDL or LDL overrides (or some equivalent).
  This aligns with other Resource types, but different Settlement may be needed.
In the case where the ESR has a telemetered Resource status of “OFF,” the ESR would receive a Verbal RUC instruction (or some equivalent).
  Not needed if “OFF” isn’t a status used by ESRs
  Again aligns with other Resource types, but different Settlement may be needed.

## Slide 4: Methods for issuing reliability directives cont.
Focusing on LDL and HDL overrides:
LDL overrides could take the following forms:
  Instruction for ESR to charge less
  Instruction for ESR to go from charging to discharging
  Instruction for ESR to discharge more
HDL overrides could take the following forms:
  Instruction for ESR to discharge less
  Instruction for ESR to go from discharging to charging
  Instruction for ESR to charge more

## Slide 5: Current Settlement for these types of instructions
LDL overrides
  Settled through “Emergency Operations Settlement”
  Looks at the inconsistency between prices and Base Points, where the price is not sufficient to cover the cost of the Resource. Cost is based on the Resource’s EOC and capped at the MOC.
HDL overrides
  Separate Settlement where a QSE may be eligible for payments when there is demonstrable financial loss associated with the override and the QSE provides documented proof through a dispute.
  Loss is related to variable cost components of DAM obligations or energy purchase or sale provisions of bilateral contracts, not loss opportunity costs.
RUCs, including Verbal RUCs
  Separate Settlement with a focus on the eligible Startup Cost and minimum-energy cost of the Resource less revenues for the Resource.

## Slide 6: The current Settlement treatment doesn’t seem to fit well with ESRs
Current Settlement processes don’t consider opportunity costs for periods later in the day.
Discussion at BESTF is that, as a starting point, MOCs for ESRs will be at the SWCAP, effectively taking MOCs out of the equation.
Also, there is the expectation that ESRs will be able to update their EOCs in the Operating Hour.
With an HDL override, ESRs could incur real cost when being instructed to consume energy at a price higher than what is on their EOC.
There are other costs that are more specific to ESRs, such as charges allocated to Load (specifically for ESRs not getting WSL treatment) and round-trip costs.

## Slide 7: High-level discussion on Settlement of reliability instructions to ESRs
Potential impacts to the ESR may include:
  Cost of discharging below “fuel” costs (i.e., cost of consuming to store that charge)
  Cost of charging at prices above the willingness to buy, as reflected in the EOC
  Opportunity costs for periods later in the day - E.g., reliability instruction directly results in increased cost or inability to discharge during higher price periods or provide AS later in the day
  Round-trip cost
  Charges allocated to Load (specifically for ESRs not getting WSL treatment)
  Impact to real-time imbalance charges (similar to HDL overrides today)
Are there other costs?
Which ones should be eligible for Make-Whole Settlement consideration when there is a reliability instruction to the ESR?

## Slide 8: High-level discussion on Settlement of reliability instructions to ESRs cont.
What should the process be for Settlement on any associate Make-Wholes?
QSE dispute-based manual Settlement
  Manual processes can be more cumbersome, but may be okay given the expected low frequency of events for the foreseeable future.
  May allow the particularities of the case to be better captured
  Would need to have Protocol guidance on costs and impacts that would be considered
Automated Settlement process
  Are there simplifying assumptions that can be made to allow for automation in some or all conditions?
  Are the previously discussed costs inherently capture in the ESR’s EOC?
  If the EOC is used, are any Make-Whole limitations needed given the near-term decision on ESR MOCs?

## Slide 9: Group Discussion and Questions

## Slide 10: Acronyms
Ancillary Service (AS)
Battery Energy Storage Task Force (BESTF)
Current Operating Plan (COP)
Day-Ahead Market (DAM)
Day-Ahead Reliability Unit Commitment (DRUC)
Energy Offer Curve (EOC)
Energy Storage Resource (ESR)
High Dispatch Limit (HDL)
Hourly Reliability Unit Commitment (HRUC)
Key Topic/Concept (KTC)
Low Dispatch Limit (LDL)
Mitigated Offer Cap (MOC)
Qualified Scheduling Entity (QSE)
Reliability Unit Commitment (RUC)
Security-Constrained Economic Dispatch (SCED)
System-Wide Offer Cap (SWCAP)
Wholesale Storage Load (WSL)