## Slide 1
AS Offer Structure and Proxy AS Offer Creation under RTC
Hailong Hui
September 19, 2019

## Slide 2: Acronyms
Ancillary Service (AS)
Controllable Load Resource (CLR)
Day-Ahead Market (DAM)
ERCOT Contingency Reserve Service (ECRS)
Energy Offer Curve (EOC)
High Sustained Limit (HSL)
Maximum Power Consumption (MPC)
Net Power Consumption (NPC)
Non-Controllable Load Resource (NCLR)
Nodal Protocol Revision Request (NPRR)
Non-Spinning Reserve Service (Non-Spin)
Qualified Scheduling Entity (QSE)
Real-Time Co-optimization (RTC)
Regulation Down Service (Reg-Down)
Regulation Up Service (Reg-Up)
Responsive Reserve Service (RRS)

## Slide 3: Outlines
KP1.3 for AS Offer Structure and Proxy AS Offer Creation
Proxy AS Offer Creation for Generation Resources
Proxy AS Offer Creation for Load Resources
  Option1
  Option2

## Slide 4: KP1.3 for AS Offer Structure and Proxy AS offer Creation
RTC will utilize the AS Offer structure that will be in place with the implementation of NPRR863.
The AS Offer submission window will be consistent with the EOC submission window.
Proxy AS Offers will not be created for Resources for use in the DAM.

## Slide 5: KP1.3 for AS Offer Structure and Proxy AS offer Creation
Proxy AS Offers will be created for Resources for use in the Real-Time Market (RTM) using the following guidelines:
  The proxy offer will be a linked AS Offer across all AS products that a Resource is qualified to provide. For Generation Resources, the proxy offer MW will be HSL.
  For each AS where the Resource has a submitted AS Offer, the price in the proxy AS Offer for that AS will be set equal to the maximum of the Resource’s highest offer price for that AS plus a factor “K”, where “K” is a configurable parameter with a value close to zero, and a proxy price floor for that AS.
  For each AS where the Resource does not have a submitted AS Offer, the price in the proxy AS Offer for that AS will be set equal to a proxy price floor for that AS.
  The system will be designed to allow different proxy price floors for instances in which the same AS can be provided by either Off-Line or On-Line Resources (i.e., the proxy price floor for an offline Non-Spin offer may be different than the proxy price floor for an online Non-Spin offer).
  The RTC optimization will enforce various Resource specific AS constraints to ensure the AS awards are feasible, considering both QSE submitted AS offers and RTC created proxy AS Offers.

## Slide 6: Proxy AS Offer Creation for Generation Resources
On-Line upward AS Product (Reg-Up, RRS, ECRS and On-Line Non-Spin)
  For OFFQS Generation Resource qualified for ECRS and Non-Spin, On-Line ECRS and Non-Spin proxy AS Offer will be created
  Reg-Down
  Off-Line Non-Spin

## Slide 7: Proxy AS Offer for Generation On-Line Upward AS Products
RTC will create a new linked proxy offer for Online upward AS Products
  Add an additional segment MW ProxyASMW equal to HSL
    If AS Offer doesn’t exist, ProxyASMW will be the first segment
    If AS Offer exists, ProxyASMW will be an additional segment
  Add proxy AS Offer price for each qualified AS product ONLY
    The proxy AS Offer price will be empty for non-qualified AS product
AS Offer MW (up to 5 per Resource) | RegUp Price ($/MW/h) | RRS Price ($/MW/h) | ECRS Price ($/MW/h) | On-Line Non-Spin Price ($/MW/h)
ASMW1 | RegUpPrice1 | RRSPrice1 | ECRSPrice1 | ONNSPrice1
ASMW2 | RegUpPrice2 | RRSPrice2 | ECRSPrice2 | ONNSPrice2
ASMW3 | RegUpPrice3 | RRSPrice3 | ECRSPrice3 | ONNSPrice3
ASMW4 | RegUpPrice4 | RRSPrice4 | ECRSPrice4 | ONNSPrice4
ASMW5 | RegUpPrice5 | RRSPrice5 | ECRSPrice5 | ONNSPrice5
ProxyASMW | ProxyRegUpPrice | ProxyRRSPrice | ProxyECRSPrice | ProxyONNSPrice

## Slide 8: Proxy AS Offer for Generation Reg-Down
RTC will create a new proxy offer for Reg-Down only when the Resource is qualified for Reg-Down (similar logic as Online upward AS products)
  Add a new segment MW ProxyASMW equal to HSL
    If Reg-Down Offer doesn’t exist, ProxyASMW will be the first segment
    If Reg-Down Offer exists, ProxyASMW will be an additional segment
  Add proxy AS Offer price for Reg-Down
AS Offer MW (up to 5 per Resource) | RegDn Price ($/MW/h)
ASMW1 | RegDnPrice1
ASMW2 | RegDnPrice2
ASMW3 | RegDnPrice3
ASMW4 | RegDnPrice4
ASMW5 | RegDnPrice5
ProxyASMW | ProxyRegDnPrice

## Slide 9: Proxy AS Offer for Generation Off-Line Non-Spin
RTC will create a new proxy Offer for Off-Line Non-Spin for Resource with telemetry Resource Status ‘OFF’ and qualified to provide Off-Line Non-Spin
  Add a new segment MW ProxyASMW equal to HSL
    If Off-Line Non-Spin Offer doesn’t exist, ProxyASMW will be the first segment
    If Off-Line Non-Spin Offer exists, ProxyASMW will be an additional segment
  Add proxy AS Offer price for Off-Line Non-Spin
AS Offer MW (up to 5 per Resource) | Off-Line Non-Spin Price ($/MW/h)
ASMW1 | OFFNSPrice1
ASMW2 | OFFNSPrice2
ASMW3 | OFFNSPrice3
ASMW4 | OFFNSPrice4
ASMW5 | OFFNSPrice5
ProxyASMW | ProxyOFFNSPrice

## Slide 10: Proxy AS Offer Creation for Load Resources-Option1
Option 1-RTC will create a new proxy AS offer only for qualified Online AS Products for Load Resources.
  This is similar to the logic for Generations Resources.
  This is also similar to today’s proxy RTM Energy Bid creation for SCED qualified CLR:
    For qualified CLR without full range Energy Bid, extend the bid to cover the full range of the Demand response capability
    For qualified CLR without Energy Bid, create a proxy Energy Bid for the entire Demand response capability at SWCAP.
  Linked proxy AS offer for qualified Online upward AS Products for both CLR and NCLR
    Add an additional segment MW ProxyASMW equal to NPC or MPC
    Add proxy AS Offer price for each qualified AS product ONLY
      ProxyASPrice=MAX(MaxASPrice+K, FloorASPrice)
  Proxy AS offer for qualified Reg-Down for CLR
    Add a new segment MW ProxyASMW equal to MPC
    Add proxy AS Offer price for Reg-Down
      ProxyRegDnPrice=MAX(MaxRegDnPrice+K, FloorRegDnPrice)

## Slide 11: Proxy AS Offer Creation for Load Resources-Option2
Option 2-RTC will create a new proxy AS offer only for offered Online AS Products for Load Resources.
  Only create a new proxy AS offer when the Load Resource has a valid AS offer. No proxy AS offer will be created for the Load Resource without AS Offer.
  Linked proxy AS offer for offered Online upward AS Products for both CLR and NCLR
    Add an additional segment MW ProxyASMW equal to NPC or MPC
    Add proxy AS Offer price for each offered AS product ONLY
      ProxyASPrice=MAX(MaxASPrice+K, FloorASPrice)
  Proxy AS offer for offered Reg-Down for CLR
    Add a new segment MW ProxyASMW equal to MPC
    Add proxy AS Offer price for Reg-Down
      ProxyRegDnPrice=MAX(MaxRegDnPrice+K, FloorRegDnPrice)

## Slide 12: Example 1: Online Upward AS Offers for Generation Resource
Example illustrates creation of proxy On-Line upward AS Offers for a Generation Resource with 100 MW HSL and 3 segments submitted.
AS Offer MW (up to 5 per Resource) | RegUp Price ($/MW/h) | RRS Price ($/MW/h) | ECRS Price ($/MW/h) | On-Line Non-Spin Price ($/MW/h)
20 | 22 | 18 | 15 | 
30 | 23 | 17 |  | 
10 | 21 |  | 16 | 
100 | 23+K | 18+K | 16+K | FloorONNSprice

## Slide 13: Example 2: No Online Upward AS Offers for CLR
AS Offer MW | RegUp Price ($/MW/h) | RRS Price ($/MW/h) | ECRS Price ($/MW/h) | Non-Spin Price ($/MW/h)
100 | FloorRegUpprice | FloorRRSprice | FloorECRSprice | FloorONNSprice
Example illustrates creation of proxy On-Line upward AS Offers for a CLR with 100 MW NPC and no AS Offers submitted.
Option1: the proxy AS offer will be created for all qualified AS products only.
Option2: no proxy AS offer will be created since there is no submitted AS offer.

## Slide 14: Example 3: No Online Reg-Down Offer for CLR
AS Offer MW | RegDn Price ($/MW/h)
100 | FloorRegDnprice
Example illustrates creation of proxy On-Line Reg-Down offers for a CLR with 100 MW MPC and no Reg-Down offers submitted
Option1: the proxy AS offer will be created for all qualified AS products only.
Option2: no proxy AS offer will be created since there is no submitted AS offer.

## Slide 15: Example 4: Online Upward AS Offers for CLR
Example illustrates creation of proxy On-Line upward AS Offers for a CLR with 100 MW NPC and 3 segments submitted.
Option 1:the proxy AS offer will be created for all qualified AS products only.
AS Offer MW (up to 5 per Resource) | RegUp Price ($/MW/h) | RRS Price ($/MW/h) | ECRS Price ($/MW/h) | On-Line Non-Spin Price ($/MW/h)
20 | 22 | 18 | 15 | 
30 | 23 | 17 |  | 
10 | 21 |  | 16 | 
100 | 23+K | 18+K | 16+K | FloorONNSprice
Option 2: the proxy AS offer will be created for all offered AS products only.
AS Offer MW (up to 5 per Resource) | RegUp Price ($/MW/h) | RRS Price ($/MW/h) | ECRS Price ($/MW/h) | On-Line Non-Spin Price ($/MW/h)
20 | 22 | 18 | 15 | 
30 | 23 | 17 |  | 
10 | 21 |  | 16 | 
100 | 23+K | 18+K | 16+K | 

## Slide 16: Example 5: No Online Upward AS Offers for NCLR
AS Offer MW | RegUp Price ($/MW/h) | RRS Price ($/MW/h) | ECRS Price ($/MW/h) | Non-Spin Price ($/MW/h)
100 |  | FloorRRSprice | FloorECRSprice | 
Example illustrates creation of proxy On-Line upward AS Offers for a NCLR with 100 MW NPC and no AS Offers submitted.
Option1: the proxy AS offer will be created for all qualified AS products only.
Option2: no proxy AS offer will be created since there is no submitted AS offer.

## Slide 17: Example 6: Online Upward AS Offers for NCLR
Example illustrates creation of proxy On-Line upward AS Offers for a NCLR with 100 MW NPC and 3 segments submitted
Option 1:the proxy AS offer will be created for all qualified AS products only.
AS Offer MW (up to 5 per Resource) | RegUp Price ($/MW/h) | RRS Price ($/MW/h) | ECRS Price ($/MW/h) | On-Line Non-Spin Price ($/MW/h)
20 |  | 18 |  | 
30 |  | 17 |  | 
10 |  | 15 |  | 
100 |  | 18+K | FloorECRSprice | 
AS Offer MW (up to 5 per Resource) | RegUp Price ($/MW/h) | RRS Price ($/MW/h) | ECRS Price ($/MW/h) | On-Line Non-Spin Price ($/MW/h)
20 |  | 18 |  | 
30 |  | 17 |  | 
10 |  | 15 |  | 
100 |  | 18+K |  | 
Option 2: the proxy AS offer will be created for all offered AS products only.

## Slide 18: More Discussion
Determine Default AS Offer price floor for different AS products:
  Can be different for Online Non-Spin and Offline Non-Spin
  Can be different for Generation RRS and NCLR RRS
Proxy AS Offer for CLR and NCLR:
  Option1 or Option2
  Other recommendations

## Slide 19
Questions