## Slide 1
KP 1.3 (14) RTC Constraints
Update on Load Resource Self Provision of RRS and ECRS
Sai Moorty
Market Design and Analysis
December 3, 2019

## Slide 2: UFR Load Resource Treatment Under RTC
Self Provision of RRS-BLK and ECRS-BLK at individual UFR Load Resource level
Impractical to arm and disarm UFR every 5 minutes and have UFR Load Resources participate actively in RTC
Proposal is to allow self-provision of RRS-BLK and ECRS-BLK based on DAM RRS-BLK, ECRS-BLK awards, RRS-BLK, ECRS-BLK AS Trades and DAM Self-arranged RRS-BLK, ECRS-BLK within a QSE
Self-provision MW quantities of RRS-BLK, ECRS-BLK is telemetered to ERCOT by QSE for each UFR Load Resource in its portfolio:
  : Telemetry to indicate RRS-BLK MW amount self-provided by On-Line UFR type Load Resource
  : Telemetry to indicate ECRS-BLK MW amount self-provided by On-Line UFR type Load Resource

## Slide 3: UFR Load Resource: Telemetered Self-Provision Validation (RRS, ECRS)
Original proposal presented on August 9th :
  Additional ERCOT validation of QSE submitted AS Trades for RRS_BLK and ECRS-BLK to ensure respective limits on these AS sub-types are respected
    Today, AS Trades are “CONFIRMED” if the buying and selling QSE submitted AS Trades have matching first and last hours, AS-subtype, and MW quantity
    Original proposal would have introduced another check by ERCOT systems before confirming QSE submitted AS Trades
Subsequent discussions resulted in NOT introducing another check by ERCOT systems
New/Updated Proposal:
  No changes to current rules for “CONFIRMING” AS Trades
  Pro-rating rule for self-provision telemetry of RRS_BLK and ECRS_BLK from UFR Load Resource
    Tweaks to original proposal
    Yes, pro-rating rules for self-provision telemetry of RRS_BLK, ECRS_BLK are still needed
  Change system wide RRS and ECRS constraints to handle cases where self-provision of RRS_BLK and ECRS_BLK exceeds the prescribed limits on the respective AS sub-types (60%, 50%)
  Still under evaluation
    Changes to Settlements to:
      No credit to QSEs that submit AS Trades for RRS_BLK and ECRS_BLK that violate prescribed limits on those AS subtypes
      Additional charge/penalty as this behavior could impact prices (LMP, MCPC) for other products

## Slide 4: UFR Load Resource: Telemetered Self-Provision Validation (RRS, ECRS)
  Step 1 : At QSE portfolio level, check if sum of telemetered self provision of RRS is less than or equal to QSE’s RRS-BLK responsibility from DAM RRS-BLK awards, validated RRS-BLK AS Trades and Self-arrangement within QSE. Similar check for ECRS-BLK
    If not, determine a Step 1 validated self-provision amount (, ), (reduce the telemetered self-provision amounts for RRS and ECRS)
  Step 2 : For each UFR Load Resource, check if
    If not, further prorate Step 1 validated ECRS self-provision first and then Step 1 validated RRS self-provision to get Step 2 validated self-provision amount (, )
 | QSE RRS DAM & AS Trade | QSE ECRS DAM & AS Trade | LR 1 Self Prov Tel. |  | LR 2 Self Prov. Tel. |  | LR 1 Validated - 1 |  | LR 2 Validated - 1 | 
 |  |  | TelSelfRRS | TelSelfECRS | TelSelfRRS | TelSelfECRS | V1-RRS | V1-ECRS | V1-RRS | V1-ECRS
Ex. 1 | 40 | 20 | 20 | 10 | 20 | 10 | 20 | 10 | 20 | 10
EX. 2 | 40 | 20 | 25 | 15 | 20 | 10 | 20 | 10 | 20 | 10
 | LR 1 Validated - 1 |  | LR1 | LR 1 Validated - 2 |  | LR 2 Validated - 1 |  | LR 2 | LR 2 Validated 2 | 
 | V1-RRS | V1-ECRS | NPF-LPC | V2-RRS | V2-ECRS | V1-RRS | V1-ECRS | NPF-LPC | V2-RRS | V2-ECRS
Ex. 1 | 20 | 10 | 41 | 20 | 10 | 20 | 10 | 15 | 15 | 0
EX. 2 | 20 | 10 | 21 | 20 | 1 | 20 | 10 | 60 | 20 | 10

## Slide 5: UFR Load Resource Treatment Under RTC
RTC awards to UFR Load Resource
  RRS-BLK award =+ additional RRS-BLK award
    Additional RRS-BLK award possible if headroom (discounting self-provided total AS) available, RRS offer exists, and economics
  ECRS-BLK award =+ additional ECRS-BLK award
    Additional ECRS-BLK award possible if headroom (discounting self-provided total AS) available, ECRS offer exists, and economics
 | LR1 | LR 1 Validated - 2 |  | LR 1 Extra AS (RRS+ECRS) eligibility | LR 2 | LR 2 Validated 2 |  | LR 2 Extra AS (RRS+ECRS) eligibility
 | NPF-LPC | V2-RRS | V2-ECRS |  | NPF-LPC | V2-RRS | V2-ECRS | 
Ex. 1 | 41 | 20 | 10 | 11 | 15 | 15 | 0 | 0
EX. 2 | 21 | 20 | 1 | 0 | 60 | 20 | 10 | 30

## Slide 6: System Wide Responsive Reserve Service (RRS) Constraints
When Self-Provision amounts for RRS_BLK within limits
Three constraints for implementing the Rules for awarding RRS
The maximum allowable RRS from the sum of RRS-BLK and RRS-FFR is capped at MIN(60% of Total_RRS_Req, (Total_RRS_Req – 1150))
The maximum allowable RRS of RRS-FFR type is MAX-RRS-FFR

## Slide 7: System Wide Responsive Reserve Service (RRS) Constraints
When Self-Provision amounts for RRS_BLK exceeds limits
One constraint for implementing the Rules for awarding RRS
No additional RRS_BLK awards (apart from self provision amounts)
No RRS_FFR awards

## Slide 8: System Wide Responsive Reserve Service (RRS) Constraints
MW
$/MW/h
RRS ASDC
Total_RRS_Req.
3000
Self Prov. RRS_BLK
When Self-Provision amounts for RRS_BLK exceeds limits
1800
RRS
MCPC
60% Total_RRS_Req.
= 1800

## Slide 9
Discussion