## Slide 1
NOGRR 195
Freddy Garcia
January 15, 2020

## Slide 2: Voltage Set Point tolerances
Currently Voltage Set Point tolerances, +/- 2%, can be more than a 14 kV spread for Generation Resources connected to 345kV POI’s.
  Difficult to maintain reliability when Resource allowed to drift far from set point.
  Using whole numbers easier for operators to determine when out of range rather than having to calculate a band that changes dynamically because of being in %.
  PDCWG recommended 1%
  NPRR 776 implemented common point of measurement eliminating metering differences between the TO and GR.
Nominal Voltage | Tolerance Band KV
345 | +/- 4kV
230 | +/- 3kV
138 | +/- 2kV
115 | +/- 2kV
69 | +/- 1kV

## Slide 3: Generator Voltage Set Point tolerances
NERC Reliability Guideline Reactive Power Planning December 2016, p 23

## Slide 4: Reliability Risks
Single or multiple Plants don’t hold voltage set point
Other Plants & dynamic devices exhausting reactive to compensate
Less dynamic reactive to respond to contingency

## Slide 5: Reliability Risk

## Slide 6: Reliability Risks: Example 1
Color key:
KVM = solid blue
KVT = dotted dark blue
MVAR = solid red
MVAR Min. = dotted dark red

## Slide 7: Reliability Risks: Example 2
High Voltages
  Reported High Voltages
  Arcing conductors, transformer issues
  Within 2% tolerance, outside 4kV

## Slide 8: Reliability Risks: In Conclusion
Poor voltage control can lead to sustained low/high voltages and:
  Decreased Dynamic Reactive Reserves
  Tripping of generating units due to low auxiliary voltage
  Increased reactive load from motor stalling and automatic substation LTC actions
  Reduced reactive support from capacitors, SVCs and line charging

## Slide 9
Questions

## Slide 10
Change in Voltage Target (KVT) with limited to no Unit MVAR Response

## Slide 11: Example 1

## Slide 12: Example 2

## Slide 13
Change in Point of Interconnect Voltage(KVM) with no Unit MVAR Response

## Slide 14: Example 1

## Slide 15: Example 2

## Slide 16: Example 3

## Slide 17
Unit operating at or near 2% tolerance band

## Slide 18: Example 1

## Slide 19: Example 2

## Slide 20: Example 3 - from presentation with Capacitor status