## Slide 1
Annual TAC Review of the Market Impacts of Reliability Unit Commitments
Analysis of 2019
David Maggio
Technical Advisory Committee
ERCOT Public
January 29, 2019

## Slide 2: Protocol Language
5.8 Annual RUC Reporting Requirement
(1) ERCOT shall report to the Technical Advisory Committee (TAC), each January, an assessment of market impacts and Settlements for the aggregate Reliability Unit Commitment (RUC) activity, delineated by type of RUC instruction as follows:
RUC instructions issued for Ancillary Service shortages (failure to sufficiently procure one or more Ancillary Service markets in the Day-Ahead Market (DAM) or subsequent Supplemental Ancillary Service Markets (SASMs));
RUC instructions issued for irresolvable transmission system constraints;
RUC instructions issued in anticipation of extreme cold weather/startup failures;
RUC instructions issued for capacity;
RUC instructions issued for system inertia; and
A summary of RUC Settlements;
(i) RUC charges associated with RUC Make-Whole Amount Total per RUC, as defined in Section 5.7.4.1, RUC Capacity-Short Charge; and
(ii) RUC Shortfall Total, as defined in Section 5.7.4.1.1, Capacity Shortfall Ratio Share.

## Slide 3: RUC-Committed Resource-Hours in 2019
(*) - The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, partial hour instructions, or otherwise not dispatchable by SCED.
 | Total | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  | 
Total Count | 228 | 59 | 169
Effective Resource-Hours (*) |  |  | 
Total Count | 201.7 | 57.4 | 144.3
Average LSL | 70.1 | 105.1 | 56.1
Average LDL | 99.4 | 199.6 | 59.5
Average BP | 116.3 | 239.4 | 67.3
Average HSL | 167.2 | 310.3 | 110.2

## Slide 4: RUC Commitment Reasons
201.7 effective RUC resource-hours in 2019
  180.6 resource-hours (90%) for local thermal congestion or voltage concerns
  21.1 resource-hours (10%) for system capacity
There were no resource-hours of commitment for Ancillary Service shortages, system inertia or extreme cold weather/startup failures
57.4 effective resource-hours (28%) were successfully bought back
  3.4 (1.7%) of these resource-hours were DAM committed
  This value is higher than last year (22% bought back in 2018)

## Slide 5: RUC-Committed Effective Resource-Hours

## Slide 6: 2019 Highlights
106.6 effective RUC resource-hours (53% of annual total) were issued to Permian Basin Resources to help resolve local issues in West Texas associated with high load in the area as well as transmission outages.
  53.3 of these hours were issued in May alone (50% of Permian Basin total).
4.8 effective RUC resource-hours were issued to switchable Resources on September 6th. These were the first switchable RUC issued since the Resource status code of ‘EMRSWGR’ went live on May 31st.

## Slide 7: RUC-Committed Resources Dispatched above LDL
When Resources did not successfully opt out, there were 46 resource-hours when the Resource was dispatched above its LDL.
  For 43 of these resource-hours, the RUC-instructed Resource was mitigated.
  For 3 of these resource-hours, the RUC-instructed Resource was not mitigated and had been DAM committed, and the hours were treated as Opted Out.
  For none of these resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor.
  For all of these resource-hours, the LMP for the RUC-instructed Resource was below the RUC offer floor.
NPRR744 (implemented 6/1/2017) remedied a historical issue in which submitted Energy Offer Curves could be below the offer floor.

## Slide 8: Reliability Deployment Price Adders
Month of 2019 | Total RTORDPA Time (Hours) | Time-weighted Average RTORDPA ($/MWh)
Jan | 0.58 | 0.01
Feb | 0.00 | 0.00
Mar | 8.00 | 0.12
Apr | 16.00 | 0.26
May | 49.42 | 1.04
Jun | 15.00 | 1.35
Jul | 0.00 | 0.00
Aug | 22.58 | 771.24
Sep | 7.58 | 179.78
Oct | 23.42 | 0.46
Nov | 4.00 | 0.65
Dec | 0.50 | 0.01

## Slide 9: RUC Make-Whole and Claw Back 2016 - 2019
** 2019- $48K in Make-Whole paid out. Only $0.47 was uplifted to Load.

## Slide 10: RUC-Related Improvements in 2019
NPRR901, Switchable Generation Resource Status Code, created the Resource status code of ‘EMRSWGR’. It was implemented on 5/31/2019.
NPRR910, Clarify Treatment of RUC Resource that has a Day-Ahead Market Three-Part Supply Award, went live on 5/31/2019. The new logic prevents the triggering of the Real-Time Reliability Deployment Price Adder and the application of a RUC offer floor when a RUC Resource has previously been awarded a Three-Part Supply offer.
NPRR912, Settlement of Switchable Generation Resources (SWGRs) Instructed to Switch to ERCOT, addresses the Settlement of Switchable Generation Resources (SWGRs) that receive a Reliability Unit Commitment (RUC) instruction to switch from a non-ERCOT Control Area to the ERCOT Control Area. It was implemented on 5/31/2019.

## Slide 11: Conclusions
In 2019, 228 instructed RUC resource-hours resulted in 201.7 effective RUC resource-hours.
  As compared to 642 and 613 for all of 2018, respectively
  28% of effective resource-hours were bought back
  Over 53% of the annual total resource-hours were for Permian Basin Resources, to help resolve local issues in West Texas associated with high load in the area as well as transmission outages.
The total RUC make-whole amount was ~$48K.
  Almost exclusively covered through capacity-short charges
ERCOT continues to work with stakeholders on issues and questions related to RUC.

## Slide 12: Appendix

## Slide 13: RUC-Committed Effective Resource-Hours by Opt Out Status*
Month | 2016 | 2017 | 2018 | 2019
Jan | 33 | 7 | 46 | 0
Feb | 28 | 20 | 0 | 0
Mar | 47 | 14 | 0 | 8
Apr | 62 | 47 | 3 | 16
May | 74 | 33 | 333 | 59
Jun | 111 | 52 | 0 | 15
Jul | 222 | 39 | 0 | 0
Aug | 83 | 76 | 15 | 0
Sep | 111 | 54 | 4 | 8
Oct | 155 | 16 | 11 | 34
Nov | 20 | 8 | 50 | 4
Dec | 0 | 5 | 14 | 1
Month | 2016 | 2017 | 2018 | 2019
Jan | 11 | 2 | 0 | 0
Feb | 12 | 0 | 0 | 11
Mar | 0 | 0 | 0 | 0
Apr | 11 | 0 | 0 | 6
May | 57 | 20 | 40 | 13
Jun | 165 | 76 | 21 | 0
Jul | 96 | 27 | 4 | 0
Aug | 49 | 23 | 28 | 8
Sep | 59 | 12 | 16 | 19
Oct | 13 | 0 | 15 | 0
Nov | 0 | 3 | 12 | 0
Dec | 0 | 0 | 2 | 0
Did Not Opt Out
Opted Out
* Effective Hours rounded to nearest whole number

## Slide 14: RUC Make-Whole and Claw Back 2016-2017*
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2016 | 2017 | 2016 | 2017 | 2016 | 2017 | 2016 | 2017 | 2016 | 2017
Jan | -29 | 0.0 | 29 | 0 | 0 | 0 | 0 | 228 | 499 | 0
Feb | - 4 | -7 | 4 | 7 | 0 | 0 | 38 | 0 | 194 | 206
Mar | - 13 | -79 | 13 | 79 | 0 | 0 | 608 | 0 | 212 | 471
Apr | -70 | -175 | 70 | 175 | 0 | 0 | 3 | 0 | 1677 | 1387
May | -45 | -21 | 45 | 21 | 0 | 0 | 88 | 641 | 1563 | 209
Jun | -176 | -40 | 176 | 40 | 0 | 0 | 115 | 163 | 2225 | 491
Jul | -372 | -57 | 372 | 57 | 0 | 0 | 156 | 6 | 3337 | 620
Aug | -138 | -121 | 138 | 121 | 0 | 0 | 2 | 15 | 2413 | 870
Sep | -240 | -25 | 240 | 25 | 0 | 0 | 46 | 79 | 2440 | 755
Oct | -153 | -4 | 153 | 4 | 0 | 0 | 81 | 47 | 3584 | 159
Nov | 0 | -10 | 0 | 10 | 0 | 0 | 275 | 25 | 147 | 149
Dec | 0 | -2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 77
* Amounts rounded to nearest thousand. Data from most recent settlement run as of 12/31/2019.

## Slide 15: RUC Make-Whole and Claw Back 2018-2019*
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2018 | 2019 | 2018 | 2019 | 2018 | 2019 | 2018 | 2019 | 2018 | 2019
Jan | -42 | 0 | 42 | 0 | 0 | 0 | 385 | 0 | 1202 | 0
Feb | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Mar | 0 | -9 | 0 | 9 | 0 | 0 | 0 | 0 | 0 | 253
Apr | 0 | -8 | 0 | 8 | 0 | 0 | 4 | 0 | 0 | 359
May | -102 | -13 | 102 | 13 | 0 | 0 | 2372 | 108 | 2824 | 915
Jun | 0 | -4 | 0 | 4 | 0 | 0 | 0 | 3 | 0 | 738
Jul | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Aug | -35 | 0 | 35 | 0 | 0 | 0 | 1 | 0 | 523 | 0
Sep | -24 | -11 | 24 | 11 | 0 | 0 | 0 | 1 | 206 | 110
Oct | -24 | -3 | 24 | 3 | 0 | 0 | 213 | 726 | 535 | 229
Nov | -381 | 0 | 381 | 0 | 0 | 0 | 79 | 49 | 977 | 0
Dec | 0 | 0 | 0 | 0 | 0 | 0 | 20 | 15 | 0 | 0
* Amounts rounded to nearest thousand. Data from most recent settlement run as of 12/31/2019.