## Slide 1
Maximum Permissible ERCOT System FA values
Marcelo Magarinos
RCWG
Jan 30, 2020

## Slide 2: Purpose
Per RCWG request at Dec/2019 meeting, ERCOT verified the potential system limitations for handling Fuel Adder (FA) values.
The identified constraint is the calculation of the Mitigated Offer Cap (MOC) that is saved in a table field that can hold values up to 999,999.99
Other parameters calculated using FAs are the Start-up and Minimum Energy costs. However, these calculations utilize floating point variables and do not represent system constraints for handling FAs

## Slide 3: Mitigated Offer Cap (MOC) calculation
The Mitigated Offer Cap is limited to $999,999.99/MWh in the system
MOC ($/MWh) = [IHR * (FIP + FA) + Variable O&M] * W
Where,
IHR = Incremental Heat Rate
FIP = Fuel Index Price
FA = Fuel Adder
Variable O&M = approved O&M cost
W = capacity factor multiplier

## Slide 4: Mitigated Offer Cap (MOC) calculation (continue)
Example:
IHR = 10 MMBtu/MWh
FIP = $3/MMBtu
FAmax = ?
Variable O&M = $5/MWh
W = 1.5
Then,
(FIP + FAmax) = {[(999,999.99 / 1.5) - 5] / 10 } = $66,666/MMBtu
FAmax = 66,666 – 3 = $66,663/MMbtu

## Slide 5: Questions?
Notes: https://castaylor.ercot.com/owa/redir.aspx?C=oPhl4_Wz9UCI7oVqJkGdaM-P4-MvhtMIRAMJFZ7-K5eOg6lo6esBMUiebAbXd4c8z8FTPzV8g8A.&URL=https%3a%2f%2ftheconversation.com%2fwhen-will-rooftop-solar-be-cheaper-than-the-grid-heres-a-map-54789%3futm_source%3dtwitter%26utm_medium%3dreferral%26utm_campaign%3dUTAustinNews
http://www.vox.com/2015/6/19/8808545/wind-solar-grid-integration
http://greeningthegrid.org/quick-reads
https://ec.europa.eu/energy/intelligent/projects/en/projects/pv-grid
http://energy.gov/eere/sunshot/systems-integration