## Slide 1
NPRR863 Phase 1
Webex Training
Nathan Smith
January 28, 2020

## Slide 2: New Terminology – Phase 1
Fast Frequency Response (FFR) – subset of RRS
  Responds within 15 cycles after frequency meets or drops below a preset threshold (59.85 HZ)
  Sustained for at least 15 minutes
  Recovers in 15 minutes
  Battery Energy Storage (combo model of Generation Resource (GEN) and Controllable Load Resource (CLR)) will be the only resource able to qualify for FFR in the initial implementation of NPRR863 (Phase 1)
This initial implementation seeks to use currently existing market submission types/fields, so as not to alter the external interfaces specification or the Market Manager
  Phase 2 implementation will contain FFR market submission item changes.

## Slide 3: Topics – What’s New?
FFR Qualified Resources
  Battery GEN and Battery CLR
  Must be SCED and RRSFFR qualified to offer
  How does a FFR qualified resource offer FFR into DAM?
  FFR-RRS Qualified MW quantity limit for individual resources
Qualified RRS % of High Sustained Limit (HSL) for individual resources
Self Arranged FFR in Phase 1 will be submitted as Self-Arranged RRSNC  market system nomenclature for RRS from Non-Controllable Loads
FFR counts toward the 50-60% Non-Controllable load cap of RRS

## Slide 4: What’s Staying the Same?
Limit of RRSNC – Still 50-60% depending on RRS Plan
1150 MW minimum for RRSGN market system nomenclature for RRS from Generation Resources
Non-battery GENs still offer in RRSGN
Non-battery CLRs still offer in RRSLD/RRSNC
AS Offers from Non-Controllable Loads

## Slide 5: AS Offers into DAM/SASM during Phase 1
Resource Type | AS Qualifications | Submits AS Offer with NCLR Flag = | Result | Awarded as | Note
Battery CLR | FFR Only | TRUE | Accepted | FFR(RRSNC) | New
 |  | FALSE | Rejected |  | No RRS Qualification
 | RRS Only | TRUE | Accepted | UFR(RRSNC) | 
 |  | FALSE | Accepted | PFR(RRSLD) | 
 | RRS and FFR | TRUE | Accepted | UFR(RRSNC) | 
 |  | FALSE | Accepted | PFR(RRSLD) | 
Battery GEN | FFR Only | TRUE | Rejected |  | Not a CLR
 |  | FALSE | Rejected |  | Battery Gen submits FFR through the Battery CLR
 | RRS Only | TRUE | Rejected |  | Not a CLR
 |  | FALSE | Accepted | PFR(RRSGN) | 
 | RRS and FFR | TRUE | Rejected |  | Not a CLR
 |  | FALSE | Accepted | PFR(RRSGN) | 
Non-Battery CLR | No Change. Non-battery CLR will not be FFR qualified in NPRR863 Phase 1. |  |  |  | 
Non-Battery GEN | No Change. Non-battery generation will not be FFR qualified in NPRR863 Phase 1. |  |  |  | 
Note: To supply FFR, only qualify for RRSFFR and SCED. Being RRS qualified will not allow a path for submitting FFR.

## Slide 6: Where does FFR fit into the RRS Plan?
RRS Plan is awarded in two groups – RRS Non-controllable (RRSNC) and Primary Frequency Response (PFR). Offers treated as FFR are awarded to the RRSNC group and count toward the limit.
RRSNC
50-60% limit
RRS Plan
RRSNC
FFR
UFR
(min. 1150 MW)
PFR
RRSGN
RRSLD

## Slide 7: Providing FFR in Real-Time
In Real-Time, the Battery providing FFR shall put the FFR responsibility on GEN part of Battery and telemeter ONFFRRRS resource status, the CLR part of Battery shall not provide FFR and shall telemeter OUTL resource status.
CLR of Battery providing FFR shall submit ONRL status for COP. Gen shall submit ON status for COP.
ONFFRRRS Resource will be dispatchable in SCED and its available capacity will be included in ORDC online reserve

## Slide 8: COP with RRS Responsibility>0 during Phase 1
Resource Type | AS Qualifications | COP Status | Result | Treated as | Note
Battery CLR | FFR Only | ONRL | Accepted | FFR(RRSNC) | New: Battery submits FFR through the Battery CLR.
 | RRS Only | ONRL | Accepted | UFR(RRSNC) | 
 |  | (ONCLR or ONRGL) and SCED qualified | Accepted | PFR(RRSLD) | 
 | RRS and FFR | ONRL | Accepted | UFR(RRSNC) | 
 |  | (ONCLR or ONRGL) and SCED qualified | Accepted | PFR(RRSLD) | 
Battery GEN | FFR Only | ON | Rejected |  | New: Battery submits FFR through the Battery CLR.
 | RRS Only | ON | Accepted | PFR(RRSGN) | 
 | RRS and FFR | ON | Accepted | PFR(RRSGN) | 
Non-Battery CLR | No Change. Non-battery CLR will not be FFR qualified in NPRR863 Phase 1. |  |  |  | 
Non-Battery GEN | No Change. Non-battery generation will not be FFR qualified in NPRR863 Phase 1 . |  |  |  | 

## Slide 9: AS Trades in NPRR863 Phase 1
In this initial implementation, RRSNC type will be used to indicate that traded MWs come from either NCLR (UFR) or FFR resources.
  Just like today with NCLRs, FFR MWs cannot be used to cover a shortage of RRSGN (PFR).

## Slide 10: Wrap-Up and Q&A
NPRR863 Phase 1 becomes effective March 1, 2020
Contact your Account Manager with any transition issues

## Slide 11: Acronyms
AS – Ancillary Services
UFR – RRS provided by Under Frequency Relay controlled Load Resources
PFR – RRS provided by Primary Frequency Response GEN/CLR
NCLR – Non-Controllable Load Resource
RRSNC – UFR type RRS provided by Non-Controllable Load Resources
RRSLD – PFR RRS provided by Controllable Load Resources
RRSGN – RRS provided by Generation Resources
BES – Battery Energy Storage (combo model of Generation Resource (GEN) and Controllable Load Resource (CLR))
SCED qualification – AS qualification allowing resources/loads to participate in AS market
RRSFFR qualification – AS qualification that allows CLRs that are not RRS qualified to submit RRS with NCLR_FLAG = True and be considered as an FFR offer.
ONFFRRRS – telemetered status for GEN providing FFR in Real-Time
OUTL – COP status for a Load Resource that is not available for interruption or control

## Slide 12: Acronyms – cont.
ONRL – COP status indicates Load Resource is available for dispatch of Responsive Reserve Service, excluding Load Resources acting as Controllable Load Resources
ONCLR – COP status indicates resource is available for dispatch of Responsive Reserve Service or Non-Spinning Reserve Service as a Controllable Load Resource
ONRGL – COP status for resource if Regulation Service is being provided along with RRS.
ORDC – Operating Reserve Demand Curve