## Slide 1
Discussion - REC Awards for DC-Coupled Resources (KTC-11)
Don Tucker
BESTFORCE Meeting
February 25, 2020

## Slide 2: Eligibility for REC Awards
As the Administrator of the Texas REC Trading Program, ERCOT will award RECs to a renewable generator based on an Entity’s approved filing by the commission.
Such filing includes details from the filing entity on all generation at a facility and a representation of how the output of the renewable resource is metered.
Only generators certified by the commission as a renewable generator are eligible to earn RECs

## Slide 3: Site Configuration
A DC-Coupled Resource, as being discussed by the BESTF, has a storage component.
One or more Energy Storage Systems (ESS) combined with one or more wind and/or solar generators behind a single point of interconnection (POI), where these combined technologies are interconnected within the site using direct current (DC) equipment. The combined technologies are then connected to the ERCOT grid using the same direct current-to-alternating current (DC-to-AC) inverter(s).
Discussions have indicated that the storage component, may or may not be totally charged by the renewable energy technology, creating at least two scenarios for discussion.

## Slide 4: Scenario 1
The inverter(s) design does not support charging the Energy Storage System from the Grid.
DC Coupled Resource where the storage component is completely charged from the renewable resource on the DC side of the inverter.
While the time period for exporting the energy to the grid and the subsequent measurement of the energy could be shifted, all exports of energy from the co-located technologies would be energy produced from the renewable resource.
Subsequently, the metered energy at the grid would represent production from the renewable resource.

## Slide 5: Scenario 2
The inverter(s) design supports charging the Energy Storage System from the Grid.
The storage component is at least partially charged or has the opportunity to charge from a source other than the renewable resource.
Subsequently, the metered energy at the grid would or could be combined with production from the renewable resource and from a source other than the renewable resource.
Requires additional meter data to accurately represent production from the renewable resource.

## Slide 6: Generation Resource Self Report Metering Requirement
ERCOT Protocols Section 14.5 addresses reporting requirements for renewable generators eligible to earn RECs
For a renewable Generation Resource or Settlement Only Generator:
Data can be provided by ERCOT based on an extract from the ERCOT Settlement system, or
Data can be self-reported based on metering facilities that are
  Installed, operated and maintained by the REC generator
  Installed in a location to only record energy from generation certified by the PUCT to receive RECs
  Compliant with American National Standards Institute (ANSI) C12, Code for Electricity Metering, metering accuracy standards; and
  Verified for accuracy every six years.

## Slide 7: Take Away from this Discussion
Commission filings by an Entity must include details on all generation at a facility and a representation of how the output of the renewable resource is metered.
Metering must be installed in a location to only record energy from generation certified by the PUCT to receive RECs.
Only generators certified by the commission as a renewable generator are eligible to earn RECs.

## Slide 8
Discussion