## Slide 1
Proxy Energy Offers and Energy Bids for ESRs (KTC-15)
Dave Maggio
BESTF Meeting
Feb. 25, 2020

## Slide 2: Acronym
CLR – Controllable Load Resource
ESR – Energy Storage Resource
HSL – High Sustained Limit
KTC – Key Topic and Concept related to BESTF
LPC – Low Power Consumption
LSL – Low Sustained Limit
MPC – Max Power Consumption
RTSWCAP – Real-Time System-Wide Offer Cap
SWCAP – System-Wide Offer Cap

## Slide 3: Outlines
Thought process driving today’s material
Current
  Proxy Energy Bid process for ESR CLRs
  Proxy Energy Offer process for ESR Generators
Proposal for the Combo Model era:
  Proxy Energy Bid process for ESR CLRs
  Proxy Energy Offer process for ESR Generators
Proposal for the Single Model era
  Proxy Energy Offer/Bid process for ESRs

## Slide 4: ERCOT evolution for Energy Storage Resources
Registration
(RARF or RIOO)
Siebel, NMMS, EMS, MMS, Settlements
Phase
A
GR
GR
CLR
CLR
Today
C
Single
Resource
Single
Resource
EMS Upgrade + RTC Go-Live 2024
Mark the GR and CLR so that it can be seen they are a pair
ESR
ESR
ESR
ESR
B
By Dec 31, 2020
Single
Resource
GR
ESR
CLR
ESR
‘Combo Model Era’
‘Single Model Era’

## Slide 5: Thought process driving today’s material
The existing processes for CLRs and Generators were not developed with ESRs in mind and do not account for the duration-limited nature of ESRs.
  For example, the current CLR proxy process can result in ESR CLRs being dispatched to consume at their maximum consumption amount as a price-taker with an Energy Bid at $9,000/MWh.
Our proposal is to take a different approach with ESRs in both the Combo Model and Single Model eras, where the proxy process tends to dispatch the Resource to a more neutral level (e.g., 0 MW).
Note that this is only the proxy process. Energy Bid/Offers for ESRs will be able to updated within the Operating Hour and ESRs are always expected to have a full-range Energy Bid/Offer.

## Slide 6: Current proxy process for ESR CLRs and ESR Generators
Today, ESR CLRs and other CLRs are treated the same when creating SCED proxy Energy Bids:
  If no Energy Bid is submitted, SCED will create a Proxy Energy Bid from LPC to MPC at SWCAP (Protocols 6.4.3.1(4)).
  If a partial bid submitted (i.e. the submitted bid doesn’t cover the full range of the CLR’s available Demand Response capability), SCED will create a proxy Energy Bid as below (Protocols 6.5.7.3(6)):
Similarly, ESR Generators and other Generators are treated the same when creating proxy Energy Offers.
MW | Price (per MWh)
LPC to MPC minus maximum MW of RTM Energy Bid | Price associated with the lowest MW in submitted RTM Energy Bid curve
MPC minus maximum MW of RTM Energy Bid to MPC | RTM Energy Bid curve
MPC | Right-most point (lowest price) on RTM Energy Bid curve

## Slide 7: Current: ESR CLR without a Energy Bid

## Slide 8: Current: ESR CLR with a partial Energy Bid

## Slide 9: Current: ESR Generator has a partial Energy Offer

## Slide 10: Proposed proxy Energy Bid for ESR CLRs in the Combo Model era
Proposal to use the following logic to create proxy Energy Bid for ESR CLRs
  If no bid submitted, SCED will create a proxy Energy Bid from LPC to MPC at -$250/MWh
  If a partial bid is submitted, SCED will create a proxy Energy Bid as below:
This will not affect the proxy Energy Bids for other CLRs.
MW | Price (per MWh)
LPC (if less than lowest MW of RTM Energy Bid) to lowest MW in RTM Energy Bid curve | Price associated with the lowest MW in submitted RTM Energy Bid curve
RTM Energy Bid curve | RTM Energy Bid curve
Maximum MW of RTM Energy Bid curve to MPC (if more than Maximum MW of RTM Energy Bid) | -$250.00

## Slide 11: Combo Model era proposal: ESR CLR without a Energy Bid

## Slide 12: Combo Model era proposal: ESR CLR with a partial Energy Bid

## Slide 13: Proposed proxy Energy Offer for ESR Generators in the Combo Model era
Propose to use the following logic to create proxy Energy Offers for ESR Generators
  If no offer submitted, SCED will create a proxy Energy Offer from LSL to HSL at SWCAP
  If a partial offer is submitted, SCED will create a proxy Energy Offer as below:
This will not affect the proxy Energy Offers for other Generators
MW | Price (per MWh)
LSL (if less than lowest MW of RTM Energy Offer) to lowest MW in RTM Energy Offer curve | Price associated with the lowest MW in submitted RTM Energy Offer curve
RTM Energy Offer curve | RTM Energy Offer curve
Maximum MW of RTM Energy Offer curve to HSL(if more than Maximum MW of RTM Energy Offer) | SWCAP

## Slide 14: Combo Model era proposal: ESR Generator without an Energy Offer

## Slide 15: Combo Model era proposal: ESR Generator with a partial Energy Offer

## Slide 16: Proposed proxy Energy Bid/Offer for ESRs in the Single Model era
QSEs will submit a single Energy Bid/Offer for ESRs including both discharging and charging.
Propose to use the following logic to create a proxy Energy Bid/Offer for ESRs
  If no Bid/Offer submitted, SCED will create a proxy Energy Bid/Offer at -$250/MWh from LSL to 0 MW and at RTSWCAP from 0 MW to HSL.
  If partial Energy Bid/Offer submitted, SCED will create a proxy Energy Bid/Offer based on the table on the next slide.
This would not change the treatment for the case in which the ESR has an Output Schedule.

## Slide 17: Proposed proxy Energy Offer/Bid for ESRs in the Single Model era
Scenario | MW Segment | Price (per MWh)
HSL MW and the highest MW point on the Energy Bid/Offer are both greater than or equal to zero, and, HSL is greater than the highest MW in submitted Energy Bid/Offer Curve | From highest MW point on submitted Energy Bid/Offer Curve to HSL MW | RTSWCAP in effect
HSL MW is greater than or equal to zero, and, the highest MW point on the Energy Bid/Offer is less than zero | From highest MW point on submitted Energy Bid/Offer Curve to 0 MW | Price associated with the highest MW in submitted Energy Offer Curve
 | From 0 MW to HSL | RTSWCAP in effect
HSL is less than zero and is also greater than the highest MW in submitted Energy Bid/Offer Curve | From highest MW point on submitted Energy Bid/Offer Curve to HSL MW | Price associated with the highest MW in submitted Energy Offer Curve
Energy Bid/Offer Curve |  | Energy Bid/Offer Curve
LSL MW and the lowest MW point on the Energy Bid/Offer Curve are both greater than or equal to zero, and, LSL is less than the lowest MW in submitted Energy Bid/Offer Curve | From LSL to lowest MW point on submitted Energy Bid/Offer Curve | Price associated with the lowest MW in submitted Energy Offer Curve
LSL MW is less than zero, and, the lowest MW point on the Energy Bid/Offer Curve is greater than zero | From LSL to 0 MW | -$250
 | From 0 MW to lowest MW point on submitted Enery Bid/Offer Curve | Price associated with the lowest MW in submitted Energy Offer Curve
LSL and the lowest MW point on the Energy Bid/Offer Curve are both less than or equal to zero, and, LSL is lower than the lowest MW point on the Energy Bid/Offer Curve | From LSL to lowest MW point on submitted Energy Bid/Offer Curve | -$250.00

## Slide 18: Single Model era proposal: ESR without an Energy Bid/Offer

## Slide 19: Single Model era proposal: ESR with a partial Energy Bid/Offer

## Slide 20: Single Model era proposal: ESR with a partial Energy Bid/Offer

## Slide 21: Single Model era proposal: ESR with a partial Energy Bid/Offer

## Slide 22: Single Model era proposal: ESR with a partial Energy Bid/Offer

## Slide 23: Single Model era proposal: ESR with a partial Energy Bid/Offer

## Slide 24: Single Model era proposal: ESR with a partial Energy Bid/Offer

## Slide 25: Single Model era proposal: ESR with a partial Energy Bid/Offer

## Slide 26: Single Model era proposal: ESR with a partial Energy Bid/Offer

## Slide 27: Single Model: ESR with an Output Schedule

## Slide 28
Discussion