## Slide 1
Implementation details for phase 1 of NPRR 863 and NPRR 960
ERCOT
Nitika Mago
Supervisor, Operations Analysis
ERCOT

## Slide 2: Implementation Scope for Phase 1
Phase 1 of NPRR863/NPRR960* (Phase 1) primarily focuses on implementing Fast Frequency Response (FFR) as a subset of Responsive Reserve Service (RRS)**. Phase 1 is expected to be effective on March 1, 2020. In Phase 1,
  Battery energy storage will be the only resource able to qualify to provide FFR.
    FFR from non-Controllable Load Resource will be supported in the next phase
  the “10-minute ramp” component of RRS will continue to exist.
    Generation Resource providing RRS will continue to be expected to release capacity (“HASL release”) to SCED once an RRS deployment is received.
  RRS limit for all Generation Resources will be based on methodology outlined in OBDR Methodology to Calculate Responsive Reserve (RRS) Service Limits.
  A limit of 450 MW will be applied on Resources providing FFR.
*Documents associated with NPRR863 and NPRR960 can be found on the ERCOT website.
** Appendix contains a full list of protocols that will be un-gray boxed.
  Fast Frequency Response (FFR)
  The automatic self-deployment and provision by a Resource of their obligated response within 15 cycles after frequency meets or drops below a preset threshold (59.85 Hz) or a deployment is response to an ERCOT Verbal Dispatch Instruction (VDI) within 10 minutes. Resources capable of automatically self-deploying and providing their full Ancillary Service Resource Responsibility within 15 cycles after frequency meets or drops below a preset threshold and sustaining a full response for at least 15 minutes may provide Responsive Response Service (RRS).
  A Resource providing RRS as FFR that is deployed shall not recall its capacity until system frequency is greater than 59.98 Hz.
  Once recalled, a Resource providing RRS as FFR must restore their full RRS Ancillary Service Resource Responsibility within 15 minutes after cessation of deployment or as otherwise directed by ERCOT.

## Slide 3: FFR Deployment – QSE Level
Resources providing FFR must respond to a frequency event autonomously when the frequency trigger criteria is met. These resources must be capable of sustaining full response for at least 15 minutes or till ERCOT recalls the deployment, whichever occurs first.
A new ICCP tag* will be created to send QSE specific RRS MWs requests/deployments to FFR Resources. QSE Specific FFR RRS MWs request/deployment will be
  non-zero when frequency reaches 59.85 Hz and
  zero when frequency reaches 59.98 Hz.
Chart: FFR Deployment (MW)
*Contact ERCOT’s EMMS Production Support personnel for details on this tag.

## Slide 4: FFR Deployment – Resource Level
A battery energy storage Resource providing FFR in Real Time must use Resource Status (RST) = 21 (i.e. ONFFRRRS) on the Generation Resource portion of combo-model.
ERCOT systems are setup to provide a Resource providing FFR SCED Base Points (BPs) and Updated Desired base Point (UDBP) subject to the Resource's dispatch limits, which are calculated using the Resource's telemetered inputs (High Sustained Limit (HSL), Low Sustained Limit (LSL), Responsive Reserve Responsibility (RRRS), Responsive Reserve Schedule (RRSC), etc.) and the submitted offer curves.
Resource providing FFR is expected to respond autonomously to frequency. Upon getting triggered, such Resource is expected to set its RRSC = 0; this allows SCED appropriately set the Resource’s BP (and thus UDBP).
When FFR is recalled, it is recommended that the Resource providing FFR follow its UDBP to ramp down to 0 MW.
Upon completion of an FFR deployment a Resource providing FFR is expected to reset RRRS/RRSC according to the Resource’s capability as soon as practicable but no later than 15 minutes (or the QSE is expected to move the RRS obligation to a different Resource).

## Slide 5: Telemetry setup Example 1
Chart: Time Sequence
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
FFR-Deployed | 0 | 0 | 0 | 10 | 10 | 10 | 10 | 0 | 0 | 0
Output | 10 | 10 | 10 | 10 | 0 | 0 | 0
UDBP | 0 | 0 | 0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0
Output | 0 | 0 | 0 | 0 | 10 | 10 | 10
RRSC* | 10 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 10 | 10 | 10 | 10 | 10
HDL/HASL | 0 | 0 | 0 | 0 | 10 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0
HSL | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10
Example below provides a high level outline of telemetry on the Generation Resource portion of combo-model when this Resource providing FFR is deployed.
Note that this example is intended to represent of sequence of events and is not indicative of time/duration.
*For a Resource that is providing FFR in Real Time ERCOT systems shall validate & limit Ancillary Service Responsibility and Ancillary Service Schedule for RRS to be less than or equal to its respective FFR Qualified MWs.
FFR Deployed
MW = HSL,
RRSC = 0,
HDL/HASL = HSL
UDBP ramps to BP
FFR Recalled
UDBP & MW ramps to 0.
RRS restored immediately.
HSL stay at pre-event level.

## Slide 6: Telemetry setup Example 2
Chart: Time Sequence
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
FFR-Deployed | 0 | 0 | 0 | 10 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 0
Output | 10 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 0
UDBP | 0 | 0 | 0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 0
Output | 0 | 0 | 0 | 0 | 10 | 10 | 10
RRSC* | 10 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10 | 10 | 10 | 10 | 10
HDL/HASL | 0 | 0 | 0 | 0 | 10 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
HSL | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 10 | 10 | 10 | 10 | 10
Example below provides a high level outline of telemetry on the Generation Resource portion of combo-model when this Resource providing FFR is deployed.
Note that this example is intended to represent of sequence of events and is not indicative of time/duration.
FFR Deployed
MW = HSL,
RRSC = 0,
HDL/HASL = HSL
UDBP ramps to BP
FFR Recalled
UDBP & MW
ramp to 0.
RRS restored.
HSL returns to pre-event level.
HSL to 0, Indicates the need to charge

## Slide 7: FFR Deployment Performance
For an FFR deployment event triggered by an under-frequency event (frequency at or below 59.85 Hz), ERCOT will reach out to Resources providing FFR to obtain high speed data to verify that
  The total time from the time frequency first decays to a value low enough to initiate action up to the time when full Ancillary Service Resource Responsibility for RRS is delivered should be no more than 15 cycles, including all relay and breaker operating times;
  The Resource deployed 95% to 110% of its Ancillary Service Resource Responsibility in 15 cycles after the frequency reached 59.85 Hz;
  The Resource sustained 95% to 110% of its Ancillary Service Resource Responsibility for the duration of the sustained response period, defined as 15 minutes or until the time of recall instruction from ERCOT, whichever occurred first;
  The Resource restored its capability to provide its Ancillary Service Resource Responsibility within 15 minutes from the end of the deployment period subject to grid conditions following the recall instruction.
This is an ad-hoc analysis and will be conducted in close coordination with the Resource.

## Slide 8: FFR Qualification
ERCOT is currently accepting requests from Resources interested to provide FFR.
FFR qualification test will be two pronged test
  a self test that demonstrates the Resource’s ability to deploy within 15 cycles of when the frequency trigger is met and to sustain response for at lease 15 minutes; and
  a coordinated test that demonstrates the Resource’s ability to change Ancillary Service Schedule for RRS telemetry in response to an ERCOT deployment.
ERCOT’s Registration systems will track the capacity a Resource providing FFR is qualified to provide.
ERCOT systems will limit RRS Offers/Awards from a Resource seeking to provide FFR in Day Ahead Market and Ancillary Service Responsibility and Ancillary Service Schedule for RRS from Resource providing FFR in Real Time per its respective FFR Qualified MWs.

## Slide 9: RRS Limits
In Phase 1, the full amount of RRS awarded to or self-arranged from an On-Line Generation Resource will be dependent upon the verified droop characteristics of the Resource.
ERCOT shall use the methodology outlined in Other Binding Document, Procedure for Calculating Responsive Reserve (RRS) Limits for Individual Resources calculate and update, using the methodology described in the Nodal Operating Guide, to compute a maximum percentage (%) of RRS and a maximum MW amount of RRS for each Generation Resource.
  This new certified report, “Responsive Reserve Limits for Generation Resources” (EMIL ID NOG2-312-M , Report ID 19236) will be posted on ERCOT’s Market Information System (MIS) | Grid | Generation page.
  A report will be posted concurrently on the day Phase 1 becomes effective. In this report the RRS limit for all thermal Generation Resources will be set to 20%. The RRS % Limit for non-thermal Generation Resource will be the limit established during RRS qualification process. A default value of 20% shall be used in all other cases.
  The timeline established in Section 6 will be followed for all subsequent RRS Limit report postings.

## Slide 10: Public Dashboard, MIS, Et. all
Two new data fields will be included in the System Ancillary Service Capacity Monitor display on ercot.com and in the QSE Ancillary Services Capacity Monitor report (EMIL ID: NP8-143-CD, Report Type ID: 11025) on ERCOT's Market Information System (MIS).
  RRS Capacity from Resources capable of Fast Frequency Response (FFR)
  Ancillary Service Resource Responsibility for RRS Resources capable of FFR
The Responsive Reserve Performance Report for Generators and CLRs report (EMID ID: NP8-543-M, Report Type ID: 13033) on ERCOT’s MIS will be updated to include response from Resources providing FFR in Real Time.
The following Business Practice Manuals will be updated to capture phase 1 FFR related expectations.
  Current Operating Plan Practices By QSE
  ERCOT and QSE Operations Practices During The Operating Hour

## Slide 11: Acronyms
BP - Base Point
FFR - Fast Frequency Response
HASL - High Ancillary Service Limit
HDL - High Dispatch Limit
HSL - High Sustained Limit
ICCP - Inter-Control Center Protocol
LSL - Low Sustained Limit
QSE - Qualified Scheduling Entity
RRRS - Responsive Reserve Responsibility
RRS - Responsive Reserve
RRSC - Responsive Reserve Schedule
RST - Resource Status
SCED - Security Constrained Economic Dispatch
UDBP - Updated Desired Base Point

## Slide 12
Appendix

## Slide 13: Protocol Sections to be Un-Gray Boxed in Phase 1
The following outlines Nodal Protocol sections that will be un-gray boxed in Phase 1. In cases where only a portion of a Section is being un-gray boxed, specific references have been included in parenthesis.
2.1, Definitions (Fast Frequency Response)
3.8.4, Hydro Generation Resources (3.8.4, Generation Resources Operating in Synchronous Condenser Fast Response)
3.9.1, Current Operating Plan (COP) Criteria (3.9.1 (5)(b)(i)(K); 3.9.1 (5)(b)(i)(Q))
3.16, Standards for Determining Ancillary Service Quantities (3.16 (2)(b)-(e); 3.16 (3); 3.16 (5)*; 3.16 (6)*; 3.16 (7))
3.18, Resource Limits in Providing Ancillary Service (3.18 (3))
4.4.7.1, Self-Arranged Ancillary Service Quantities (4.4.7.1 (9)(c)*)
4.4.7.1.1, Negative Self-Arranged Ancillary Service Quantities (4.4.7.1.1 (3)*)
4.4.7.3, Ancillary Service Trades (4.4.7.3(7))
4.6.4.1.3, Responsive Reserve Service Payment
4.6.4.2.3, Responsive Reserve Service Charge
6.5.7.5, Ancillary Services Capacity Monitor (6.5.7.5 (1)(a)(iv); 6.5.7.5 (1)(b)(iv); 6.5.7.5 (1)(m) - PRC7)
6.5.7.6.2.2, Deployment of Responsive Reserve Service (6.5.7.6.2.2 (2)(a)-(b); 6.5.7.6.2.2(13)-(16))
6.5.9.4.1, General Procedures Prior to EEA Operations (6.5.9.4.1(1)(a), 6.5.9.4.1(1)(d)*)
8.1.1.1, Ancillary Service Qualification and Testing (8.1.1.1 (10)-(11))
8.1.1.3.2, Responsive Reserve Capacity Monitoring Criteria
8.1.1.4.2, Responsive Reserve Energy Deployment Criteria (8.1.1.4.2 (1)(b)-(c); 8.1.1.4.2(2)-(7))
8.5.2, Primary Frequency Response Measurements
8.5.2.1, ERCOT Required Primary Frequency Response
9.2.3, DAM Settlement Charge Types (9.2.3 (1)(h); 9.2.3(1)(l))
*As written in NPRR 960.

## Slide 14: Nodal Operating Guide Sections to be Un-Gray Boxed in Phase 1
The following outlines Nodal Operating Guide sections that will be un-gray boxed in Phase 1. In cases where only a portion of a Section is being un-gray boxed, specific references have been included in parenthesis.
1.4, Definitions (Automatic Generation Control)
2.2.4.1, Maintenance and Verification
2.2.4.2, Regulation Provider Loss of AGC
2.3, Ancillary Services
2.3.1.2, Additional Operational Details for Responsive Reserve Providers (2.3.1.2 (1); 2.3.1.2(3)-(5); 2.3.1.2 (8)(b); 2.3.1.2 (8)(d); 2.3.1.2 (9)-(11))
2.3.1.2.1, Limit on Generation Resources and Controllable Load Resources Providing RRS (2.3.1.2.1(1)-(4))
4.5.2, Operating Procedures(4.5.2 (3)(f)) (4.5.2 (3)(f))
8, Attachment F

## Slide 15: Other Binding Documents to be Un-Gray Boxed in Phase 1
The following outlines Other Binding Documents that will be un-gray boxed in Phase 1.
Methodology for Determining Minimum Ancillary Service Requirements
Procedure for Calculating Responsive Reserve (RRS) Limits for Individual Resources

## Slide 16: FFR Qualification Details - Self Test
The following steps should be followed when conducting a Self Test for FFR:
  Ancillary Service Resource Responsibility must be set equal to MW capacity for which the Resource seeks qualification for FFR.
  The test is performed by adding a frequency offset such that frequency decays low enough to initiate response from the Resource. Note that the initiation setting of the under-frequency relay or similar trigger mechanism shall not be any lower than 59.85 Hz;
  The test starts at time t0 when the frequency exceeds the initiation setting & initiates a response from the Resource. The following signals should be recorded with a resolution of no less than 32 samples per second (a) Frequency (Hz) (b) MW Output (MW)
  Upon completion send recorded data with at least 15 minutes of data to ERCOT.
The following criteria will be used to evaluate Self Test for FFR:
  The total time from the time frequency first decays to a value low enough to initiate action up to the time when full Ancillary Service Resource Responsibility for RRS is delivered should be no more than 15 cycles, including all relay and breaker operating times;
  The resource must demonstrate its ability to sustain the scheduled level of deployment for at least 15 minutes at a minimum level of 95% but not more than a maximum level of 110% of the MW capacity for which the Resource seeks qualification for FFR.
  Note ERCOT systems will track the capacity a Resource providing FFR is qualified to provide.