## Slide 1
Resource Integration Workshop
Resource Integration Topics
ERCOT
Jay Teixeira
March 17, 2020

## Slide 2: Quarterly Stability Assessment (QSA)
Planning Guide 5.9
Next Deadline for QSA
If a GINR is not included in QSA, its Initial Synchronization date will be automatically delayed to the next quarter
All-Inclusive Generation Resource Initial Synchronization Date | Last Day for an IE to meet prerequisites as listed in paragraph (4) below | Completion of Quarterly Stability Assessment
Upcoming January, February, March | Prior August 1 | End of October
Upcoming April, May, June | Prior November 1 | End of January
Upcoming July, August, September | Prior February 1 | End of April
Upcoming October, November, December | Prior May 1 | End of July

## Slide 3: Quarterly Stability Assessment (QSA)
Planning Guide 5.9, Quarterly Stability Assessment
Issue’s seen in previous QSA’s
  10 day comment period for FIS
    Needs to be complete before QSA deadline
    TSPs need to plan for it
  Dynamic Model Review
    Dependent on FIS Stability study
    Need to meet PG 6.9 15 to 30 days prior to QSA deadline

## Slide 4: Facility Study Reports
Trend towards no longer providing separate document
If in one document, need to put reference in file name
  [Project Name][INR#] Solar Facilities and Short-Circuit Report FINAL.pdf
  [Project Name] [INR#]_FIS_(SS_SC_F)_(020218).pdf
Some TSPs have included the Facility Study as an appendix with including reference in file name.
ERCOT Compliance, for FAC002, requires a reference to all four files in preparation for NERC audit
The Facility study can be hard to find without explicit reference

## Slide 5: Adding PG 6.9 Generation as Separate Table in FIS Reports
  Add generation meeting PG6.9 to the cases if they have impacts on the stability of the study area
  List added generation in a separate table in the report
  Specify the cutoff date for adding PG6.9 generation in the report
  PG6.9 generation in monthly GIS reports

## Slide 6: FIS Study Explanation of How GTC’s Respected
The dispatch of generation in the study area is mandated by PG 5.4.5
PGRR 076 includes modifications to this paragraph:
  The dispatch level may be reduced to respect any published stability limits or to reach a power flow solution
ERCOT would like the TSPs to show how the GTC limits were respected in the dispatch
If the POI is near or in any existing GTC, the critical contingencies defined in the QSA/GTC documents should be studied

## Slide 7: TSP supplying dynamic data set and data set contents
Purpose: to help debugging model issues experienced during the QSA and/or flatstart efforts;
Dynamic data set should be submitted together with the FIS stability report on RIOO;
File type “FIS Stability Study CONFIDENTIAL”
Data set should include:
  Power flow case: .sav or .raw file
  Dynamic case .snp or .dyr file

## Slide 8: GINR Time Line (Fastest)

## Slide 9: Swim Lanes and Self-Limiting Resource
Link to BESTF KTC 13

## Slide 10: Resource Integration and Ongoing Operations – Interconnection Services (RIOO-IS) – Releases
No new functionality releases
Attestation Issue – still an issue with attestations
Oncor Comment
  TSP’s request for a view/export file that will show needed data that can be shared with other Oncor stakeholders, i.e., Dashiell, Power Engineers, etc., who may not have RIOO access.

## Slide 11: Active PGRR’s
PGRR071 - Update Interconnection Process Timetables to Align with NPRR926 – Approved 1/1/2020.
NPRR973, NOGRR196, PGRR074, RRGRR022 – Add Definitions for Generator Step-Up and Main Power Transformer - TAC April 1, 2020.
PGRR076 – Improvements to Generation Resource Interconnection or Change Request (GINR) Process – ROS April 2, 2020.

## Slide 12: Oncor Comments
Reactive Power Study timeline
  When in the GINR process should this be due?
  See GINR Time Line in earlier slide
  See PGRR076 addition of paragraph 5.7.1 (4) (vi)
VRT analysis
  Clarification that real power should recover back to full within 1 second after voltage recovery to 0.9 pu
    Preliminary Performance Guideline for VRT Tests, Revision 2, May 23, 2019
    LVRT power recovery expectation in DWG Procedure Manual section 3.1.5.4
Future of the ERCOT Screening Study
  This may already be in the agenda but we’d like to request clarification on how/if ERCOT will be performing the Screening Study for future GINRs
    ERCOT will move towards not performing the Screening Study when a simultaneous SS/FIS is requested in the future

## Slide 13: Other contact information
ResourceIntegrationDepartment@ercot.com is distribution list for Resource Integration department

## Slide 14: Questions?
Thank you!