## Slide 1
Review of January RENA
Jian Chen
Market Analysis and Validation
CMWG
April. 6th, 2020

## Slide 2: Monthly Sum of RENA
Chart: Monthly RENA
| 2018_1 | 2018_2 | 2018_3 | 2018_4 | 2018_5 | 2018_6 | 2018_7 | 2018_8 | 2018_9 | 2018_10 | 2018_11 | 2018_12 | 2019_1 | 2019_2 | 2019_3 | 2019_4 | 2019_5 | 2019_6 | 2019_7 | 2019_8 | 2019_9 | 2019_10 | 2019_11 | 2019_12 | 2020_1
RENA | 17360518.08 | 691747.97 | 16840252.36 | 1969051.32 | 19255110.18 | 30282841.98 | 8971407.82 | 12603966.11 | 6873637.75 | 11345542.9 | 334035.31 | 6944336.96 | 2058297.53 | 3727816.22 | 13403094.87 | 8685081.62 | 5757657.93 | 1258274.42 | 889736.46 | 2689011.93 | 244.83 | 5664537.93 | -4954683.66 | 9852252.01 | 6464832.55

## Slide 3: Daily RENA with RT Congestion
Chart: Daily RENA vs RT Congestion Rent
| 43831 | 43832 | 43833 | 43834 | 43835 | 43836 | 43837 | 43838 | 43839 | 43840 | 43841 | 43842 | 43843 | 43844 | 43845 | 43846 | 43847 | 43848 | 43849 | 43850 | 43851 | 43852 | 43853 | 43854 | 43855 | 43856 | 43857 | 43858 | 43859 | 43860 | 43861
SCED_Congestion_Rent | 1757811.1908 | 20166.0742 | 1227360.932 | 3609653.9661 | 1490043.2118 | 2938310.7037 | 1570866.2579 | 10075301.1762 | 2688767.4954 | 5403607.54 | 3236177.3903 | 4535590.1389 | 3114302.0592 | 2480902.2214 | 2462256.9209 | 4446529.8157 | 3712570.7171 | 1616386.119 | 524470.4921 | 214006.6313 | 2847295.6493 | 1561675.7656 | 797060.1112 | 266247.2407 | 2467023.582 | 3076489.7353 | 1819615.852 | 8822459.5429 | 944871.8076 | 4911635.5377 | 4127571.0867
RENA | 149282.1 | -1115.71 | -11862.45 | 49074.55 | 72306.03 | 152620.51 | 135177.52 | 135180.41 | 203479.78 | 422368.49 | 428212.28 | 1916055.01 | 96310.95 | 111231.8 | 169604.49 | -81689.91 | 201147.46 | 120334.7 | 181133.7 | 34483.36 | -44793.65 | -17234.95 | 26921.2 | 9665.72 | 156267.84 | 233557.24 | 102436.91 | 1341724.68 | 88922.72 | 72611.57 | 32381.86
The total RENA in January was around $6.5M, while the total SCED congestion rent was around $88.8M.
Notes: High RENA on OD 1/12 and OD 1/28

## Slide 4: Daily RENA and Estimated DAM oversold on RT congestion
The total estimated DAM oversold amount in January was around $4.2M.
Chart: Estimated DAM oversold vs RENA
| 43831 | 43832 | 43833 | 43834 | 43835 | 43836 | 43837 | 43838 | 43839 | 43840 | 43841 | 43842 | 43843 | 43844 | 43845 | 43846 | 43847 | 43848 | 43849 | 43850 | 43851 | 43852 | 43853 | 43854 | 43855 | 43856 | 43857 | 43858 | 43859 | 43860 | 43861
Sum of Oversold | 200078.3945 | -2468.8786 | 132385.7283 | -181373.9362 | 104971.0455 | 96642.1422 | 176168.1392 | 463044.9552 | 245952.2788 | 466853.0292 | 306612.6874 | 826880.1341 | 98263.7667 | 101364.3481 | 63627.1843 | -182167.425 | 200174.5538 | 97301.9159 | 204668.981 | 40380.4948 | -24569.9604 | -36001.9875 | 29421.5998 | 22447.0686 | 139667.3957 | 178855.5619 | 103156.2769 | 447456.0233 | 55004.5584 | -37980.3133 | -93094.7351
RENA | 149282.1 | -1115.71 | -11862.45 | 49074.55 | 72306.03 | 152620.51 | 135177.52 | 135180.41 | 203479.78 | 422368.49 | 428212.28 | 1916055.01 | 96310.95 | 111231.8 | 169604.49 | -81689.91 | 201147.46 | 120334.7 | 181133.7 | 34483.36 | -44793.65 | -17234.95 | 26921.2 | 9665.72 | 156267.84 | 233557.24 | 102436.91 | 1341724.68 | 88922.72 | 72611.57 | 32381.86

## Slide 5: OD 1/12/2020
$1.9M RENA was observed. Most of the RENA was related to the following issues:
DAM oversold on the RT congestion: There was about $0.7M DAM oversold on the RT constraint DCPSJON5: 6017__A, as the contingency was disabled in DAM by the Mitchell bend RAS, which is set to be triggered by the overloading on 6017__A.
Different RT Congestion Rent in Settlement: it was found a large difference between SCED calculated RT congestion rent ($4.5M) versus the settlement collected congestion rent ($3.5M), when some of real time energy was settled at the meter prices different from the resource dispatching prices.

## Slide 6: Cause of Different Congestion Rent in Settlement (Example)
The missing congestion rent in Settlement happened when some real time resource meter price (RTRMPR) was higher than the resource’s dispatching price, which was related to the locations of meters and the contingency definition.
G
CB1
Meter 1
Resource
X
SF: 0%
SF: 50%
LN1
SF: 50%
RTRMPR: $30
RTRMPR: $-20
Res LMP: $-20
System Lambda $30
Shadow Price
$100
CB2
Meter 2
LN2
X
300MW
200MW
100MW

## Slide 7: OD 1/28/2020
$1.3 million RENA was observed. Most of the RENA was related to the following issues:
PTP Obligation with links to Options: The RT congestion SVCAMIL8: LAUREL_LA_PAL_1 was inside Valley area and significantly raised the LMPs on some RNs in east Valley area. Therefore, the values of PTP with links to Options sourced from these RNs became negative but settled with $0. The missing revenue was around $1M.
DAM oversold on the RT congestion: There was also $0.6M DAM oversold on the constraint SVAMIL8: LAUREL_LA_PAL_1. The oversold was mostly due to extra one hour extension on the related planned outage.
Notes: Need check the resource submission in DAM on 1/28

## Slide 8: Summary
RENA observed in January, 2020 was relatively moderate, comparing to the historical values.
The majority of RENA was related to congestion “oversold” in DAM, which could be further related to topology difference between DAM and RTM, LDF, and RAS modeling.
PTP w/ links to options also contributed significant part of RENA in January, specially on OD 1/28.
The rest of RENA was related to the differences between SCED and Settlement.