## Slide 1
DC-Coupled Resource and Self Limiting Resource/Facility
(BESTF KTC-11 and KTC-13)
April 2020

## Slide 2: DC-Coupled Resource, KTC-11
One or more Energy Storage Systems (ESS) combined with one or more wind and/or solar generators behind a single point of interconnection (POI), where these combined technologies are interconnected within the site using direct current (DC) equipment. The combined technologies are then connected to the ERCOT grid using the same direct current-to-alternating current (DC-to-AC) inverter(s).
DC-Coupled Resources shall register as an ESR with a DC-Coupled attribute so that ERCOT systems can differentiate it from a stand-alone ESR. In addition, at Registration (RARF/RIOO), Resource Entities will be required to submit the same level of detail for both the generation facility (solar or wind) and the ESS as is required for stand-alone Generation Resources and ESRs.
Notes: This wording is from KTC-11. KTC-11 was approved by TAC on 04/01/2020. ERCOT is working on the NPRR, based on KTC-11, to add DC-Coupled Resource concept into the Protocols.

## Slide 3: Self Limiting generation site, KTC-13
A Self-Limiting generation site is a combination of one or more Generation Resources behind a single POI, where the sum of the capacity of these Resources is greater than either the maximum power export (Pmax) rating as established in the SGIA, or the inverter rating (if DC-Coupled). Similar consideration may also apply to maximum power withdrawal (Pmin), if combined with Energy Storage System.
QSE representing the Self-Limiting generation site bears the responsibility of ensuring (via control scheme or equipment limits) that energy exports from the generation site do not exceed the Pmax and energy withdrawals from the grid do not exceed the Pmin.
If Self-Limiting generation site includes energy storage system it’s covered in BESTF KTC-13 http://www.ercot.com/mktrules/keypriorities/bes/ktc13
Notes: This wording is from KTC-13. KTC-13 was approved by TAC on 04/01/2020. ERCOT is working on the NPRR & PGRR, based on KTC-13, to add Self-Limiting concept into the Protocols.