## Slide 1: Supply Analysis Working Group Report to WMS
May 6, 2020

## Slide 2: SAWG Open Action Items from WMS
TAC Assignment: Review Methodology used to determine CONE
  Status: in progress; update later in report
Review impacts on CDR from monthly generation interconnection report
  Status: ERCOT presented analysis of planned project COD update trends and impact of alternative CDR eligibility criteria on planned capacity accounting at several SAWG meetings
  Does WMS have additional direction?
Review of Resource Adequacy forecasts and development of a Net Load forecast
  Status: Probabilistic SARA modeling in progress; status update later in report
  Probabilistic SARA model update expected for May SAWG

## Slide 3: SAWG April Meeting – Final Summer SARA & CDR Release Plans
Release Date: May 13th
Next SAWG: May 28th – will cover SARA and CDR
Q&A from April SAWG:
  SARA and CDR will include a revised load forecast for COVID-19 impacts, based on latest Moody’s economic scenarios
  Revised load forecast will not be release ahead of CDR/SARA
  ERCOT is currently planning to develop a single COVID-19 impact load forecast
  ERCOT is planning to post the COVID-19 impact load forecast after the May 13th SARA/CDR release

## Slide 4: SAWG April Meeting
Consultant Review of Wind Peak Average Capacity Contribution Methodology:
  Consultant agreed with ERCOT’s methodology of using a 10-year lookback
  Noted that some counties should be switched from “Other” to “Coastal”
  Final report will be posted to Resource Adequacy page soon
NERC 2020 Summer Reliability Assessment/Long-term Reliability Assessment
  Final Summer Reliability Assessment expected June 7th
  Long Term Reliability Assessment:
    Will include data submitted after the CDR release
    Expected December 17th

## Slide 5: SAWG Update - CONE Assignment from TAC
TAC Assignment:
  Review Methodology used to determine CONE
  Note that a comment came up at RTC TF on April 30th , that was within the scope of this assignment
Background:
  SAWG has been working on this since mid 2019
  ERCOT previously presented a timeline for the study to be done in coordination with every other LTSA (= every 4 years) and to feed into the Reserve Margin Study
  Expected documents:
    NPRR for Section 4.4.11 (1)(c)
    Language for a “CONE Study Methodology Draft” to be part of the “ERCOT Study Process and Methodology Manual for EORM MERM”

## Slide 6: SAWG Update - CONE Assignment from TAC
NPRR
  ERCOT and SAWG leadership working on NPRR for Section 4.4.11 (1)(c) “System-wide Offer Caps”
  Will replace current chart and language on revising PNM
  Plan to review at SAWG for stakeholder comment ~ June SAWG
  Goal to have NPRR filed and through stakeholder process by end of 2020
CONE Study Methodology Draft
  Background:
    ERCOT presented language for a “CONE Study Methodology Draft” to be part of the “ERCOT Study Process and Methodology Manual for EORM MERM http://www.ercot.com/calendar/2019/12/13/172748-SAWG
    We requested feed back for February SAWG
  Only comments received from TCPA:
    For Peaker Net Margin purposes a CONE parameter for natural gas-fired Combustion Turbine or peaker, must be used
    If different technologies are to be used, those should each be done as a separate CONE
  Next Steps:
    No other feedback received
    ERCOT to revise “CONE Study Methodology Draft” and bring back to SAWG ~ June SAWG

## Slide 7: SAWG April Meeting – Probabilistic SARA
New Wind Output Modeling Approach:
  Incorporated wind profiles for 1980-2017 and scaled up the profiles based on incremental new installed capacity since 2017
  Fit probability distributions for the wind values for each of the summer peak day hours, 1:00 pm – 8:00 pm
  Applied the correlation coefficients to the Monte Carlo simulation to narrow the range of wind output outcomes across the eight hours
  Findings
    1,000-trial model run using wind profiles resulted in a 50th percentile value of 6,933 MW for HE 5:00 pm; peak average capacity contribution for Preliminary Summer SARA is 6,924 MW – very close
    New wind uncertainty modeling approach reduces simulation run-time by 70%
Incorporated PUN uncertainty modeling, which correlates a net grid injection probability distribution with Load
Next Steps
  Incorporate solar probabilistic modeling similar to wind approach
  Incorporate new wind and solar profile data
  Update model with Final Summer SARA
  Present next version at May SAWG

## Slide 8: SAWG April Meeting
Annual 2019 Unregistered Distributed Generation Report
  Presented to WMS
  First Annual report to include reports from NOIEs of >2 MW of “<50kW”
  Total Unregistered DG of 692 MW
Review of Existing Distributed Generation (2015-2019)
  “Informal” review of both unregistered and registered DG
  Total Settlement-Only DG of 849 MW

## Slide 9: Next SAWG Meeting
May 28th
  May 13th SARA and CDR
  Probabilistic SARA model updates