## Slide 1
Review of March RENA
Jian Chen
Market Analysis and Validation
CMWG
June. 1st, 2020

## Slide 2: Monthly Sum of RENA
Chart: Monthly RENA
| 2018_10 | 2018_11 | 2018_12 | 2018_3 | 2018_4 | 2018_5 | 2018_6 | 2018_7 | 2018_8 | 2018_9 | 2019_1 | 2019_10 | 2019_11 | 2019_12 | 2019_2 | 2019_3 | 2019_4 | 2019_5 | 2019_6 | 2019_7 | 2019_8 | 2019_9 | 2020_1 | 2020_2 | 2020_3
RENA | 11345542.9 | 334035.31 | 6944336.96 | 16840252.36 | 1969051.32 | 19255110.18 | 30282841.98 | 8971407.82 | 12603966.11 | 6873637.75 | 2058297.53 | 5782558.4 | -5002889.63 | 9852252.01 | 3727816.22 | 13403094.87 | 8685081.62 | 5757657.93 | 1258274.42 | 889736.46 | 2689013.3 | 6604.22 | 6464832.55 | 7431714.33 | 26361333.17

## Slide 3: Daily RENA with RT Congestion
Chart: Daily RENA vs RT Congestion Rent
| 43891 | 43892 | 43893 | 43894 | 43895 | 43896 | 43897 | 43898 | 43899 | 43900 | 43901 | 43902 | 43903 | 43904 | 43905 | 43906 | 43907 | 43908 | 43909 | 43910 | 43911 | 43912 | 43913 | 43914 | 43915 | 43916 | 43917 | 43918 | 43919 | 43920 | 43921
RT Congestion_rent | 6894019.1186 | 7433346.6708 | 7175446.0979 | 7836625.6157 | 3521206.1818 | 2954078.6146 | 4609096.9765 | 5749929.6749 | 9706741.9198 | 8585548.1303 | 10670605.4668 | 16635204.1249 | 8351099.8009 | 3538713.7146 | 4456783.2789 | 4371779.1066 | 8226682.8746 | 8372275.279 | 5132167.764 | 4520819.2745 | 4251724.5339 | 9690027.1218 | 9986760.9041 | 15477957.521 | 11725371.5339 | 11400010.2618 | 6982717.7429 | 6000771.7457 | 5190140.392 | 439233.7935 | 1346167.6098
RENA | 624398.17 | 2109182.12 | 288386.52 | -598997.11 | 609546.37 | 287738.91 | 10985.81 | 501674.85 | 130553.93 | 876608.34 | 779291.04 | 447618 | 765570.75 | 226505.9 | 142731.82 | 255861.03 | 1350277.22 | 1420188.6 | 1099787.13 | 853003.58 | 161344.8 | 795648.44 | 5077604.03 | 5552086.16 | 321604.39 | -484582.57 | 482620.45 | 1878250.25 | -2116.8 | -47692.4 | 445653.44
The total RENA in March was around $26.4M, while the total SCED congestion rent was around $221M.

## Slide 4: Daily RENA and Estimated DAM oversold on RT congestion
The total estimated DAM oversold amount in March was around $19.4M.
Chart: Estimated DAM oversold vs RENA
| 43891 | 43892 | 43893 | 43894 | 43895 | 43896 | 43897 | 43898 | 43899 | 43900 | 43901 | 43902 | 43903 | 43904 | 43905 | 43906 | 43907 | 43908 | 43909 | 43910 | 43911 | 43912 | 43913 | 43914 | 43915 | 43916 | 43917 | 43918 | 43919 | 43920 | 43921
RENA | 624398.17 | 2109182.12 | 288386.52 | -598997.11 | 609546.37 | 287738.91 | 10985.81 | 501674.85 | 130553.93 | 876608.34 | 779291.04 | 447618 | 765570.75 | 226505.9 | 142731.82 | 255861.03 | 1350277.22 | 1420188.6 | 1099787.13 | 853003.58 | 161344.8 | 795648.44 | 5077604.03 | 5552086.16 | 321604.39 | -484582.57 | 482620.45 | 1878250.25 | -2116.8 | -47692.4 | 445653.44
Sum of Oversold | 528406.0647 | 1873684.2757 | 15760.4706 | -844451.9928 | 470542.2664 | 237518.1439 | 293098.1169 | 456724.2016 | -196425.3376 | 653318.248 | 435574.3263 | 174576.0014 | 668141.5448 | 108149.1468 | 7459.323 | -95472.7112 | 895089.9488 | 950147.1155 | 899078.8792 | 727030.7568 | -143598.6763 | 257443.2816 | 5000280.5517 | 4839060.6024 | -462313.7368 | -674006.6794 | 507060.1031 | 1731310.216 | -221010.1277 | -68100.1887 | 353090.1796

## Slide 5: OD 3/2/2020
$2.1M RENA was observed on OD 3/2/2020. Its RENA was related to the DAM “oversold” on the several RT constraints on 6100_F and 6100_G in West Texas.
A planned outage was modeled in DAM at one of upstream stations of 6100__F/G, which rerouted the flow and relieved the congestions in DAM. However, the outage was delayed and the information was updated after the DAM run. Therefore, the topology difference between DAM and RTM caused most of the oversold amount.

## Slide 6: OD 3/17/2020~3/19/2020
$1.4M, $1.4M and $1.1M RENA was observed on OD 3/17, 3/18 and 3/19 respectively. Most of the RENA was related to the oversold on the RT constraints in South Texas area.
It was found that those RT constraints were related to the planned outage on the 345kV line from Lobo to Fowlerton. The line outage was scheduled to end on 3/17 but got extended to 3/19. The outage information was updated but after the DAM runs. Therefore, the topology difference between DAM and RTM caused most of the oversold amount.

## Slide 7: OD 3/23/2020 and 3/24/2020
$5.1M and $5.6M RENA was observed on OD 3/23 and 3/24 respectively. The majority of the RENA was related to the oversold on the RT constraint DCRLLSW5: 588_A_1.
It was found that this RT constraint was related to the planned outage on the 138kV line from Lewisville to Jones Street TNP. An outage was also scheduled on the nearby line from TI TNP to West TNP, which was modeled in DAM and relieved the congestion in DAM. However, the later outage was not taken in RT. Therefore, the topology difference between DAM and RTM models caused the “oversold” in DAM.

## Slide 8: OD 3/28/2020
$1.9M RENA was observed on OD 3/28. Most of the RENA was related to the oversold of the RT constraints on 6100_F in West Texas.
Planned outages were scheduled at the stations nearby 6100_F, which were planned to end as the new transmission line was scheduled to energize. However, the outage was then extended as the energization was delayed. The outage information was updated after the DAM run. Therefore, the topology difference between DAM and RTM models caused the “oversold” amount the constraints.

## Slide 9: Summary
$26.4M RENA observed in March, 2020, which was higher than normal months.
The majority of RENA was related to congestion “oversold” in DAM, which could be further related to topology difference between DAM and RTM, LDF, and RAS modeling.
  DAM runs with the latest outage information in outage scheduler when DAM closes at 10AM the day before OD. So any update after that will not be included in DAM model, and may result in the difference between DAM and RTM.
  It should also be noted that the delay, extension or recall of outages are part of normal operations. TSP or QSE shall continually update information in ERCOT outage scheduler based on their latest field conditions.

## Slide 10: Summary (Cont.)
PTP w/ links to options also contributed part of RENA in March, around $4.2 million.
The rest of RENA was related to the differences between SCED and Settlement.

## Slide 11: March CRR Balance Account
Chart: Daily CRR value vs DAM Congestion Rent
| 43891 | 43892 | 43893 | 43894 | 43895 | 43896 | 43897 | 43898 | 43899 | 43900 | 43901 | 43902 | 43903 | 43904 | 43905 | 43906 | 43907 | 43908 | 43909 | 43910 | 43911 | 43912 | 43913 | 43914 | 43915 | 43916 | 43917 | 43918 | 43919 | 43920 | 43921
Payment/Charge to CRRAH | 4451170.56 | 6500825.22 | 9269426.94 | 8559132.55 | 6563962.28 | 2279753.22 | 3425316.61 | 4047137.37 | 5672647.57 | 7797413.35 | 7076230.63 | 8916214.88 | 6312861.91 | 5324348.08 | 4444542.39 | 5004470.29 | 4715314.96 | 5935236.94 | 5623346.15 | 4748364 | 5287363.77 | 6692211.74 | 8362024.42 | 10011724.75 | 16677404.46 | 13353004.25 | 7301973.47 | 3678494.91 | 4355811.79 | 3607949.1 | 4186264.27
DACONGRENT | 4690009.6 | 7247396.28 | 9547298.85 | 8667932.08 | 7856249.49 | 2862782.05 | 3930120.21 | 5059243.64 | 6112986.71 | 8018305.36 | 7725690.13 | 9443304.8 | 6519496.62 | 5507125.81 | 4525480.57 | 5100136.96 | 5227091.92 | 6252992.74 | 6045087.61 | 4982059.65 | 5218661.21 | 6532232.37 | 8611860.12 | 10592752.98 | 14184049.93 | 14246584.93 | 8059067.02 | 4561439.5 | 4995687.84 | 4526300.61 | 4902312.4
Chart: Daily Credit
| 43891 | 43892 | 43893 | 43894 | 43895 | 43896 | 43897 | 43898 | 43899 | 43900 | 43901 | 43902 | 43903 | 43904 | 43905 | 43906 | 43907 | 43908 | 43909 | 43910 | 43911 | 43912 | 43913 | 43914 | 43915 | 43916 | 43917 | 43918 | 43919 | 43920 | 43921
DAILY_CREDIT | 238839.04 | 746571.06 | 277871.91 | 108799.53 | 1292287.21 | 583028.83 | 504803.6 | 1012106.27 | 440339.14 | 220892.01 | 649459.5 | 527089.92 | 206634.71 | 182777.73 | 80938.18 | 95666.67 | 511776.96 | 317755.8 | 421741.46 | 233695.65 | -68702.56 | -159979.37 | 249835.7 | 581028.23 | -2493354.53 | 893580.68 | 757093.55 | 882944.59 | 639876.05 | 918351.51 | 716048.13