## Slide 1
Emergency Settlement under RTC – Non-SCED Failure Scenarios
David Maggio
Austin Rosel
June 10, 2020

## Slide 2: Emergency Settlement under RTC
In 2019, KPs were developed for emergency settlement with a focus on cases with a SCED Failure and where Emergency Base Points are issued.
However, the emergency settlement equations are also used for other conditions that have not been discussed with the RTCTF.

## Slide 3: SCED Failure and Emergency Base Point KPs
KP1.5(13) – (15) processes and emergency settlement when Emergency Base Points are issued due to a SCED failure.
  (13) - The processes and procedures during a SCED/RTC failure will remain the same: Emergency Base Points and held prices (SPPs, Meter prices and MCPCs) through the 15-minute recovery period.
  (14) - In Emergency Base Points, RTC systems will consider the AS awards from the most recent SCED execution. Non-AS awarded capacity will be utilized ahead of AS awarded capacity and, if necessary, Non-Spin capacity will be utilized before ECRS and ECRS will be utilized before Regulation Service and RRS capacity.
  (15) - No new Settlement calculations will be needed to address the case where there is a SCED failure.
The QSE would be settled the same as today. The AS revenues and AS offer curve would not be considered.

## Slide 4: Reason for Review
The existing KPs are focused on one use case of emergency settlement.
Current emergency settlements looks at cost and revenues for energy only.
In some cases, RTC may require additional review to ensure overall Resource cost recovery.
Determine if current settlement mechanisms need to be adjusted for certain situations where the Resource may be impacted by Ancillary Service awards and prices as well as energy dispatch and prices.

## Slide 5: Settlement Type Summary
6.6.9 Settlement
(1) Emergency Base Points Issued.
(2) VDI to operate for unannounced Generation Resource Test
(3) QSGR that comes On-Line as a result of a Base Point greater than zero.
(4) QSE receives a Base Point that is inconsistent with RTSPP (price correction). QSE that receives a manual override. (Emergency “hold” approach).
(5) SCED failure.
(8) CFC test or instructed to operate in CFC mode.

## Slide 6: Acronyms
Ancillary Service (AS)
Key Principle (KP)
ERCOT Contingency Reserve Service (ECRS)
Market Clearing Price for Capacity (MCPC)
Non-Spinning Reserve Service (Non-Spin)
Real-Time Co-optimization (RTC)
Real-Time Co-optimization Task Force (RTCTF)
Responsive Reserve Service (RRS)
Security-Constrained Economic Dispatch (SCED)
Settlement Point Price (SPP)