## Slide 1: NPRR1025 Analysis Resmi Surendran Shell Energy North America

## Slide 2
What is the reason for the change
Current Design
Issues with the proposed change
Open questions

## Slide 3: Analyzing stated reasons for the change
Analyzing reasons given for the proposed change
RTC will not have RDPA in MCPC
  Incorrect per KP1.1 (6) : RDPA will apply to both energy and AS
RTOLRDPA is an energy price difference & it does not represent the value of reserves in Real-Time. RDPA has nothing to do with AS
  Incorrect as current implementation is an approximation of RTC and in RTC, RDPA represents the lost opportunity component of MCPC of online AS reserves
RDPA is not part of DAM
  Partially Incorrect. There is no explicit pricing run in DAM as the OOM actions are taken in RT. However, just like ORDC is indirectly reflected in the DAM prices, RDPA is reflected in DAM prices as well.

## Slide 4: Analyzing stated reasons for the change ….. Continued
RDPA causes divergence issues between DAM and RT
  Incorrect as DAM co-optimizes E & AS and hence includes lost opportunity in AS MCPC. In fact, proposed changes increase divergence as avg DAM MCPC is much higher than avg (ORDC+RDPA) and removing RDPA increases the divergence
RDPA is unnecessarily flowing back and forth between gen & load
  Incorrect as paying for providing additional reserves in RT and charging for non-performance or buying back reserves is fundamental to our market design for creating appropriate market incentives for RT performance and incentive for long term hedging.
RDPA is un-hedgable
  Incorrect as MPs can hedge their risks in DAM and forward markets
Removing RDPA will reduce DAM AS price
  Incorrect under scarcity as RDPA will be reflected in DAM energy offers/bids and hence will be in DAM AS MCPC due to co-optimization

## Slide 5: Current Design
Final energy price is sum of
  system lambda & congestion component from SCED (LMP)
  ORDC adder is calculated based on RT reserves (RTRSVPOR)
  Increase in system lambda in the pricing run (rerunning SCED after removing out of market energy) over the original SCED run (RTRDP)
Payment for energy produced: LMP + RTRSVPOR + RTRDP
Payment for additional reserves in RT: RTRSVPOR + RTRDP
Charges for AS buyback: RTRSVPOR + RTRDP
Net payment for AS deployed in RT: DAM MCPC + LMP
      DAM MCPC + RT energy price – RT AS buyback price
      DAM MCPC + (LMP + RTRSVPOR + RTRDP) – (RTRSVPOR + RTRDP)
      MCPC pays for providing AS & LMP pays for providing energy
BP is consistent with LMP & MP submitted offer

## Slide 6: Issues with proposed change
Inadequate compensation for resources following SCED dispatch
Divergence from RTC design
Suppression of AS price
Divergence of DAM and RT AS price
Exacerbation of current AS double payment under scarcity
Divergence from fundamental scarcity pricing principles

## Slide 7: Issues #1 - Inadequate compensation for following BP
Offer price on the MP submitted offer at BP is consistent with LMP
The final energy price (LMP+ RTRSVPOR + RTRDP) and BP are inconsistent and paying RTRSVPOR + RTRDP to the additional reserves accounts for the inconsistency.

## Slide 8: Issue #2: Divergence from RTC design
RDPA under different scenarios | Scarcity scenario |  |  | Non-scarcity scenario |  | 
 | $ at 59GW | $ at 59.5GW | RDPA | $ at 53GW | $ at 53.5GW | RDPA
Energy | 2750 | 4525 | 1775 | 50 | 55 | 5
REGUP | 2700 | 4475 | 1775 | 0 | 5 | 5
RRS | 2725 | 4500 | 1775 | 25 | 30 | 5
ECRS | 2500 | 3525 | 1025 | 0 | 0 | 0
NSPIN | 1500 | 1500 | 0 | 0 | 0 | 0
Relationship between RDPA for energy and RDPA for online reserve prices in RTC could be analyzed to approximate the relationship between current energy price and the current Ancillary Service imbalance price for online reserves. RTC Automated Scenario Analysis 072219
RTOLRDPA for energy and AS are linked due to lost opportunity and hence RTOLRDPA for energy ends up being the same as the RTOLRDPA for Regulation Service and Responsive Reserve (RRS).

## Slide 9: Issue #3: Suppression of AS price
AS MCPC has two component
  Value based on the available reserve (MW level) from ORDC
  Values based on lost opportunity of providing energy from RDPA
Suppression due to ERS deployment
  From additional OOM reserves
      ORDC reserves are not adjusted for the extra MW created by ERS deployments.
      Mitigation of reserve price suppression due to ERS deployment is currently only accomplished by RDPA adder in AS imbalance.
      Adjusting ORDC reserves won’t fully account for the RDPA removal as VOLL in ORDC calculation is reduced by system lambda
  From lost opportunity of energy
      Removal of RDPA from AS imbalance suppresses AS price due to removal of lost opportunity

## Slide 10: Issue #4: Divergence of DAM and RT AS price
DAM prices already include the risk premium
Contrary to the arguments made, removing components from already lower RT AS price further exasperate the divergence
AS prices on 8/13 & 8/15 where much lower in DAM because Energy prices were lower in DAM. The expectation of scarcity was lower.
Yrs Vs $/MWh | DAM MCPC for RRS | ORDC | RDPA | RT MCPC (ORDC+RDPA)
2017 | $9.77 | $0.21 | $0.16 | $0.37
2018 | $17.64 | $1.97 | $0.08 | $2.05
2019 | $26.61 | $9.76 | $3.55 | $13.31
HE 15 DAM Vs SCED 15:05 | REGUP | RRS | NSPIN | HB_BUSAVG | ORDC | RDPA | Lambda | ORDC+RDPA | Final SPP
8/13/2019 | $1,489 | $2,542 | $1,484 | $1,510 | $2,367 | $5,629 | $1,005 | $7,995 | $9,000
8/15/2019 | $786 | $818 | $779 | $803 | $2,983 | $5,098 | $920 | $8,080 | $9,000

## Slide 11: Issue #4: Divergence of DAM and RT AS price
A higher expectation of scarcity will cause a higher DAM energy offers/bids which in turn will result in higher AS MCPC in DAM due to co-optimization in DAM
  When Energy and AS are linked the market clearing for marginal resources will follow
  Profits from energy = Profits from AS
  DAM LMP – Energy offer = DAM MCPC – AS offers
  DAM MCPC = DAM LMP – Energy offer + AS offers

## Slide 12: Issue #5: Exacerbation of current double payment
Currently, 1MW of RRS awarded in DAM gets DAM MCPC + RT LMP when deployed. Under the proposed change, 1MW of RRS awarded in DAM gets DAM MCPC + RT LMP + RT RDPA
The proposed change exacerbates the current double payment for AS under scarcity due to ORDC potentially going to zero as approach scarcity.
Current double payment issue: Under scarcity, currently ORDC could go to zero while under RTC AS MCPC & energy price will go to $9k.
  1MW of RRS awarded in DAM gets DAM MCPC which could be as high as $9k. In RT, when the RRS is deployed, ORDC could go to zero and energy price could go to $9k. Removing RDPA from AS imbalance would increase the situations where the 1MW of RRS gets net paid $18k.

## Slide 13: Issue #6: Divergence from scarcity pricing principle
Paying for providing additional reserves in RT and charging for non-performance or buying back reserves is fundamental to our market design for creating appropriate market incentives.
Reducing the buyback price reduces the incentive for Ancillary Service deliverability in Real-Time and reduces the incentive for long term hedging, both of which are considered as key benefits of scarcity pricing mechanism.
Reducing the RT AS price for reserves reduces the incentive for making additional reserves available in RT.

## Slide 14: Next Steps: Need to answer
What is the exact problem we are trying to solve? Are we creating more problems with the change?
What is the impact of RDPA on RRS MCPC under RTC?
How is the change consistent with scarcity pricing design?
Why is ‘scarcity pricing/DAM hedging for scarcity pricing/creating incentive for entity to hedge long term’ an issue with market design?
How to address the issue of MPs losing money from following SCED dispatch with the proposed?
How to address removal of mitigation of reserve price suppression due to ERS deployment with proposed change?

## Slide 15
Questions?