## Slide 1
Battery Storage Capacity Contribution for CDR and BESTF update
Supply Analysis Working Group
Julia Matevosyan
Resource Adequacy
June 22nd, 2020

## Slide 2: Research Study Findings (NREL, LBNL, EPRI, ICF)
Storage capacity contribution is still a topic of ongoing research
ERCOT has reviewed storage capacity contribution studies carried out by the National Renewable Energy Laboratory (NREL), Lawrence Berkeley National Laboratory (LBNL), Electric Power Research Institute (EPRI) and ICF International (ICF)
NREL’s, EPRI’s and ICF’s studies all included ERCOT system as one of their test cases
Even though the methods used in the studies are different, the conclusions are generally very similar

## Slide 3: Research Study Findings (NREL, LBNL, EPRI, ICF)
Storage capacity contribution depends on its duration and intended use (i.e. AS or energy arbitrage or both).
Storage duration is determined as maximum energy divided by maximum discharge capacity.
Based on the studies, storage with sufficient duration is expected to contribute with 100 % capacity over peak net load hours.
The width of the net load peak is system-specific but as more storage is added to a system the width of peak net load will increase.
Thus, for storage of a given duration there will be a maximum installed capacity after which it is no longer contributing 100% over the entire duration of the net load peak.

## Slide 4: Current Situation
Based on 05/31/2020 GIS Report:
153 MW of installed battery storage capacity
643 MW with SGIA and Financial Security Posted
100 MW with SGIA
109 MW of planned DGRs
almost 7 GW of battery storage (with FIS started) in the interconnection queue with COD before mid-2023 .
about 1 GW of those have COD before summer 2021

## Slide 5: Current Situation and BESTF Impact
ERCOT currently uses 0% capacity contribution for battery storage
ERCOT currently does not collect data on storage duration (h) or maximum energy (MWh).
This data will be available once NPRR1002 “Energy Storage Resource Single Model Registration and Charging Restrictions in Emergency Conditions…” and RRGRR023 are approved and implemented in RIOO-IS, and Resource Entities update their resource information.
NPRR1002 and RRGRR023 are currently on track for August BOD approval
RIOO-IS implementation is expected by Q4 2021
Notes: NPRR1002 voted unanimously by ROS to endorse, PRS unanimously voted to recommended approval on 6/11/2020, next step is July PRS for IA, then July TAC and August BOD
RRGRR023 ROS unanimously recommended approval, next step is July ROS for IA, then July TAC, then August BOD.

## Slide 6: Storage Capacity Contribution: Proposed Way Forward
ERCOT proposes to evaluate storage capacity contribution based on historic performance over peak load hours (or peak net load hours), similarly to wind and solar
For this evaluation storage should be divided into groups by duration
ERCOT will need storage MWh and duration information prior to RIOO implementation.
ERCOT may issue periodic RFI to gain this information for upcoming projects until RIOO implementation
RFI should also collect information on intended use, projects that are intended solely for provision of FFR should be excluded from capacity evaluation.

## Slide 7: Storage Capacity Contribution: Proposed Way Forward
Once a meaningful amount of storage resources becomes commercial (capacity or number of resources threshold?), ERCOT will start including storage for CDR Reserve Margin calculation purposes.
ERCOT will file an NPRR documenting the methodology for calculating storage capacity contribution:
  Using historic data, ERCOT will be calculating historic average capacity contributions across peak load hours and net load peak hours, similarly to wind and solar.
  ERCOT then adjust the capacity contribution of storage in accordance with historic performance

## Slide 8: Self-Limiting Facilities and Self-Limiting Resources
NPRR1026 BESTF-7 Self-Limiting Facilities and Self-Limiting Resources at July PRS for language review.
Self-Limiting Facility – Multiple GRs or ESRs at the same POI with a limit on combined maximum MW injection and/or withdrawal that is less than installed capacity of these Resources.*
Self-Limiting Resource – A GR or ESR with a limit on its maximum MW Injection and/or withdrawal which is less than the installed capacity of the Resource.*
ERCOT needs to capture these limits in Resource Adequacy reporting.
* This is a summary, not an exact definition as per NPRR1026

## Slide 9: DC-Coupled Resources
NPRR BESTF-6 DC-Coupled Resources coming up soon
DC-Coupled Resources – One or more Energy Storage Systems (ESS) combined with one or more wind and/or solar generators behind the same POI, where these combined technologies are interconnected within the site using direct current (DC) equipment. The combined technologies are then connected to the ERCOT grid using the same direct current-to-alternating current (DC-to-AC) inverter(s).
RRGRR023 includes additional parameters that will be requested from Self-Limiting Facilities, Self-Limiting Resources and DC-Coupled Resources

## Slide 10: Capacity Contribution of DC-Coupled Resources
ERCOT proposes to evaluate capacity contribution of DC-Coupled Resources based on historic performance.
Once a meaningful amount of such resources becomes commercial (MW or number threshold?), ERCOT will start including DC-Coupled Resources for CDR Reserve Margin calculation purposes.
Recent EPRI study on capacity contribution of DC-Coupled Resources (using ERCOT as a test case) has found that it depends on:
storage duration
storage size in relation to the overall plant size
type of other generation in the DC-Coupled Resource (i.e. solar or wind)
Method of charging (grid charging or self-charging)
Intended use of DC-Coupled Resources (energy only or AS)
amount of background solar.
For capacity contribution evaluation, it may be necessary to group DC-Coupled Resources based on the above criteria

## Slide 11: Co-located vs Standalone Storage
Based on 05/31/2020 GIS Report:
Almost 7 GW of storage in the interconnection queue
About 43% of those are co-located with solar
Currently ERCOT does not have information if co-located plants are going to be DC or AC-coupled

## Slide 12: References to the Studies
EPRI: Energy Storage Capacity Value Estimation, Report 3002013957, January 2019, http://membercenter.epri.com/abstracts/Pages/ProductAbstract.aspx?ProductId=000000003002013491
NREL: The Potential for Battery Energy Storage to Provide Peaking Capacity in the United States, Report, June 2019, https://www.nrel.gov/docs/fy19osti/74184.pdf
LNBL: Drivers of the Resource Adequacy Contribution of Solar and Storage for Florida Municipal Utilities, October 2019, https://emp.lbl.gov/publications/drivers-resource-adequacy
ICF: Unlocking the Hidden (Capacity) Value in Energy Storage, Whitepaper, 2016 https://www.icf.com/insights/energy/unlocking-the-hidden-capacity-value-in-energy-storage

## Slide 13: Thank you! Questions?
Julia Matevosyan
jmatevosjana@ercot.com

## Slide 14: ERCOT: 2018 Form EIA-860 Data - Schedule 3, 'Energy Storage Data' (Operable Units Only)
Note: Duration (h) is calculated as Energy Capacity (MWh)/Maximum Discharge Rate (MW) and is not part of Form EIA – 860 Data