## Slide 1: Simple “Dec. Game” Example

## Slide 2: Example
We have a 195MW solar resource at node A serving a load center at B through a 200MW line.
A 9.9999MW unaffiliated battery locates at node A.
The solar resource has sold an “as available/at the busbar” product to a large corporation that doesn’t follow icky power markets, they just like solar!
This leaves the solar facility completely hedged without buying CRRs.
The battery owner has 2 ways to make revenue. They can participate in the A/S market or they can arbitrage energy prices.
Since the line from A to B has never congested in the past, the battery owner is able to pick up all 180MWs of the peak weekday and weekend CRRs available from A to B for the minimum 1 cent price.
Once the month begins, the battery operator runs at 5MWs constraining the line dropping the price to $0 with the price at B continuing at an average price of $20/MWh. The battery operator is able to do this for two hours then has to spend the third recharging at the unconstrained $20 price. For simplicity, let’s assume the battery operator bought pricetaking PTPs to move the CRR position into real time.

## Slide 3: Settlement
From a settlement standpoint for every hours, the battery operator:
Is charged for the energy withdrawn from the system – -9.9999MWhs/3 * $20/MWh = -$66.67
Is charged for the 5MWs of congestion flow - -5MWs * $20/MWh = -$100.00
Is charged for the CRR position - -180MWs * $0.01/MWh = -$1.80
Is paid for the 180MW PTP position held 180MWs * $20/MWh = $3,600.00
Total settlement per hour $3,431.53
Total settlement for the month * 12 * 30 $1,235,351.00
Note that in the other 12 hours the battery is also gaining revenue by providing A/S.
In the next month, the Battery Owner continues to bid low for the CRRs
  If the CRRs come up in price the Battery Owner doesn’t clear and provides A/S
  If the CRRs clear, we are back to arbitrage