## Slide 1
Ancillary Service Deployment Expectations and Durations Follow Up
ERCOT
July 22, 2020

## Slide 2: Acronyms
ERCOT Contingency Reserve Service (ECRS)
Key Principle (KP)
Fast Frequency Response (FFR)
Market Clearing Price for Capacity (MCPC)
Non-Spinning Reserve Service (Non-Spin)
Regulation Down Service (Reg-Down)
Regulation Up Service (Reg-Up)
Responsive Reserve Service (RRS)
State-Of-Charge (SOC)

## Slide 3: Reiteration of high-level points from the July 15th meeting
Each Ancillary Service product is designed and procured to mitigate a unique kind of risk in Real-Time.
To address these different risks, there are different types of Resource attributes that are needed to maintain reliability and that are intended to be incented through the market for Ancillary Services.
  For example, “Fast-burn” vs. “slow-burn”

## Slide 4: Example for FFR presented on July 15th
 | HSL/LSL (MW) | Max/Min SOC (MWh) | FFR Qual. MW | Energy Bid $/MWh | Energy Offer $/MWh | FFR Offer $/MW/h
Battery A | +-10MW | Max: 20MWh Min: 0.1MWh | 20MW | -10 to 0 MW @$45/MWh | 0 to 10 MW @$100/MWh | 20MW @$0/MW/h
Battery B | +-10MW | Max: 20MWh Min: 0.1MWh | 20MW | -10 to 0 MW @$-300/MWh | 0 to 10 MW @$100/MWh | 20MW @$1/MW/h
Note:
SOC is not used in the ERCOT market software.
Ramp Rate for both Batteries are 999 MW/minute
To be awarded 20 MW of FFR, the Base Point must be -10MW and there must be sufficient stored energy (i.e., SOC) to deliver a sustained 10 MW injection to grid for 15 minutes. 20 MW of FFR is by stopping charging consumption of 10 MW and then injecting 10 MW as measured at the POI
The minimum SOC required for both Batteries to provide 20 MW of FFR is 2.5MWh (10MW*0.25hour)

## Slide 5: Example for FFR presented on July 15th cont.
Note: Similar logic would apply for Reg-Up/Down (also 15 minute duration ) and ECRS/Non-Spin (1 hour duration)
20 MW
18 MW
A-UDSP
A-SOC
-10 MW
10 MW
3 MWh
3.33 MWh
2.833 MWh
2 MWh
A-FFR Award
SCED 1
SCED 2
SCED 3
FFR Frequency event @t+2 minutes that lasts for ~7.5 minutes
SCED
Off Cycle
Value |  | SCED 1 @t=0 | SCED Off Cycle @t=3 | SCED 2 @t=5 | SCED 3 @t=10
Battery A telemetry | MW | -10 MW | 10 MW | 10 MW | 10 MW
 | FFR cap | 20 MW | 20 MW | 20 MW | 18 MW
 | SOC | 3 MWh | 3.16 MWh | 2.833 MWh | 2.0 MWh
Battery B telemetry | MW | 0 MW | 0 MW | 0 MW | 0 MW
 | FFR cap | 20 MW | 20 MW | 20 MW | 20 MW
 | SOC | 20 MWh | 20 MWh | 20 MWh | 20 MWh
SCED prices | LMP | $40 / MWh | $43 / MWh | $40 / MWh | $40 / MWh
 | RRS MCPC | $0.5 / MWh | $0.8 / MWh | $0.5 / MWh | $1.0 / MWh
Battery A awards | BP | -10 MW | -10 MW | -10 MW | -10 MW
 | FFR | 20 MW | 20 MW | 20 MW | 18 MW
Battery B awards | BP | 0 MW | 0 MW | 0 MW | 0 MW
 | FFR | 0 MW | 0 MW | 0 MW | 2 MW
3.16 MWh

## Slide 6: Example 2 from Dr. Siddiqi’s slides (material duplicated for discussion purposes)
Note:
GR is the marginal Resource when 80MW Frequency Event occurs
Most Resources fully awarded with Energy at $35/MWh & RRS at $5/MW/h; all other capacity Energy & AS offers above $200/MW/h
The minimum SOC required for Battery to qualify to provide 20 MW of FFR is 2.5MWh (10MW*0.25hour) under both Options
Option 1: Min SOC required for Battery to offer 20MW of FFR into SCED is 0.83MWh – exactly same as needed to offer 20MW Energy
Option 2: Min SOC required for Battery to offer 20MW of FFR into SCED is 2.5MWh – only 0.83MWh needed to offer 20MW of Energy
 | HSL/LSL (MW) | Max/Min SOC (MWh) | FFR/RRS Qual. MW | Energy Bid $/MWh | Energy Offer $/MWh | FFR/RRS Offer $/MW/h
Battery | +-10MW | Max: 20MWh Min: 0.1MWh | 20MW | -10 to 0 MW @$200/MWh | 0 to 10 MW @$200/MWh | 20MW @$0/MW/h
GR | 100MW or 80MW | N/A | 20MW | N/A | 0 to 100 MW @$40/MWh | 20MW @$10/MW/h

## Slide 7: Example 2 from Dr. Siddiqi’s slides cont.
Note: Similar logic would apply for Reg-Up/Down (also 15 minute duration ) and ECRS/Non-Spin (1 hour duration)
20 MW
12 MW
BES-UDSP
BES-SOC
-10 MW
10 MW
2.5 MWh
2.83 MWh
2.333 MWh
1.5 MWh
BES-FFR Award
SCED 1
SCED 2
SCED 3
FFR Frequency event @t+2 minutes that lasts for ~7.5 minutes
SCED
Off Cycle
2.66 MWh
18.66 MW
Value |  | SCED 1 @t=0 | SCED | SCED 2 @t=5 | SCED 3 @t=10
 |  |  | Off Cycle @t=3 |  | 
Battery telemetry | MW | -10 MW | 10 MW | 10 MW | 10 MW
 | FFR cap/Award (Opt 1) | 20 MW | 20 MW | 20 MW | 20 MW
 | FFR cap/Award (Opt 2) | 20 MW | 20 MW | 18.66 MW | 12 MW
 | Base Point (Opt 1) | -10 MW | -10 MW | -10 MW | -10 MW
 | Base Point (Opt 2) | -10 MW | -10 MW | -8.66 MW | -2 MW
 | SOC | 2.5 MWh | 2.66 MWh | 2.333 MWh | 1.5 MWh
GR telemetry | MW | 0 MW | 80 MW | 80 MW | 80 MW
 | RRS cap | 16 MW | 16 MW | 16 MW | 16 MW
 | RRS Award (Opt 1) | 0 | 0 | 0 | 0
 | RRS Award (Opt 2) | 0 | 0 | 1.34 | 8
 | Base Point (Opt 1) | 0 MW | 80 MW | 80 MW | 80 MW
 | Base Point (Opt 2) | 0 MW | 80 MW | 78.66 MW | 72 MW
SCED prices | LMP (Opt 1) | $35 / MWh | $40 / MWh | $40 / MWh | $40 / MWh
 | RRS MCPC (Opt 1) | $5 / MWh | $10 / MWh | $10 / MWh | $10 / MWh
 | LMP (Opt 2) | $35 / MWh | $40 / MWh | $200 / MWh | $200 / MWh
 | RRS MCPC (Opt 2) | $5 / MWh | $10 / MWh | $170 / MWh | $170 / MWh

## Slide 8: Discussion on outcome difference pre-deployment
The previous examples have focused on outcomes where the SOC drops because of deployment, but what if the SOC is lower pre-deployment?
Value |  | SCED 1 @t=0
Battery telemetry & awards | MW | -10 MW
 | FFR capability and award (Opt 1) | 20 MW
 | FFR capability and award (Opt 2) | 13.33 MW
 | Base Point (Opt 1) | -10 MW
 | Base Point (Opt 2) | -10 MW
 | SOC | 0.93 MWh
Physical capability of battery | MW actually able to deploy for 15 minutes | 13.33 MW
 | Duration capable of deploying at full FFR award MW (Opt 1) | 5 minutes
 | Duration capable of deploying at full FFR award MW (Opt 2) | 15 minutes
 | FFR capability for next SCED after 5 minutes of deployment (Opt 1) | 10 MW
 | FFR capability for next SCED after 5 minutes of deployment (Opt 2) | 12.22 MW
 | FFR capability for next SCED with no FFR deployment (Opt 1) | 20 MW
 | FFR capability for next SCED with no FFR deployment (Opt 2) | 16.66 MW
Pricing outcomes (non-scarcity) | RRS MCPC (Opt 1) | “X” $/MWh
 | RRS MCPC (Opt 2) | >= “X” $/MW/h
Pricing outcomes (scarcity) | RRS MCPC (Opt 1) | ASDC @ “Y” MW
 | RRS MCPC (Opt 2) | ASDC @ “Y” MW minus 6.67 MW

## Slide 9: Conclusions
In developing the KPs, the task force already defined Ancillary Services by outlining the qualification for those services.
Allowing Resources to sell a 15-minute or hourly service based on 5-minute capability masks the current system need and true value of that service.
In general, this may mean that prices are too low. But it may also lead to higher prices when the service is truly needed and deployed beyond the 5-minute timeframe.
The two proposals do result in changes to dispatch, awards, and Resource commitment
  If there has not yet been a need to deploy Ancillary Services and Resources are able to offer in to those Ancillary Services bases on 5-minute capability, the market signal is that less capability is needed.

## Slide 10
Appendix – Updated Summary Tables based on July 15th Discussion

## Slide 11: Summary of the Ancillary Service Discussions
Ancillary Service Subcategory | Qualification Duration | Triggered/Deployed | Recalled
RRS (PFR from SCED-dispatchable Resources) | 15 min. | Automatically based on frequency to deploy more | Automatically based on frequency to deploy less
RRS (under-frequency relay) | 1 hour | Automatically based on a frequency trigger (59.7 Hz); or Manually instructed by ERCOT (TE*, EEA or NERC Standards) | Deployed until recalled by ERCOT based on frequency and PRC recovery (XML message shows “0” deployment)
RRS (FFR from SCED-dispatchable Resources) | 15 min. | Automatically based on a frequency trigger (59.85 Hz); or Manually instructed by ERCOT (NERC Standards) | Deployed until recalled by ERCOT based on frequency (LFC signal shows “0” deployment)
RRS (FFR from Non-Controllable Load Resources) | 15 min | Automatically based on a frequency trigger (59.8 Hz); or Manually instructed (AS Manager) by ERCOT (EEA or NERC Standards) | Deployed until recalled by ERCOT. Allowed to withdraw from the grid only after frequency is stable and PRC above 2,500 MW
RRS (Resources in synchronous condenser fast-response mode) | 1 hour | Automatically based on a frequency trigger (59.8 Hz); or Manually instructed by ERCOT (TE*, EEA or NERC Standards) | Deployed until recalled by ERCOT based on frequency and PRC recovery (LFC signal shows “0” deployment)
*TE refers to Transmission Emergency
The table below is intended to provide a summarized view covering topics from both recent special RTCTF meetings
  For all instances, less Ancillary Services may be awarded based on the interaction between power balance and the ASDCs as system conditions get more scarce.

## Slide 12: Summary of the Ancillary Service Discussions cont.
Ancillary Service Subcategory | Qualification Duration | Triggered/Deployed | Recalled
Reg-Up/Down | 15 min. | Automatically through LFC signals to deploy more | Automatically through LFC signals to deploy less
ECRS (SCED-dispatchable Resources including QSGRs) | 1 hour | Less awarded based on the interaction between power balance and the ASDCs | More awarded based on the interaction between power balance and the ASDCs
ECRS (Resources in synchronous condenser fast-response mode | 1 hour | Automatically based on a frequency trigger (59.8 Hz); or Manually instructed by ERCOT (TE*, EEA or NERC Standards) | Deployed until recalled by ERCOT based on frequency and PRC recovery (LFC signal shows “0” deployment)
ECRS (“blocky” Load Resources) | 1 hour | Manually instructed by ERCOT (TE*, EEA or NERC Standards) | Deployed until recalled by ERCOT based on frequency and PRC recovery (LFC signal shows “0” deployment)
“On-line” Non-Spin | 1 hour | Less awarded based on the interaction between power balance and the ASDCs | More awarded based on the interaction between power balance and the ASDCs
“Off-line” Non-Spin (including non-active power augmentation) | 1 hour | Manually instructed by ERCOT based on PRC, 30-minute system-wide ramp capability, or special congestion circumstances | Deployed until recalled by ERCOT based on PRC, 30-minute system-wide ramp capability, or special congestion circumstances
*TE refers to Transmission Emergency