## Slide 1
PLWG: PGRR082 Summary
August 19, 2020

## Slide 2: PGRR Purpose
ERCOT is seeing an increasing number of small generators being proposed
The existing interconnection process does not apply to these smaller projects
The need for visibility of the size and location of these projects becomes more important as the number of them grows
There is also need to clarify interconnection requirements for small generators connecting at either transmission or distribution voltage

## Slide 3: PGRR Summary
Create the concept of large and small generators
  Large generators are 10 MW or greater
  Small generators are less than 10 MW
  Interconnection kV level is not considered in the definition
Maintain the existing interconnection process for large generators
Create a tracking process for small generators and small capacity modifications (1 MW or greater, less than 10 MW)
Create language specific to large generators on the distribution system
Streamline and reorganize the existing PG Section 5 language in order to better incorporate new language

## Slide 4: Summary of Proposed Additions to the PG
A new sub-section was added to create a tracking process for small generators
  Interconnection Procedures for Small Generators
Several existing sub-sections were modified to include small generators and large, distribution-connected generators in Section 5 and 6.9
  Applicability
  Status sub-sections
  Interconnection Agreements
  Security Screening Study
  Additions of Proposed Generation to the Planning Models

## Slide 5: Proposed: 5.2 General Provisions
Ordered the sequence of the initiation process
Moved several existing sub-sections into the new 5.2
  Applicability
  Confidentiality
  Renamed the section related to updating requested information
  Inactive Status
  Project Cancellations
  Interconnection Agreements and Procedures

## Slide 6: Proposed concepts for Applicability
Small Generator Process
  New generator
    Aggregate nameplate capacity* is less than 10 MW
  Modified capacity
    Increase any generator’s nameplate capacity by 1 MW or greater, but less than 10 MW
Large Generator Process
  New generator
    Aggregate nameplate capacity* is 10 MW or greater
  Modified capacity
    Increase any generator’s nameplate capacity by 10 MW or greater
    Increase an existing small generator to a large generator nameplate capacity
*Aggregate nameplate capacity is calculated by summing the capacity of all generators at a substation that are proposed by the same Entity or Affiliates

## Slide 7: Proposed: 5.3 Interconnection Study Procedures for Large Generators
Several existing sub-sections were relocated into the new 5.3:
Security Screening Study
Full Interconnection Study
ERCOT Economic Study
ERCOT QSA

## Slide 8: Proposed: 5.4 Interconnection Procedures for Small Generators
New sub-section includes:
Small Generator Review Meetings
Submission of IA and TSP and/or DSP Studies and Technical Requirements
Reviews and Approval to Submit Model Information
Transmission System Reliability Impact

## Slide 9: Comments
Bill Blevins
Bill.Blevins@ercot.com
(512)-248-6691

## Slide 10: Proposed Deletions to PG Section 5
Existing Sub-section | Existing Sub-section Name | Reason for Deletion
5.1 | Introduction: Paragraph (2) | unnecessary
5.1.1 | Applicability: Paragraph (2) | unnecessary
5.1.2 | Responsibilities | redundant
5.2 | Generation Interconnection Process: Paragraph (1) | unnecessary
5.2.2 | Generation Interconnection or Change Request Submission Requirements: Paragraph (1), (3) | redundant
5.3 | Full Interconnection Study Request: Paragraph (2), (3), (4) | unnecessary/redundant
5.4.2.1 | Full Interconnection Study Process Overview: Paragraph (6) | unnecessary
5.4.2.2 | Full Interconnection Study Elements: Paragraph (7) | unnecessary
5.5.2 | Other Arrangements for Transmission Service | unnecessary
5.7.2 | Interconnection Study Fees: Paragraph (1) | unnecessary
5.7.3 | Generation Interconnection and Full Interconnection Study Application Fees: Paragraph (2)(c) | unnecessary
5.7.5 | Interconnection Process Timetables | belongs in handbook
5.8.1 | Other Standards | unnecessary

## Slide 11: Proposed Relocations in PG Section 5
Existing Sub-section | Existing Sub-section Name | New Sub-section
5.2.1 | Generation Interconnection or Change Request Application: Paragraph (7), (8), (9) | 5.2.2
5.2.2 | Generation Interconnection or Change Request Submission Requirements: Paragraph (2) | 5.2.2(4)
5.3 | Full Interconnection Study Request | 5.3.2
5.4.7 | Economic Study | 5.3.3
5.4.9 | Proof of Site Control | 5.3.2.1
5.4.10 | Confidentiality | 5.2.3
5.5 | Interconnection Agreement | 5.2.8
5.7.2 | Interconnection Study Fees: Paragraph (2) | 5.2.2
5.7.3 | Generation Interconnection and Full Interconnection Study Application Fees: Paragraph (1)(c) | 5.2.2(3)
5.7.3 | Generation Interconnection and Full Interconnection Study Application Fees: Paragraph (2) | 5.3.2(2)(c)
5.7.6 | Inactive Status | 5.2.5
5.7.7 | Cancellation of a Project Due to Failure to Comply with Requirements | 5.2.6
5.8.2 | Transformer Tap Position | 5.2.4(1)
5.9 | Quarterly Stability Assessment | 5.3.4

## Slide 12: Proposed Renaming in PG Section 5
Existing Sub-section | Existing Sub-section Name | New Sub-section Name
5 | Generation Interconnection or Change Request | Generation Interconnection or Modification
5.2 | Generation Interconnection Process | Initiation of the Generation Interconnection or Modification
5.3 | Full Interconnection Study Request | Full Interconnection Study
5.3.2 | Modifications to Request Declarations of Resource Data Accuracy | Duty to Update Project Information and Respond to ERCOT and TSP Requests
5.4 | Study Processes and Procedures | Interconnection Study Procedures for Large Generators
5.4.2.1 | Full Interconnection Study Process Overview | Full Interconnection Study Scoping Process
5.4.2.2 | Full Interconnection Study Elements | Full Interconnection Study Procedure