## Slide 1
Update On NPRR 863 Phase 2 Scope for FFR
August 14, 2020
BESTF
Nitika Mago
Operation Analysis, ERCOT

## Slide 2: Ancillary Services from Energy Storage Resources
Following the full implementation of FFR as a part of NPRR 863 FFR Phase 2 project, for any particular operating hour in the Day Ahead Market (DAM), a Energy Storage Resource (ESR) Generation Resource (ESR-Gen) and ESR Controllable Load Resource (ESR-CLR) will be able to offer Regulation, RRS-PFR, RRS-FFR and Non-Spin simultaneously*.
  This is different from phase 1 implementation wherein (a) only ESR-CLR is able to offer RRS-FFR in DAM (b) ESR-CLR may either offer RRS-FFR or RRS-PFR (c) ESR-Gen is not able to offer RRS-FFR.
Similarly for any particular operating hour, DAM optimization may award an ESR-Gen or ESR-CLR Regulation, RRS-PFR, RRS-FFR and Non-Spin concurrently.
  ESR-Gen and ESR-CLR will be able to carry RRS-PFR and RRS-FFR concurrently in Real Time.
*Assuming the ESR-Gen or ESR CLR is qualified for the A/S or A/S sub-type it is offering in DAM.
Resource Type | Online Reserves |  |  |  |  | Regulation-Down | Offline Reserves
 | REGUP | RRS-PFR | RRS-FFR | RRS-UFR | ONNS | REGDN | OFFNS
ESR-CLR | Yes | Yes | Yes | No | Yes | Yes | No
ESR-Gen | Yes | Yes | Yes | No | Yes | Yes | No

## Slide 3: Ancillary Services from Load Resources
Following the full implementation of FFR as a part of NPRR 863 FFR Phase 2 project, for any particular operating hour in the Day Ahead Market (DAM), a Non-Controllable Load Resource (NCLR) will be able to offer either RRS-FFR, or RRS-UFR*.
For any particular operating hour, DAM optimization may award an NCLR per its offer, either RRS-FFR or RRS-UFR.
  NCLR will be not able to carry RRS-FFR and RRS-UFR concurrently in Real Time.
*Assuming the NCLR is qualified for the A/S sub-type it is offering in DAM.
Resource Type | Online Reserves |  |  |  |  | Regulation-Down | Offline Reserves
 | REGUP | RRS-PFR | RRS-FFR | RRS-UFR | ONNS | REGDN | OFFNS
NCLR (Offer Option 1) | No | No | Yes | No | No | No | No
NCLR (Offer Option 2) | No | No | No | Yes | No | No | No