## Slide 1
Summer 2020 Load Shape Analysis
Carl Raish
Principal Load Profiling an Modeling
DSWG - September 18, 2020

## Slide 2: Analysis Overview
  This analysis looks at changes in load shapes that occurred in 2020.
  The approach is to estimate regression models for the class of ESIIDs using the Jan 1, 2018 to March 10, 2020 time period.
  The models were then run with 2020 inputs to develop load shapes to compare to actual load shapes that were realized.

## Slide 3: Aggregate Residential Load on 4CP Days
Actual Residential load shapes are generally higher than the model estimates in the morning, early afternoon and night hours.
The largest load increases occur close to noon.

## Slide 4: Aggregate Non-Res – Non 4CP Load on 4CP Days
Actual Non-Residential load shapes are generally lower than the model estimates throughout the day.
The largest load decreases occur close to HE17.

## Slide 5: Aggregate BUSIDRRQ Load on 4CP Days
Actual BUSIDRRQ load shapes are generally lower than the model estimates throughout the day.
The largest load decreases occur close to HE17.
August graph is based on initial settlement.

## Slide 6: Residential Load Impact
Residential load models were estimated using Jan 2018 – Feb 2020, and used to estimate what the load would be during the months of 2020.
Weekday average energy was 6% higher for the April – August time period and is down to about 4% higher for August.
Weekday HE17 load was 8% higher for the April – August time period and is down to about 3% higher for August.
J
M
F
A
M
J
M
F
A
M
J
J
J
A
J
M
F
A
M
J
J
A

## Slide 7: Non-Residential – Not On 4CP Billing
Non-Residential load models were estimated using Jan 2018 – Feb 2020, and used to estimated what the load would be during the months of 2020.
Weekday average energy was 8% lower for the April – August time period and has trended up to about 2% lower for August.
Weekday HE17 load was 10% lower for the April – August time period and has trended up to about 5% lower for August.
J
M
F
A
M
J
J
A
J
M
F
A
M
J
J
A

## Slide 8: Telemetry Analysis - 4CP Responders
  For the last few years we have used State Estimator telemetry from substations and circuits to identify a set of circuits with significant levels of 4CP response.
  Note: the circuits account for a small but significant share of the total 4CP response.
  The list of identified circuits (217) has been incorporated into a display tool to provide real-time awareness to ERCOT operators of 4CP response occurring.
  The telemetry from these circuits has been used in this analysis to get a sense of load shape changes for this set of ESIIDs with more current data (as opposed to using settlement interval data which has a ~35 day lag for BUSIDRRQ ESIIDs).

## Slide 9: Telemetry Analysis – 217 4CP Circuits
Weekday average energy and HE 17 load for these 4CP responder circuits has been about 13% lower for the April – August time period for 2020 vs 2019.
The reduction started on about April 1 and leveled out on April 13.
The load is slowly trending back up and is now down about 9% from 2019.
J
M
F
A
M
J
J
A
J
M
F
A
M
J
J
A

## Slide 10: Hurricane Hannah Valley Station Aggregate Load
Hannah impact started July 25 and had lingering effects through August 10.

## Slide 11: Questions?
ON
OFF
craish@ercot.com 512/248-3876