## Slide 1
DAM RAS Modeling Error and Potential Price Correction – Analysis of Price and Settlement Impacts
David Maggio
Director, Market Design & Analytics
TAC
9/23/2020

## Slide 2: Background - Timeline
August 19, 2020 – A modeling update was made in the ERCOT Network Model to update the status of a Remedial Action Scheme (RAS).
  The update was manually implemented through the process of a Downstream Production Change (DPC), which is a process to update the Network Model between routine database loads.
  The purpose of this DPC was to enable the Bearkat RAS, both in ERCOT’s Energy Management System (EMS) and Market Management System (MMS). The Bearkat RAS was enabled correctly with the DPC.
  During the process of this DPC, however, the Stryker Creek RAS was inadvertently disabled for the Day-Ahead Market (DAM) between Operating Days (OD) August 20 and August 24, 2020. This issue did not impact the Real-Time Market.
    August 24, 2020 – ERCOT identified the incorrect status of the Stryker Creek RAS in MMS and corrected its status before the start of DAM for OD August 25.
    August 25, 2020 – ERCOT notified the market regarding a DAM price correction for OD August 24 and corrected prices for that day before the prices became final.
    August 27, 2020 – ERCOT issued Market Notice M-A082720-01 regarding incorrect RAS modeling in the DAM and determined that the DAM prices on ODs August 20, 21 and 23 were also impacted.

## Slide 3: Price Correction Impact Review
ERCOT’s analysis used original settled quantities with corrected prices based on DAM reruns, with the Stryker Creek RAS correctly enabled.
  Note: The Settlement data provided herein is an estimate; final Settlement amounts may differ.
All Settlement amounts are net amounts due to/from ERCOT in $ thousands. Negative amounts are increased payments to Market Participants; positive amounts are increased charges.
The % amount is the absolute value of the % of impact to the previously settled net amount due to/from ERCOT.
In addition to the DAM impacts detailed herein:
  Balancing account impacts resulting in additional $7K funds to be deposited into CRR Balancing account. The amounts paid/refunded due to resettlement will depend on the Balancing Account balance at the time of resettlement.
  Minimal changes to Real-Time Settlements due to Ancillary Service charges that will be reconciled based on actual Load Ratio Shares.

## Slide 4: Price Correction Study for the DAM
Market: DAM
Impacted ODs: 8/20/2020, 8/21/2020 and 8/23/2020
Price Correction Methodology: ERCOT reran the DAM on these ODs with the Stryker Creek RAS correctly enabled.
The following slides include analysis of the price and Settlement impacts of the DAM price correction using the new DAM solution.
  Quantities (awarded MWs) do not change; only prices.

## Slide 5: Potential DAM Price Correction Price Impacts
OD | Count of Changes in Price for the 4 Hubs and 4 Competitive Load Zones across all Hourly Intervals of the Affected ODs |  |  |  |  |  |  | 
 | < -$10/MWh | >= -$10/MWh & < -$1/MWh | >= -$1/MWh & < -$0.1/MWh | >= -$0.1/MWh & < $0.1/MWh* | >= $0.1/MWh & < $1/MWh | >= $1/MWh & < $10/MWh | >= $10/MWh | No Change
8/20/2020 | 0 | 0 | 81 | 64 | 4 | 0 | 0 | 43
8/21/2020 | 0 | 0 | 21 | 82 | 12 | 0 | 0 | 77
8/23/2020 | 0 | 0 | 52 | 40 | 24 | 0 | 0 | 76
8/24/2020* | 0 | 0 | 94 | 17 | 32 | 24 | 0 | 25
** For 7/7/2020, corrected DAM prices were posted prior to becoming final.
Note: a positive value indicates that the corrected or proposed price is higher than the original price.
* This column does not include prices that were not affected.

## Slide 6: Potential DAM Price Correction Settlement Impacts
 | Energy Purchases |  | Energy Sales |  | PTP Purchases |  | CRR Settlements |  | AS Payments |  | Make-whole Payment | 
8/20/2020 | (76.6) | 0.4% | 78.8 | 0.4% | (5.4) | 0.8% | 8.3 | 1.4% | 10.9 | 1.7% | 0.0 | 0.0%
8/21/2020 | (38.6) | 0.2% | 40.9 | 0.2% | (5.0) | 0.7% | 5.0 | 0.9% | 2.2 | 0.4% | 0.0 | 0.0%
8/23/2020 | (10.9) | 0.1% | 11.3 | 0.1% | (2.4) | 0.3% | 1.8 | 0.2% | (0.8) | 0.1% | 0.0 | 100.0%
8/24/2020* | 389.5 | 1.5% | (387.3) | 1.5% | (57.2) | 20.3% | 66.0 | 20.2% | (7.5) | 1.1% | 0.8 | 26.5%
* For 8/24/2020, corrected DAM prices were posted prior to becoming final.
Note: all Settlement amounts are net amounts due to/from ERCOT in $ thousands.

## Slide 7: DAM Price Correction Settlement Impacts on Counter-Parties
** The maximum of percentage change to any single Counter-Party with impact more than $500 (set as NA when no single counter party has impact more than $500)
* The maximum of absolute impact to any single Counter-Party in $ thousands
OD | Maximum Impact to Counter-Parties | 
 | Maximum Amount* | Maximum Percentage**
8/20/2020 | 4.4 | 67.6%
8/21/2020 | 1.5 | 59.2%
8/23/2020 | 0.7 | 2.8%
8/24/2020*** | 6.8 | 202.2%
*** For 8/24/2020, corrected DAM prices were posted prior to becoming final.