## Slide 1
Review of July RENA
Jian Chen
Market Analysis and Validation
CMWG
Oct. 5th, 2020

## Slide 2: Monthly Sum of RENA
Chart: Monthly RENA
| 2018_7 | 2018_8 | 2018_9 | 2018_10 | 2018_11 | 2018_12 | 2019_1 | 2019_2 | 2019_3 | 2019_4 | 2019_5 | 2019_6 | 2019_7 | 2019_8 | 2019_9 | 2019_10 | 2019_11 | 2019_12 | 2020_1 | 2020_2 | 2020_3 | 2020_4 | 2020_5 | 2020_6 | 2020_7
RENA | 8971407.82 | 12603966.11 | 6873637.75 | 11345542.9 | 334035.31 | 6944336.96 | 2058297.53 | 3727816.22 | 13403094.87 | 8685081.62 | 5757657.93 | 1258274.42 | 889736.46 | 2689013.3 | 6604.22 | 5782591.59 | -5054952.39 | 9942188.32 | 6398653.76 | 7591379.41 | 26975003.07 | 2778215.61 | 14181885.21 | -360546.88 | 1578253.8

## Slide 3: Daily RENA with RT Congestion
The total RENA in July was around $1.6M, while the total SCED congestion rent was around $66.6M.
Chart: Daily RENA vs RT Congestion Rent
| 44013 | 44014 | 44015 | 44016 | 44017 | 44018 | 44019 | 44020 | 44021 | 44022 | 44023 | 44024 | 44025 | 44026 | 44027 | 44028 | 44029 | 44030 | 44031 | 44032 | 44033 | 44034 | 44035 | 44036 | 44037 | 44038 | 44039 | 44040 | 44041 | 44042 | 44043
RT Congestion_rent | 2196274.3172 | 740152.52 | 1119532.8149 | 1098723.018 | 1388983.6544 | 1231883.7011 | 238351.0726 | 4180173.45 | 2470005.6227 | 1738868.4497 | 447928.1652 | 414317.9907 | 1436411.0421 | 1972602.8005 | 953434.6797 | 2707873.3028 | 3556317.7713 | 1100192.1407 | 391763.2513 | 687844.2133 | 405245.8679 | 240951.0994 | 222925.4204 | 401037.4555 | 587313.19 | 52109.0335 | 9284134.9356 | 205502.7493 | 506316.8346 | 8391858.0374 | 16243532.667
RENA | 347493.03 | -121005.78 | 1561.51 | 13811.01 | 112974.66 | 104490.23 | 9500.69 | 164011.44 | 173239.93 | -52051.74 | 29437.83 | -90498.98 | 1274.77 | 44584.24 | 28654.21 | 42349.73 | -81498.8 | -21564.32 | -13568.02 | -16105.27 | 147765.9 | 7190.99 | 2037.84 | -34729.12 | -3597.84 | 1781.95 | 2067842.49 | -77530.09 | -30678.41 | -90079.89 | -1088840.39

## Slide 4: Daily RENA and Estimated DAM Oversold on RT Congestion
The total estimated DAM oversold amount in July was around
$0.7M.
Chart: Estimated DAM oversold vs RENA
| 44013 | 44014 | 44015 | 44016 | 44017 | 44018 | 44019 | 44020 | 44021 | 44022 | 44023 | 44024 | 44025 | 44026 | 44027 | 44028 | 44029 | 44030 | 44031 | 44032 | 44033 | 44034 | 44035 | 44036 | 44037 | 44038 | 44039 | 44040 | 44041 | 44042 | 44043
RENA | 347493.03 | -121005.78 | 1561.51 | 13811.01 | 112974.66 | 104490.23 | 9500.69 | 164011.44 | 173239.93 | -52051.74 | 29437.83 | -90498.98 | 1274.77 | 44584.24 | 28654.21 | 42349.73 | -81498.8 | -21564.32 | -13568.02 | -16105.27 | 147765.9 | 7190.99 | 2037.84 | -34729.12 | -3597.84 | 1781.95 | 2067842.49 | -77530.09 | -30678.41 | -90079.89 | -1088840.39
Sum of Oversold | 356450.7888 | -112471.1981 | -11078.1507 | -61255.5142 | 79407.5735 | 58682.9302 | -10549.4716 | 148503.1941 | 186937.9736 | -42683.3296 | 8144.5324 | -112241.4548 | -24415.3746 | 8281.7363 | -2065.9765 | 14139.5037 | -53145.8424 | 8202.8661 | -10122.2646 | -10103.4115 | 95672.4457 | -3914.5718 | -1537.6616 | -15236.2177 | 9660.2754 | 8519.6911 | 2026684.1297 | -70681.6434 | -42903.1019 | -454870.775 | -1265290.573

## Slide 5: OD 7/27/2020
$2.1M RENA was observed on OD 7/27/2020. All the RENA was related to the DAM “oversold” on the RT constraints in Valley area: DNEDWED8: AZTECA_HEC1_1 ($1.4M) and SMV2NED8: NEDIN_MVWED_1A_1 ($0.7M)
Hurricane Hanna went through South Texas area on 7/25 and caused multiple transmission outages in Valley area. The RT constraints above were related to the force transmission outages on the lines from North Edinburg to McColl Road and North McAllen.
The outage was original entered on 7/25 with its planned end date set as 7/26. However, the outage was extended on 7/26 after the damage was further evaluated. The extension was submitted after OD 7/27 DAM run.

## Slide 6: OD 7/31/2020
-$1.1M RENA was observed on OD 7/31/2020. Most of the negative RENA caused by “undersold” on the RT constraints in Valley area.
As transmission line outages remained and Valley loads went high due to high temperatures, significant RT congestion rent (~$16M) were observed. Meanwhile, it was observed that the RT congestion rent was actually higher than the RT value of DAM flows, which resulted in the “undersold” condition with negative RENA.
The “undersold” on OD 7/31/2020 was related to two causes: 1) LDF difference between DAM and RTM; 2) RT flow in the constraint was higher than the constraint limit.

## Slide 7: Summary
A total of $1.6M RENA observed in July, 2020. High positive and negative RENA were observed in the end of month, after Hurricane Hanna went through South Texas area.
The RENA in the end of July were related to the DAM “oversold” or “undersold” on the RT constraints in Valley area, which were further related to topology difference between DAM and RTM, LDF, and the difference between RT flow and limit.
PTP w/ links to options also contributed part of RENA in July, around $1.0 million, but no significant day stood out.

## Slide 8: July CRR Balance Account
Chart: Daily CRR value vs DAM congestion Rent
| 44013 | 44014 | 44015 | 44016 | 44017 | 44018 | 44019 | 44020 | 44021 | 44022 | 44023 | 44024 | 44025 | 44026 | 44027 | 44028 | 44029 | 44030 | 44031 | 44032 | 44033 | 44034 | 44035 | 44036 | 44037 | 44038 | 44039 | 44040 | 44041 | 44042 | 44043
Payment/Charge to CRRAH | 2267606.73 | 1653149.39 | 1075493.09 | 1486931.85 | 970337.28 | 1151265.94 | 1194658.31 | 2414947.53 | 3297466.43 | 3081009.6 | 2784887.95 | 1895695.57 | 2613946.55 | 3592771.03 | 1764203.84 | 1389281.76 | 1679585.33 | 1428451.31 | 699796.02 | 1232296.92 | 953017.74 | 602767.95 | 897569.58 | 875448.17 | 848814.82 | 780608.29 | 422571.67 | 2834846.48 | 5845535.04 | 5021115.77 | 3100196.51
DACONGRENT | 2874920.5 | 2084486.56 | 1318931.33 | 1997677.92 | 1245202.35 | 1500239.64 | 1545025.7 | 2898316.41 | 3841288.45 | 3652912.83 | 3130902.22 | 2340061.6 | 3274574.53 | 4378433.53 | 2175184.63 | 1699114.08 | 1755860.97 | 1541884.25 | 912328.12 | 1546471.61 | 1139494.36 | 783291.49 | 1193541.5 | 1144952.09 | 1170180.58 | 1114772.64 | 529390.91 | 2462568.56 | 4854018.03 | 4578679.33 | 2868405.55
Chart: Daily Credit
| 44013 | 44014 | 44015 | 44016 | 44017 | 44018 | 44019 | 44020 | 44021 | 44022 | 44023 | 44024 | 44025 | 44026 | 44027 | 44028 | 44029 | 44030 | 44031 | 44032 | 44033 | 44034 | 44035 | 44036 | 44037 | 44038 | 44039 | 44040 | 44041 | 44042 | 44043
DAILY_CREDIT_OR_SHORT | 607313.77 | 431337.17 | 243438.24 | 510746.07 | 274865.07 | 348973.7 | 350367.39 | 483368.88 | 543822.02 | 571903.23 | 346014.27 | 444366.03 | 660627.98 | 785662.5 | 410980.79 | 309832.32 | 76275.64 | 113432.94 | 212532.1 | 314174.69 | 186476.62 | 180523.54 | 295971.92 | 269503.92 | 321365.76 | 334164.35 | 106819.24 | -372277.92 | -991517.01 | -442436.44 | -231790.96