## Slide 1: Demand Side Working Group update to the Wholesale Market Subcommittee
10/07/2020
Christian Powell, PEC, Chair
Holly O’Neill, MP2, Vice Chair
Mike Hourihan, CPower, Vice Chair

## Slide 2: June 19 DSWG Webex Meeting Recap
  Controllable Load Resources in the Ancillary Service Market
  Behind the Meter – Energy Storage
  ERCOT Summer 2020 Load Analysis
  Demand Response Survey Update
  Load Resources (non-CLR) Update
  Goals Review

## Slide 3: Controllable Load Resources in the Energy and Ancillary Service Markets
ERCOT presented on the current status of CLRs participating in the ERCOT region.
Applicable Definitions and General Review of Ancillary Services in the ERCOT Region
Load Resource Characteristics
Registration and Modeling
Qualification and Testing
Real Time Energy Market
Ancillary Service Participation
Performance Analysis and Compliance Activities

## Slide 4: Controllable Load Resources in the Energy and Ancillary Service Markets (cont.)
Notable Takeaways:
Most Load Resources participating in AS market are non-controllable LRs.
Recently several data centers have begun participating as CLRs.
CLRs are awarded the same as GRs and face similar requirements.
CLRs can participate in Reg Up, Reg Dn, RRS and NSRS.
The portion of a CLR’s load providing AS can be limited from 20% to 100% of the MPC (based on its droop setting).
Performance for AS is included in the CLREDP metrics.

## Slide 5: Behind the Meter – Energy Storage
Shams Siddiqi presented on battery energy storage collocated with load behind a single POI that requests to participate in the AS Market as a CLR not a Generation Resource.
Battery would charge/discharge behind the POI, but not inject MW back to grid
Battery would not be eligible for WSL treatment
Battery would be the controlling device for load proposed to be modeled as CLR
Currently, a CLR that is behind the same POI as Load must separately telemeter its energy.
ERCOT committed to working with Mr. Siddiqi to discuss all the issues and will bring back to DSWG next month.

## Slide 6: ERCOT Summer 2020 Load Analysis
ERCOT gave a presentation on Load response covering Summer 2020 (through August).
  The analysis looked at changes in load shapes that occurred in 2020.
  The approach was to estimate regression models for ESIIDs using the Jan 1, 2018 to March 10, 2020 time period.
  The models were then run with 2020 inputs to develop load shapes to compare to actual load shapes.
  Results:
  Actual Residential load shapes are generally higher than the model estimates in the morning, early afternoon, and night hours with the largest increases occurring close to noon.
  Actual Non-Residential load shapes are generally lower than the model estimates throughout the day with the largest decreases occurring close to HE17.
  Weekday average energy and HE 17 load for telemetered 4CP responder circuits has been about 13% lower for the April – August time period for 2020 vs 2019.
  The load is slowly trending back up and is now down about 9% from 2019.

## Slide 7: Demand Response Survey Update
ERCOT gave a presentation on the status of DR Survey notifications and participation submittals.
August 15: Participating REPs and NOIEs submitted responses to ERCOT indicating whether they expect to have Demand/Price response programs operating on September 1 snapshot date.
September 1: REPs may submit requests for ERCOT ESIID file to use for pre-validation of files submitted to ERCOT.
October 15: date for REPs to have submitted an ESIID file and if applicable on Event File.
October 31: Deadline for REP and NOIE file submissions.
November 7: Deadline for NOIEs to resolve any discrepancies identified by ERCOT.
December 15: ERCOT report posted to MIS.

## Slide 8: Load Resources (non-CLR) Update
ERCOT posted the deployments of NCLRs back several years to 2011.
Still taking feedback on future presentation to convey total participation of NCLRs in the market including data not already provided in the 60-day and 2-day reports, identifying location of load resource reports, and reporting on NCLR prorations.