## Slide 1
ERCOT Update
Behind-the-Meter Energy Storage
ERCOT Staff
DSWG
October 16, 2020

## Slide 2
Behind-the-Meter Battery Energy Storage
At the 9/18/20 DSWG meeting, Crescent Power proposed the following:
Battery co-located with firm Load behind the meter that will never inject into the grid as measured at the POI, and desires to:
  Provide Ancillary Services (primarily RRS) from full range of battery
  Reduce Load during pricing events by discharging battery -- but ensuring a smaller or zero net Load, as measured at POI
  Reduce Load during 4CP intervals by discharging battery -- but ensuring a smaller or zero net Load, as measured at POI
ERCOT reviewed the concept of such a Resource registering as a CLR “with additional requirements” -- but with those requirements it became obvious that in reality this is an ESR with unique requirements
Note that in order to provide AS the ESS must register as a “R”esource (ESR)
This presentation suggests a possible path forward for this concept, pending stakeholder discussion and input
Preliminary discussion only (not an ERCOT endorsement)

## Slide 3: Behind-the-Meter Battery Energy Storage
High-level summary
ERCOT is still in the initial stages of reviewing necessary changes
Additional discussions will be required before writing protocols (again – this is offered as a possible path forward)
ESR subtype:
  Would register as an ESR but operate “like” a CLR
  Would be modeled separately from any existing firm load with the following unique operating characteristics:
    Never injects to the grid
    Settled at Load Zone SPP
  Participates in the energy market (SCED) as an ESR
    In combo model era, CLR portion has a RTM Energy Bid and Generation Resource portion is either in OUT status or sets HSL to zero
    In single model era, participates only with the Bid portion of the Energy Bid/Offer Curve
  Participates in AS markets
  If the battery is responding to price event or 4CP, it cannot be active in the market
    Could set OUT status or set LSL=HSL=0

## Slide 4: Behind-the-Meter Battery Energy Storage
The following changes would be necessary for this ESR subtype to be able to meet its stated objectives:
  ESR would be settled at its Load Zone Settlement Point
  Restricting this Resource type to sites where there is a single POI with a single modeled Load present prior to installation of the battery – i.e., transition to ESR
  Telemetry for the ESR and mandatory telemetry requirement at the POI
    Modifications to calculation of PRC using battery State of Charge telemetry
    Allow for telemetry offsets to allow SCED to provide full range of basepoints – e.g., instead of -10 to +10 MW allow -20 to 0 MW
    Performance criteria similar to CLR
  Address how ESR will provide RRS when ESR is charging or when ESR is fully charged and how ERCOT will measure performance
    Specify new requirements/rules for telemetry of the Load and ESR
  Specify new requirements/rules for ESR outage
  Reactive requirements same as ESR
Note: ERCOT has a concern that as an increasing number of large single-site CLRs come onto the system and are dispatched on Load Zone shift factors, ERCOT may start experiencing problems managing congestion with these resources.