## Slide 1
Day-Ahead Market (DAM) Performance
Kenan Ögelman
Vice President, Commercial Operations
Technical Advisory Committee
October 28, 2020

## Slide 2: DAM Agenda
Delays
Overview
Submissions
Efforts Undertaken to Reduce PTP Bids
Binding Constraints
What Does DAM Delay Mean?
Summary

## Slide 3: DAM Delays
Chart: # of Late DAM Publishes Dec, 2010 – Sep, 2020
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Total | 5 | 42 | 17 | 4 | 6 | 4 | 5 | 2 | 9 | 10 | 20

## Slide 4: DAM Overview
Allotted Time for DAM Execution
  3 ½ Hours (10:00am - 1:30pm)
  Allotted time includes optimization time, data input validation, PVT execution/validation, DAM output posting process, etc.
Security Constrained Unit Commitment & Dispatch
  Iterations between the optimization engine (MIP & QP) that commits/dispatches Resources, and the network analysis that determines transmission feasibility of commitment/dispatch and supplies transmission constraints to the optimization engine
Factors that can lead to long run times
  Large volume of variables – both continuous and integer variables
    More Integer variables can exponentially increase run-time
    Currently experiencing performance issues when volume of PTP interval submissions exceed 170K
  Large number of modeled transmission constraints, temporal constraints and transmission outages, typically in shoulder months that can lead to more transmission constraints
  Increase in number of Settlement Points (Resource Node, Hub, or Load Zone) can lead to long run times

## Slide 5: DAM Submissions
Both Energy Bids and Energy-Only Offers trend up, while TPO trends down
Chart: Energy intervals Dec 2010 - Sep 2020

## Slide 6: DAM Submissions – Average PTP Quantities (MWH) Becoming More Granular
Chart: PTP Quantity Average Dec 2010 - Sep 2020

## Slide 7: DAM Submissions – Total PTP quantities (MW) and intervals trend upward
Chart: PTP Quantity vs Intervals Dec 2010 - Sep 2020

## Slide 8: Efforts Undertaken to Reduce PTP Bids
NPRR925, Increasing Minimum Quantity for PTP Obligation Bids, and SCR798, Limit on the total number of PTP Obligation bids that can be submitted into the Day-Ahead Market (DAM) per Qualified Scheduling Entity (QSE) and per Counter-Party (CP), was implemented on August 8, 2019
On March 25, 2020, a market notice was sent to change the Counter-Party limit of SCR798 (99,999 to 2,000) for DAM PTP bids
On July 13, 2020, a market notice was sent to change the Counter-Party limit from 2,000 to 1,500 for DAM PTP bids

## Slide 9: DAM Binding Constraints
* # of constraints considered by DAM is much larger
Chart: DAM Binding Constraints Dec 2010 - Sep 2020

## Slide 10: What Does DAM Delay Mean?
DAM delays are disruptive to the market and create additional steps for DAM operators and downstream ERCOT operations to manage the timeline deviation
Upon DAM delay:
  ERCOT control room will issue an Advisory and make hotline calls. They will also have to cancel Advisory and make hotline calls following the completion of DAM
  Market Participants must manage timeline deviation and respond to ERCOT hotline call
If DAM delays continue to worsen, ERCOT may have to abort DAM. This may create risk for stakeholders.
    Impact on Real-Time energy market
    ERCOT procures AS in the DAM

## Slide 11: Summary
The allotted 3 ½ hours is not purely optimization time. The allotted time also includes, but is not limited to:
  Process time needed for PVT data prep, transfer, and execution
  Input/output verifications
  Error handling
  DAM close delays
Over the years ERCOT has seen increase in large volumes of continuous and integer variables
  DAM participation has trended upward, with PTP bids largely contributing to the increased variables
  DAM Energy Bids (EB) and Energy-Only Offers (EOO) have increased
  DAM binding constraints have trended upward
ERCOT wants to engage with stakeholders to manage the increased complexities in a way that provides the greatest value to the market.

## Slide 12: Questions???