## Slide 1
Proposed Ancillary Service Methodology and
Preliminary Quantities For 2021
Nov 18, 2020
TAC
ERCOT Staff

## Slide 2: Stakeholder Discussion Timeline
September 08, 2020 – PDCWG (Visit 1)
September 21, 2020 – WMWG (Visit 1)
October 14, 2020 – PDCWG (Visit 2)
October 27, 2020 – WMWG (Visit 2)
November 04, 2020 - WMS
November 05, 2020 - ROS
November 18, 2020 - TAC
December 8, 2020 - BoD

## Slide 3: Scope of Discussion
Following is a summary of the proposed changes in the methodologies used for determining Ancillary Service (A/S) quantities for 2021.
  ERCOT is not recommending any change to the methodology used for determining Responsive Reserve Service (RRS).
    ERCOT is proposing to change the minimum RRS-PFR limit for 2021 based on updates to NERC’s BAL-003 Interconnection Frequency Response Obligation (IFRO) assessment for 2021.
  ERCOT is recommending one change in each of the methodologies used for computing Non-Spin and Regulation reserves to account for growth in installed PVGR capacity.
The A/S quantities for 2021 contained in this presentation are based on the methodology that was approved in December 2019. The quantities for 2021 reflect moving forward the historic data on which these are based, unless otherwise noted.
A redline version of the draft methodology and spreadsheets that contain the associated quantities for January through October of 2021 have been posted on the meeting page for this meeting.

## Slide 4: Responsive Service Methodology (RRS) - 2021
ERCOT is not recommending any changes to the methodology used for determining Responsive Reserve Service (RRS).
ERCOT is proposing to change the minimum RRS-PFR limit for 2021 to 1420 MW. This change is based on preliminary results from NERC’s BAL-003 Interconnection Frequency Response Obligation (IFRO) assessment for 2021. This preliminary IFRO analysis for 2021 primarily captures an increase in ERCOT’s Resource Contingency Criteria from 2750 MW to 2805 MW.
The preliminary RRS quantities for January 2021 through October 2021 in subsequent slides have been computed using 2019 and 2020 system inertia conditions and updated RRS table.
  The RRS table tracks RRS requirements for different inertia conditions. This table was updated for 2021 to use a minimum RRS-PFR limit of 1420 MW.

## Slide 5: Hourly Average RRS Comparison
Notes: On an average red is similar to blue.
On an average largest increase between red and blue is 53 MW in May. Avg increase is 11 MW
On an average largest increase between gray and red is 91 MW in Feb, Mar. Avg increase is 62 MW
On an average largest increase between gray and blue is 126 MW in May. Avg increase is 73 MM

## Slide 6: Regulation Service Methodology - 2021
ERCOT is recommending one change in the methodology used for computing Regulation reserves. Specifically, ERCOT is proposing to create and incorporate Solar Adjustment tables into the Regulation Service Methodology similar to the Wind Adjustment tables.
  Solar Adjustment tables will track incremental MWs of Regulation needed to account for additional variability per 1000 MW increase in installed solar capacity.
The preliminary Regulation quantities for January 2021 through October 2021 in subsequent slides have been computed using current methodology (2019 and 2020 five-minute net load variability), updated Wind Adjustment tables and the proposed Solar Adjustment tables.

## Slide 7: Solar Adjustment Tables - 2021
Notes: Avg Reg Up adjustment for solar pre SCR811 is 16 MW, post SCR811 is 5 MW
Avg Reg Down adjustment for solar pre SCR811 is 16 MW, post SCR811 is 5 MW

## Slide 8: Regulation Up March
Notes: Trends between blue and orange are fairly similar. Largest change is 71 MW in HE23.
Max increase between orange and red is 220 MW in HE18. On an average increase of 58 MW
Max increase between orange and green is 60 MW in HE16,HE17. On an average increase of 23 MW

## Slide 9: Regulation Up June
Notes: Trends between blue and orange are fairly similar. Largest change is 90 MW in HE19.
Max increase between orange and red is 275 MW in HE19. On an average increase of 89 MW
Max increase between orange and green is 70 MW in HE15. On an average increase of 21 MW

## Slide 10: Regulation Down March
Notes: Trends between blue and orange are fairly similar. Largest change is 36 MW in HE22.
Max increase between orange and red is 158 MW in HE9. On an average increase of 69 MW
Max increase between orange and green is 71 MW in HE16. On an average increase of 26 MW

## Slide 11: Regulation Down June
Notes: Trends between blue and orange are fairly similar. Largest change is 103 MW in HE14.
Max increase between orange and red is 279 MW in HE9. On an average increase of 91 MW
Max increase between orange and green is 71 MW in HE17. On an average increase of 23 MW

## Slide 12: Hourly Average Regulation Comparison
Notes: Reg Up
On an average blue and orange are fairly similar
On an average largest increase between orange and red is 89 MW in June. Avg increase 71 MW.
On an average largest increase between green and red is 23 MW in Feb-May. Avg increase 20 MW.
Reg Down
On an average blue and orange are fairly similar
On an average largest increase between orange and red is 91 MW in June. Avg increase 74 MW.
On an average largest increase between green and red is 26 MW in Mar, April. Avg increase 21 MW.

## Slide 13: Non Spinning Reserve Methodology (Non-Spin) - 2021
ERCOT is recommending one change in the methodology used for computing Non-Spin reserves. Specifically, ERCOT is proposing to create and incorporate a Solar Over-Forecast Error Adjustment table.
  Solar Over-Forecast Error Adjustment Table will track estimated increase in solar over forecast error per 1000 MW increase in installed solar capacity.
The preliminary Non-Spin quantities for January 2021 through October 2021 in subsequent slides have been computed using current methodology (2018, 2019 and 2020 Net load and Net load Forecast), updated Wind Over-Forecast Error Adjustment table and the proposed Solar Over-Forecast Error Adjustment table.

## Slide 14: Solar Over-Forecast Error Adjustment Table - 2021
Solar Over-Forecast Error Adjustment Table track estimated increase in solar over forecast error per 1000 MW increase in installed solar capacity.
Max: 63 MW per 1000 MW additional solar capacity
Mean: 16 MW per 1000 MW additional solar capacity

## Slide 15: Non-Spin March
Notes: Max change between 2020 and 2021 in HE11-14 is 136 MW. On an average decrease of 42 MW
Max change between 2021 and Adj in HE15-18 is 209 MW. On an average increase of 80 MW
Between 2020 and Adj on an average increase of 38 MW

## Slide 16: Non-Spin June
Notes: Max change between 2020 and 2021 in HE11-14 is 86 MW. On an average decrease of 8 MW
Max change between 2021 and Adj in HE15-18 is 224 MW. On an average increase of 91 MW
Between 2020 and Adj on an average increase of 83 MW

## Slide 17: Hourly Average Non-Spin Comparison
Notes: On an average orange is lower than blue
On an average largest increase in red is 92 MW in May. Avg Increase 74 MW.

## Slide 18: Summary
Following is a summary of the proposed Ancillary Service Methodology for 2021
  No change is being recommended to the methodology used for determining Responsive Reserve Service (RRS).
    Minimum RRS-PFR limit for 2021 is recommended to be changed based on updates to NERC’s BAL-003 Interconnection Frequency Response Obligation (IFRO) assessment for 2021. RRS table for 2021 will be updated to use the changed minimum RRS-PFR limit.
  One change is being recommended in each of the methodologies used for computing Non-Spin and Regulation reserves.
ERCOT is seeking TAC’s endorsement for the proposed 2021 Ancillary Service Methodology.

## Slide 19
Appendix

## Slide 20: RRS March
Notes: Trends between blue and red are fairly similar.
Max Change between blue and red in HE7-10 is 51 MW. On an average decrease of 36 MW
Max Change between red and gray in HE7-10 is 94 MW. On an average increase of 91 MW
Max Change between blue and gray in HE15-18 is 91 MW. On an average increase of 54 MW

## Slide 21: RRS June
Notes: Trends between blue and red are fairly similar.
Max Change between blue and red in HE3-6 is 109 MW. On an average increase of 48 MW
Max Change between red and gray in HE3-6 is 76 MW. On an average increase of 40 MW
Max Change between blue and gray in HE3-6 is 185 MW. On an average increase of 88 MW