## Slide 1
Phase Shifting Transformer Optimization in ERCOT Markets
Donald House
Supervisor, CRR
CMWG
December 17, 2020

## Slide 2: PST optimization in ERCOT markets
To better align with Day-Ahead Market (DAM) processes, ERCOT will start optimizing Phase Shifting Transformers (PSTs) in CRR Auctions in January 2021
  There are 9 active PSTs in ERCOT
This presentation will give a high level overview of how the CRR PST optimization will compare to the DAM and Real-Time Market
This is not intended to be a deep-dive discussion on the use of PSTs in ERCOT markets

## Slide 3: PST optimization in CRR Auctions
After this modification, all 9 PSTs will be optimized in a 2-part process during the auction run
  An initial run will be completed to reduce overloads where capacity is constrained by existing baseload and to set the starting PST angles
  During the auction optimization, PST angles may be moved throughout a range of +/- 30 degrees to minimize overloads on the binding constraints
  PST angles may vary for each month and TOU in the auction

## Slide 4: PST optimization in CRR Auctions
ERCOT started working on this modification after completing the framework upgrade in December 2018
  Last discussed with CMWG in September 2019
  A market notice was sent on 12/2/2020 to announce that CRR will begin optimizing PSTs
  Extensive testing completed by both the software vendor and ERCOT
    ERCOT used actual Production data to run the test auctions
    In general, test results show 1-2% increase in awarded MW and auction revenue
      However, some test auctions slightly decreased the MW awards and/or auction revenue
        So, optimizing PSTs does not guarantee increased awards

## Slide 5: PST optimization in CRR Auctions
ERCOT will not be posting the PST angles used in the auction optimization or any costs associated with moving the PSTs
  This is consistent with DAM
  A system change would be necessary to revise the auction results or DAM file postings to include this PST data
ERCOT will begin PST optimization with the following auctions and will optimize in all subsequent auctions:
  2021.FEB.Monthly.Auction (results to be posted 1/21/2021)
  2022.2nd6.AnnualAuction.Seq4 (results to be posted 2/4/2021)

## Slide 6: PST optimization in DAM
DAM also optimizes all 9 PSTs
PSTs may be moved through a full range of tap settings from 1-33, with 17 being neutral
  PST settings may vary for each hour of the Operating Day
  Negligible cost to move the PSTs

## Slide 7: PST optimization in Real-Time
Real-Time does not attempt to optimize PSTs in the same manner as CRR and DAM
ERCOT Transmission and Security procedures would activate a constraint first before studying to see if a PST can be moved to help relieve congestion
  Not all PSTs can be controlled remotely
  PSTs have a default value and can try to control MW flow to that value when they are in automatic mode
    Default values are set by the TDSP
    SCED assumes the tap settings are fixed at the telemetered value and does not try to move them

## Slide 8: PST optimization in ERCOT markets
Reminder that ERCOT will begin optimizing PSTs in CRR Auctions with the auctions run in January 2021
Questions about the PST optimization in CRR Auctions can be sent to ERCOTCRR@ercot.com