## Slide 1
Steve Reedy
Deputy Director, ERCOT IMM
sreedy@potomaceconomics.com
512-225-7139
CMWG
December 17, 2020

## Slide 2: Problem Statement – Current Transmission Demand “Curves”
Minimum of $2,000 shadow price cap for very small violations of post-contingency constraints:
  Can cause price oscillations in constraints with no effective helping resources
  Overvalues small violations
Maximum of $5,000 shadow price cap for very large violations of post-contingency constraints:
  Undervalues large violations.
  ERCOT implements out of market actions at ~125%, best to take all possible market actions before then.

## Slide 3: Proposed Improvement
All for post-contingency constraints
  BASECASE constraint shadow price cap to remain as-is at $9,251/MW
Constraint flow from 100%-102% - Shadow price cap set as curve, starting at $500/MW and increasing linearly to current shadow price cap (depends on voltage level and whether deemed irresolvable)
Flow 120%+ - Shadow price cap set at $9,251/MW

## Slide 4: Proposal - Example
Example for 345kV contingency constraint not deemed irresolvable:
Contingency constraint flow as a percentage of limit
Shadow price cap ($/MW)
100%
102%
120%
500
4,500
9,251
*not to scale