## Slide 1
Example for NPRR1057 Discussion
Pamela Shaw
ERCOT
WMS
January 6, 2021

## Slide 2: Introduction to the Revision Request
This Nodal Protocol Revision Request (NPRR) arose out of an outcome observed with the Panhandle Hub in October, where all Hub Buses within the Hub were de-energized for a portion of the 28th.
The goals are the NPRR are to:
  Change the Protocols and systems to include the Panhandle 345 kV and Lower Rio Grande Valley 138/345 kV Hubs in Section 6 of the Protocols where the calculation of Locational Marginal Prices (LMPs) for Hubs is discussed; and
  Eliminate unclear, redundant portions of Hub Real-Time Settlement Point Prices (SPPs) formulas.
Additional comments were also submitted to clarify how:
  Hub LMPs are used to determine Hub Real-Time SPPs; and
  The de-energized condition is managed for the ERCOT Hub 345kV Bus Average LMP.

## Slide 3: Example of Current and Proposed Outcomes
Case:
  Between the 11:20 am and 11:25 am execution of Security-Constrained Economic Dispatch (SCED), all of the Electrical Buses within the Hub become de-energized.
  With the Panhandle 345 kV not defined in the Section 6.6.1.5 formula, the LMP is set to $0/MWh when the all the Hub Buses are de-energized.
  The default for the Real-Time SPP calculation is only designed to address the condition when all the Hub Buses are de-energized for the entirety of the 15-minute Settlement Interval.
SCED Interval | LMP | Settlement Interval Ending | SPP
11:15 | $30/MWh | 11:30 | $20/MWh
11:20 | $30/MWh |  | 
11:25 | $0/MWh |  | 
11:30 | $0/MWh | 11:45 | $25/MWh *
11:35 | $0/MWh |  | 
11:40 | $0/MWh |  | 
* $25/MWh is the price for the ERCOT Hub 345kV Bus Average for the example
SCED Interval | LMP | Settlement Interval Ending | SPP
11:15 | $30/MWh | 11:30 | $28.33/MWh
11:20 | $30/MWh |  | 
11:25 | $25/MWh * |  | 
11:30 | $25/MWh * | 11:45 | $25/MWh *
11:35 | $25/MWh * |  | 
11:40 | $25/MWh * |  | 
Current
Proposed