## Slide 1
Annual TAC Review of the Market Impacts of Reliability Unit Commitments
Analysis of 2020
David Maggio
Technical Advisory Committee
ERCOT Public
January 27, 2021

## Slide 2: Protocol Language
5.8 Annual RUC Reporting Requirement
(1) ERCOT shall report to the Technical Advisory Committee (TAC), each January, an assessment of market impacts and Settlements for the aggregate Reliability Unit Commitment (RUC) activity, delineated by type of RUC instruction as follows:
RUC instructions issued for Ancillary Service shortages (failure to sufficiently procure one or more Ancillary Service markets in the Day-Ahead Market (DAM) or subsequent Supplemental Ancillary Service Markets (SASMs));
RUC instructions issued for irresolvable transmission system constraints;
RUC instructions issued in anticipation of extreme cold weather/startup failures;
RUC instructions issued for capacity;
RUC instructions issued for system inertia; and
A summary of RUC Settlements;
(i) RUC charges associated with RUC Make-Whole Amount Total per RUC, as defined in Section 5.7.4.1, RUC Capacity-Short Charge; and
(ii) RUC Shortfall Total, as defined in Section 5.7.4.1.1, Capacity Shortfall Ratio Share.

## Slide 3: RUC-Committed Resource-Hours in 2020
(*) - The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, partial hour instructions, or otherwise not dispatchable by SCED.
 | Total | Opt-Out | Non-Opt-Out
Instructed Resource-Hours |  |  | 
Total Count | 224 | 30 | 194
Effective Resource-Hours (*) |  |  | 
Total Count | 220.1 | 29.3 | 190.8
Average LSL | 180.0 | 120.3 | 189.1
Average LDL | 193.5 | 173.5 | 196.6
Average BP | 204.4 | 200.7 | 205.0
Average HSL | 296.7 | 265.7 | 301.4

## Slide 4: RUC Commitment Reasons
220.1 effective RUC resource-hours in 2020
  220.1 resource-hours (100%) for local thermal congestion or voltage concerns
There were no resource-hours of commitment for capacity concerns, Ancillary Service shortages, system inertia, or extreme cold weather/startup failures
29.3 effective resource-hours (13%) were successfully bought back
  This value is lower than last year (28% bought back in 2019)
  An additional 11.3 effective resource-hours (5% of total) were DAM committed

## Slide 5: RUC-Committed Effective Resource-Hours

## Slide 6: 2020 Highlights
183 effective RUC resource-hours (83% of annual total) were issued in late July and early August as a result of damage caused by Hurricane Hanna and associated transmission congestion.
  Several 138 kV lines and 69-kV lines experienced storm-related damage in the area and were forced out.
Commitments were for the XNED258:NEDIN_138H constraint (loss of one transformer at North Edinburg overloads the other transformer)
182 effective hours were issued to NEDIN_CC1 and 1 hour was issued to DUKE_CC1

## Slide 7: RUC-Committed Resources Dispatched above LDL
When Resources did not successfully opt out, there were 52.9 resource-hours when the Resource was dispatched above its LDL.
  For 0.8 of these resource-hours, the LMP for the RUC-instructed Resource was above the RUC offer floor.
  For 52.1 of these resource-hours, the LMP for the RUC-instructed Resource was below the RUC offer floor.
    For 41.3 of these resource-hours, the RUC-instructed Resource was mitigated.
    For 10.8 of these resource-hours, the RUC-instructed Resource was not mitigated and had been DAM committed, and the hours were treated as Opted Out.

## Slide 8: Reliability Deployment Price Adders
Month of 2020 | Total RTORDPA Time (Hours) | Time-weighted Average RTORDPA ($/MWh)
Jan | 2.9 | 0.07
Feb | 12.3 | 0.42
Mar | 0.6 | 3.07
Apr | 0.0 | 0.00
May | 0.0 | 0.00
Jun | 0.0 | 0.00
Jul | 21.0 | 0.39
Aug | 151.0 | 0.47
Sep | 1.8 | 0.63
Oct | 0.0 | 0.00
Nov | 3.0 | 0.62
Dec | 0.0 | 0.00

## Slide 9: RUC Make-Whole and Claw Back 2017 - 2020
** 2020- $404K in Make-Whole paid out. Only $0.25 was uplifted to Load.

## Slide 10: RUC-Related Improvements in 2020
NPRR970 Reliability Unit Commitment (RUC) Fuel Dispute Process Clarification, Implemented March 2020
NPRR856, Treatment of OFFQS Status is Day-Ahead Make Whole and RUC Settlements, Implemented May 2020
NPRR977, Create MIS Posting for RUC Cancellations, Implemented May 2020
NPRR884, Adjustments to Pricing and Settlement for Reliability Unit Commitments (RUCs) of On-Line Combined Cycle Generation Resources, Implemented May 2020
NPRR1019 Pricing and Settlement Changes for Switchable Generation Resources (SWGRs) Instructed to Switch to ERCOT, Partially implemented June 2020 (automation of offers will be delivered separately as part of a future project)

## Slide 11: Conclusions
In 2020, 224 instructed RUC resource-hours resulted in 220.1 effective RUC resource-hours.
  As compared to 228 and 201.7 for all of 2019, respectively
  13.3% of effective resource-hours were bought back
  83% of the annual total resource-hours were due to the damage caused by Hurricane Hanna and associated congestion.
The total RUC make-whole amount was ~$404K.
  Almost exclusively covered through capacity-short charges.
The total RUC claw back charge amount was ~$484K.

## Slide 12: Appendix

## Slide 13: RUC-Committed Effective Resource-Hours by Opt Out Status*
Month | 2017 | 2018 | 2019 | 2020
Jan | 7 | 46 | 0 | 3
Feb | 20 | 0 | 0 | 12
Mar | 14 | 0 | 8 | 1
Apr | 47 | 3 | 16 | 0
May | 33 | 333 | 59 | 0
Jun | 52 | 0 | 15 | 0
Jul | 39 | 0 | 0 | 21
Aug | 76 | 15 | 0 | 151
Sep | 54 | 4 | 8 | 0
Oct | 16 | 11 | 34 | 0
Nov | 8 | 50 | 4 | 3
Dec | 5 | 14 | 1 | 0
Month | 2017 | 2018 | 2019 | 2020
Jan | 2 | 0 | 0 | 0
Feb | 0 | 0 | 11 | 0
Mar | 0 | 0 | 0 | 0
Apr | 0 | 0 | 6 | 0
May | 20 | 40 | 13 | 6
Jun | 76 | 21 | 0 | 0
Jul | 27 | 4 | 0 | 11
Aug | 23 | 28 | 8 | 8
Sep | 12 | 16 | 19 | 0
Oct | 0 | 15 | 0 | 4
Nov | 3 | 12 | 0 | 0
Dec | 0 | 2 | 0 | 0
Did Not Opt Out
Opted Out
* Effective Hours rounded to nearest whole number

## Slide 14: RUC Make-Whole and Claw Back 2017-2018*
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2017 | 2018 | 2017 | 2018 | 2017 | 2018 | 2017 | 2018 | 2017 | 2018
Jan | 0.0 | -42 | 0 | 42 | 0 | 0 | 228 | 385 | 0 | 1202
Feb | -7 | 0 | 7 | 0 | 0 | 0 | 0 | 0 | 206 | 0
Mar | -79 | 0 | 79 | 0 | 0 | 0 | 0 | 0 | 471 | 0
Apr | -175 | 0 | 175 | 0 | 0 | 0 | 0 | 4 | 1387 | 0
May | -21 | -102 | 21 | 102 | 0 | 0 | 641 | 2372 | 209 | 2824
Jun | -40 | 0 | 40 | 0 | 0 | 0 | 163 | 0 | 491 | 0
Jul | -57 | 0 | 57 | 0 | 0 | 0 | 6 | 0 | 620 | 0
Aug | -121 | -35 | 121 | 35 | 0 | 0 | 15 | 1 | 870 | 523
Sep | -25 | -24 | 25 | 24 | 0 | 0 | 79 | 0 | 755 | 206
Oct | -4 | -24 | 4 | 24 | 0 | 0 | 47 | 213 | 159 | 535
Nov | -10 | -381 | 10 | 381 | 0 | 0 | 25 | 79 | 149 | 977
Dec | -2 | 0 | 0 | 0 | 0 | 0 | 0 | 20 | 77 | 0
* Amounts rounded to nearest thousand. Data from most recent settlement run as of 01/07/2021.

## Slide 15: RUC Make-Whole and Claw Back 2019-2020*
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2019 | 2020 | 2019 | 2020 | 2019 | 2020 | 2019 | 2020 | 2019 | 2020
Jan | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 0 | 0
Feb | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 168 | 0 | 394
Mar | -9 | 0 | 9 | 0 | 0 | 0 | 0 | 19 | 253 | 0
Apr | -8 | 0 | 8 | 0 | 0 | 0 | 0 | 0 | 359 | 0
May | -13 | 0 | 13 | 0 | 0 | 0 | 108 | 0 | 915 | 0
Jun | -4 | 0 | 4 | 0 | 0 | 0 | 3 | 0 | 738 | 0
Jul | 0 | -40 | 0 | 40 | 0 | 0 | 0 | 82 | 0 | 148
Aug | 0 | -356 | 0 | 356 | 0 | 0 | 0 | 210 | 0 | 2197
Sep | -11 | 0 | 11 | 0 | 0 | 0 | 1 | 0 | 110 | 0
Oct | -3 | 0 | 3 | 0 | 0 | 0 | 726 | 0 | 229 | 0
Nov | 0 | -8 | 0 | 8 | 0 | 0 | 49 | 0 | 0 | 140
Dec | 0 | 0 | 0 | 0 | 0 | 0 | 15 | 0 | 0 | 0
* Amounts rounded to nearest thousand. Data from most recent settlement run as of 01/07/2021.