## Slide 1
2020 Analysis of REP and NOIE Demand Response
Carl L Raish
Principal Load Profiling and Modeling
Retail Market Subcommittee – February 2, 2021

## Slide 2: Overview
  Summer 2020 Analysis Update
  Total System-level Demand Response
    Re-constituted ERCOT Load
    Responding NOIE and ESIID counts
  Price Response and Retail DR Participation Trends
  DR/PR Category details
    4CP Response
    Real Time Pricing (IRT)
    Day-Ahead Pricing (IDA)
    NOIE Price Response
    Peak Rebate (PR)
    Other Direct Load Control (OLC)
    Time of Use (TOU)
    Free Days/Hours (FDH)

## Slide 3: Summer 2020 Analysis Update
  Covid impacts on baseline development.
    Limited use of Regression Baseline to Residential and NOIE loads
    Competitive Non-Residential ESIIDs used Mid-8-of-10, Nearest 20, and Meter-before-meter-after baselines
  Hurricane Hannah
    Substation level analysis indicated impacts in South Weather Zone
    Identified specific ESIIDs with load impacts
    Excluded interval data for these ESIIDs/days from analysis
      Baselines
      Actuals

## Slide 4
Total System-Level Demand Response

## Slide 5: Load Reductions by Category/System Level
HE 17:00 MW Reductions
Total System DR: Amount of reduction with no double counting:
1. For an ESIID participating in more than one category
2. For a NOIE classified as responding to both price and 4CP

## Slide 6: ESIIDs/NOIEs by Category/System Level
HE 17:00 ESIIDs/NOIEs with Reductions
Total System DR: Amount of reduction with no double counting:
1. For an ESIID participating in more than one category
2. For a NOIE classified as responding to both price and 4CP

## Slide 7: Responding ESIIDs and Reductions

## Slide 8: Responding NOIEs and Reductions

## Slide 9
Actual ERCOT Total Load
+
Total System DR
Summer 2020

## Slide 10: Total System Demand Response

## Slide 11: Total System Demand Response

## Slide 12: Total System Demand Response

## Slide 13: Total System Demand Response

## Slide 14: Total System Demand Response

## Slide 15
Price Response and Retail DR Participation Trends

## Slide 16: 4CP Response Trend
Red Arrows: HE17 Price > $1,000 Black Arrows: HE17 Price > $500
2014
2015
2016
2017
2020
2019

## Slide 17: 4CP Response Trend

## Slide 18: REP Demand Response Participation Trends

## Slide 19: NOIE Demand Response Participation Trends

## Slide 20
DR/PR Category Details

## Slide 21: 4CP/NearCP Events 2020
4CP Days
NearCP Days
Date | ESIIDs | NOIEs | HE 17 Reduce MW
8-Jun | 3,711 | 20 | 1,880
13-Jul | 3,429 | 19 | 2,765
13-Aug | 3,691 | 20 | 2,416
1-Sep | 5,200 | 20 | 2,803
Date | ESIIDs | NOIEs | HE 17 Reduce MW
5-Jun | 3,771 | 12 | 912
9-Jun | 4,812 | 18 | 1,961
1-Jul | 3,691 | 20 | 1,148
2-Jul | 3,940 | 10 | 1,472
8-Jul | 2,542 | 8 | 722
9-Jul | 2,934 | 13 | 1,135
10-Jul | 3,455 | 12 | 1,324
14-Jul | 2,863 | 18 | 1,399
6-Aug | 2,837 | 13 | 1,495
7-Aug | 3,462 | 13 | 1,479
10-Aug | 3,783 | 18 | 1,642
11-Aug | 3,754 | 20 | 1,980
12-Aug | 3,690 | 19 | 2,358
14-Aug | 3,804 | 21 | 2,590
28-Aug | 3,432 | 17 | 2,275
 | Residential | Non-Residential
4CP Incentive | 0 | 202
4CP Advise/ Control | 79,154 | 1,356
NOIE Participation

## Slide 22: Indexed Real-Time ESIID Participation
Indexed Real-Time - 20,424 Residential ESIIDs for 2020
  In 2019 they were reported as:
    BI – 129
    RTP – 6,879
    Peak Rebate – 2,032
    TOU - 228
    Not reported – 11,156
Indexed Real-Time - 82,991 Non-Residential ESIIDs for 2020
  In 2019 they were reported as:
    BI – 44,469
    RTP– 13,507
    Peak Rebate – 85
    Not reported – 24,930

## Slide 23: Indexed Real-Time High Price Events 2020
Date | ESIIDs | Max Reduce MW | Avg Reduce MW | Avg Price $/MWh
4-Aug | 5,117 | 80 | 38 | $504
5-Aug | 5,377 | 91 | 75 | $764
6-Aug | 5,488 | 78 | 76 | $429
7-Aug | 5,831 | 92 | 69 | $386
10-Aug | 5,416 | 106 | 104 | $705
14-Aug | 42,374 | 686 | 463 | $616
28-Aug | 35,720 | 314 | 290 | $298
31-Aug | 45,653 | 351 | 281 | $909
1-Sep | 6,266 | 63 | 54 | $870

## Slide 24: Indexed Day- Ahead ESIID Participation
Indexed Day-Ahead - 22 Residential ESIIDs for 2020
  In 2019 they were reported as:
    RTP – 1
    TOU - 1
    Not reported – 20
Indexed Day-Ahead - 915 Non-Residential ESIIDs for 2020
  In 2019 they were reported as:
    BI – 102
    RTP– 46
    Peak Rebate – 1
    Not reported – 766

## Slide 25: Indexed Day-Ahead High Price Events 2020
Date | ESIIDs | Max Reduce MW | Avg Reduce MW | Avg Price $/MWh
High DA Only |  |  |  | 
8-Jun | 399 | 7 | 6 | $261
13-Aug | 381 | 12 | 11 | $560
High DA and RT |  |  |  | 
14-Aug | 368 | 10 | 4 | $1,233
High RT Only |  |  |  | 
28-Aug | 326 | 9 | 8 | $298
31-Aug | 422 | 3 | 1 | $912
1-Sep | 6,266 | 63 | 54 | $870

## Slide 26: Indexed Pricing Combined ESIID Participation
Business
Residential
2014 – 2019 BI + RTP 2020 IRT + IDA

## Slide 27: NOIE Price Response
NOIEs did report participation in IRT and also used other categories to respond to price.
Category | Residential | Non-Residential
Conservation Voltage Reduction | 575,926 | 45,939
Indexed Real-Time | 0 | 3
Other Direct Load Control | 206,533 | 3,585
Other | 303,385 | 0
Peak Rebate | 905 | 1,283
Time-of-Use | 1,872 | 1,077
Total (unique) | 973,656 | 47,349

## Slide 28: NOIE High Price Events
Date | NOIEs | Max Reduce MW | Avg Reduce MW | Avg Price $/MWh
27-Jul | 4 | 103 | 64 | $298
31-Jul | 5 | 138 | 66 | $455
3-Aug | 2 | 52 | 29 | $627
4-Aug | 3 | 104 | 85 | $764
5-Aug | 4 | 78 | 58 | $504
6-Aug | 5 | 154 | 146 | $429
7-Aug | 6 | 163 | 105 | $386
10-Aug | 4 | 79 | 73 | $705
14-Aug | 17 | 1,175 | 855 | $615
28-Aug | 6 | 160 | 140 | $301
14-Aug | 17 | 896 | 641 | $844
1-Sep | 6 | 305 | 273 | $870

## Slide 29: Direct Load Control ESIID Participation
Business
Residential

## Slide 30: Direct Load Control Events
Many other summer events … most had relatively small aggregate reductions
Date | ESIIDs | HE 17 Reduce MW | Max Reduce MW | Avg Reduce MW | Avg Price $/MWh
14-Aug | 6,375 | 34 | 40 | 21 | $616
28-Aug | 2,817 | 32 | 32 | 18 | $298
31-Aug | 3,148 | 32 | 37 | 21 | $1,053
1-Sep | 111 | 40 | 24 | 17 | $870

## Slide 31: Peak Rebate ESIID Participation
Business
Residential

## Slide 32: Peak Rebate Events - 2020
Date | ESIIDs | HE 17 Reduce MW | Max Reduce MW | Avg Reduce MW | Avg Price $/MWh
5-Jun | 5,658 | 19.2 | 20.2 | 13.9 | -
1-Sep | 3 | 0.1 | 0.2 | 0.0 | $870

## Slide 33: TOU ESIID Participation
Business
Residential

## Slide 34: Free Days/Hours ESIID Participation
Free Days/Hours 467,671 Residential ESIIDs for 2020
  In 2019 they were reported as:
    TOU - 256,598
    TOU/Peak Rebate – 4,917
    OLC – 58
    OLC/TOU - 325
    Peak Rebate – 12,876
    RTP – 341
    Not reported – 192,556
Free Days/Hours 984 Non-Residential ESIIDs for 2020
  In 2019 they were reported as:
    TOU – 626
    TOU/Peak Rebate– 4
    Peak Rebate – 4
    Not reported - 350

## Slide 35: Questions?
ON
OFF
craish@ercot.com 512/248-3876