## Slide 1
BTM Dispatch and Pricing
Wholesale Market Working Group
Dan Jones
2/18/2021

## Slide 2: Example Description
EPS Meter
(POI)
G1 Gross HSL = 10 MW
G1 Gross LSL = 0 MW
G1 Cost/Offer = $30/MWh
L1 = 30 MW (flat)
L1 is operationally independent of G1, but in same QSE
Current Rules
  Registration as a PUN is not required to allow for netting of BTM Gen and Load
  Netting is applicable in Operations and in Settlement
  Load that is netted against BTM gen is not “ERCOT Load” in Operations or in Settlement
  Net Gen @ POI settled at the nodal price; Net Load @ POI settled at the load zone price
  G1 is self-dispatched up to the quantity of BTM Load
  G1 is ERCOT-dispatched for quantities exceeding BTM Load
G1
L1

## Slide 3: Scenario 1
Load = 30 MW
Gen output = 10 MW
Netting In Operations and Settlement
(Current Rules)
RN = $10
LZ = $75
Load = 30 MW
Gen output = 0 MW
No Netting In Operations, but Netted in Settlement
(Not Current Rules)
RN = $10
LZ = $75
Incentive to self-dispatch G1 to 10 MW
Inefficient self-dispatch of G1 relative to its cost/offer ($30) and the nodal price ($10) due to G1 effectively settling at LZ price ($75) up to L1 MW
No self-dispatch of G1
G1 is efficiently dispatched at 0 MW by ERCOT relative to its cost/offer ($30) and the nodal price ($10)
ERCOT Dispatch and Settlement of G1/L1 are not aligned
  G1 incentive is to produce 10 MW, which is inconsistent with its cost/offer ($30) relative to the nodal price ($10) and inconsistent with its Basepoint of 0 MW

## Slide 4: Scenario 2
Netting In Operations and Settlement
(Current Rules)
RN = $75
LZ = $10
No Netting In Operations, but Netted in Settlement
(Not Current Rules)
RN = $75
LZ = $10
Incentive to self-dispatch G1 to 0 MW
Inefficient self-dispatch of G1 relative to its cost/offer ($30) and the nodal price ($75) due to G1 effectively settling at LZ price ($10) up to L1 MW
No self-dispatch of G1
G1 is efficiently dispatched at 10 MW by ERCOT relative to its cost/offer ($30) and the nodal price ($75)
ERCOT Dispatch and Settlement of G1/L1 are not aligned
  G1 incentive is to produce 0 MW, which is inconsistent with its cost/offer ($30) relative to the nodal price ($75) and inconsistent with its Basepoint of 100 MW
Load = 30 MW
Gen output = 0MW
Load = 30 MW
Gen output = 10 MW

## Slide 5: “ERCOT Load” Differences
ERCOT RT Load is equal to the sum of telemetered Generation Resource Net MW minus DC Tie Flows (where + = DC Export; - = DC Import)
In the case of “Netting in Operations and Settlement (Current Rules)” the example above will contribute 0 MW to ERCOT RT Load and 0 MW to ERCOT Settlement Load
In the case of “No Netting in Operations, but Netted in Settlement (Not Current Rules),” the example above will contribute 100 MW to ERCOT RT Load and 0 MW to ERCOT Settlement Load
Load = 100MW
Gen output = 100MW