## Slide 1
2021 February Winter Event Analysis of Load Reductions
Carl L Raish
Principal Load Profiling and Modeling
Retail Market Subcommittee – April 14, 2021

## Slide 2: Overview
Initially targeted TDSP controlled outages considering substations they reported to PUCT
Shifted to include ESIIDs with storm-related outages – many ESIIDs had outages prior to the load shedding and were subject to TDSP load shed as well
Analysis targeted ESIIDs identified with outages as well as ESIIDs
  Deployed for ERS
  Containing Load Resources deployed for RRS
  Previously Identified as on Indexed pricing (Day-Ahead/Real-Time) and/or 4CP responders
  Other ESIIDs identified as responding during the event
  4 million deployed ESIIDs to analyze (3.8 million Residential, 468,000 Non-Residentia
Developed algorithms to identify outage ESIIDs and control group ESIIDS
  Algorithms varied across the load type
  Based on number of zero intervals (15-min) Feb 1 – Feb 4
  Outage ESIID - lots of zeros on Feb 15 – 19 compared to earlier days
  Control group ESIID – small number of zeros throughout
  Some ESIIDs were neither
  Examined interval data for every ESIID (~8 million)

## Slide 3: Overview
Goal was to analyze load response for all 28 days in February to capture anything happening before, during and after the event.
Performed analysis generally in categories of Profile Type
  Created two new ones for analysis, not necessarily reporting, purposes
  ‘LOWUSE’ for ESIIDs with very low usage (< 2 KWh per day)
  ‘LIGHT’ for ESIIDs with > 75% night-time use
  Note: excluded ESIIDs with ‘DG’ and ‘WD’ profile types, ESIIDs with zero use for most days prior to the event
  Also have not yet started analysis of NOIE load reductions
Baselines developed for all ‘deployed’ ESIIDs:
  ‘Control’ groups for Residential and smaller Business ESIIDs
  Used ‘near-day’ baselines for large Business (subject to 4CP billing)
  Used ‘near-day’ baselines for Business Load Factor ESIIDs (not subject to 4CP billing) for which sufficiently similar ESIIDs were not found
    Peak demands for these ESIIDs range from 5/10 KW to 700 KW
  MAPE: Residential 1%, Business 0.5% (based on days with no reductions)

## Slide 4: Competitive Residential ESIIDs with Zero Load for Hour
HI/LO WR
‘Lighting’
PV
Low Use
Max - 3.3 million Residential ESIIDs across the four types

## Slide 5: Competitive Business ESIIDs with Zero Load for Hour
Transmission
Distribution 4CP
Distribution Non-4CP
Non-demand
Max – 477,000 Business ESIIDs across six types
(PV and OG-FLT not shown)

## Slide 6: Competitive Res Plus Bus Load Reductions

## Slide 7: Daily Load Reductions Feb 14 – 20, 2021
Event Day | Max Reduce Interval | Max Reduce MW | Min Reduce Interval | Min Reduce MW | Average Day Reduce MW
2/14/2021 | 96 | 4,276 | 1 | 2,360 | 3,094
2/15/2021 | 80 | 22,460 | 1 | 5,013 | 18,070
2/16/2021 | 34 | 22,487 | 96 | 14,818 | 18,578
2/17/2021 | 36 | 16,477 | 95 | 8,224 | 13,101
2/18/2021 | 31 | 9,382 | 2 | 7,626 | 8,327
2/19/2021 | 32 | 8,640 | 96 | 5,848 | 7,313
2/20/2021 | 33 | 6,036 | 95 | 4,280 | 5,327
Total Competitive Residential Plus Business Load Reductions

## Slide 8: Daily Load Reductions Feb 14 – 20, 2021
Event Day | Max Reduce Interval | Max Reduce MW | Min Reduce Interval | Min Reduce MW | Average Day Reduce MW
2/14/2021 | 96 | 3,763 | 1 | 2,242 | 2,886
2/15/2021 | 80 | 11,600 | 1 | 4,202 | 10,134
2/16/2021 | 40 | 12,308 | 96 | 9,910 | 10,983
2/17/2021 | 38 | 10,792 | 95 | 7,658 | 9,570
2/18/2021 | 32 | 8,265 | 96 | 7,180 | 7,730
2/19/2021 | 32 | 7,716 | 96 | 5,685 | 6,879
2/20/2021 | 6 | 5,659 | 95 | 4,427 | 5,206
Total Competitive Business Load Reductions

## Slide 9: Daily Load Reductions Feb 14 – 20, 2021
Event Day | Max Reduce Interval | Max Reduce MW | Min Reduce Interval | Min Reduce MW | Average Day Reduce MW
2/14/2021 | 96 | 512 | 15 | 92 | 209
2/15/2021 | 79 | 10,883 | 1 | 811 | 7,936
2/16/2021 | 33 | 10,214 | 96 | 4,908 | 7,595
2/17/2021 | 36 | 5,719 | 95 | 566 | 3,531
2/18/2021 | 31 | 1,126 | 3 | 211 | 597
2/19/2021 | 32 | 923 | 75 | 58 | 434
2/20/2021 | 29 | 404 | 64 | - | 237
Total Competitive Residential Load Reductions

## Slide 10: Residential Load Mildest Weekday Before Event
Day Weighted Average Dry Bulb 60.5°
Hourly Peak Total Plus Reduce 10,526 MW – 1.4 KW per ESIID

## Slide 11: Residential Load Coldest Weekday Before Event
Day Weighted Average Dry Bulb 32.5°
Hourly Peak Total Plus Reduce 19,591 MW – 2.6 KW per ESIID

## Slide 12: Residential Load Sunday Before Event
Day Weighted Average Dry Bulb 22.4°
Hourly Peak Total Plus Reduce 26,324 MW – 3.5 KW per ESIID

## Slide 13: Residential Load First Day of Event
Day Weighted Average Dry Bulb 13.4°
Hourly Peak Total Plus Reduce 27,418 MW – 3.7 KW per ESIID
264% of mildest day peak … 2.34 KW per ESIID increase

## Slide 14: Residential Load Second Day of Event
Day Weighted Average Dry Bulb 17.6°
Hourly Peak Total Plus Reduce 26,304 MW – 3.5 KW per ESIID

## Slide 15: Residential Load Third Day of Event
Day Weighted Average Dry Bulb 28.0°
Hourly Peak Total Plus Reduce 21,615 MW – 2.9 KW per ESIID

## Slide 16: Residential Load Fourth Day of Event
Day Weighted Average Dry Bulb 27.7°
Hourly Peak Total Plus Reduce 21,395 MW – 2.8 KW per ESIID

## Slide 17: Residential Load Last Day of Event
Day Weighted Average Dry Bulb 30.4°
Hourly Peak Total Plus Reduce 22,019 MW – 2.9 KW per ESIID

## Slide 18: Residential Load Saturday After Event
Day Weighted Average Dry Bulb 41.7°
Hourly Peak Total Plus Reduce 18,150 MW – 2.4 KW per ESIID

## Slide 19: Business Load Mildest Weekday Before Event
Day Weighted Average Dry Bulb 60.5°
Hourly Peak Total Plus Reduce 26,607 MW – 26.4 KW per ESIID
No high prices

## Slide 20: Business Load Coldest Weekday Before Event
Day Weighted Average Dry Bulb 32.5°
Hourly Peak Total Plus Reduce 23,615 MW – 23.4 KW per ESIID …89% of mildest day peak
Price response started ~500 MW, … 6 KW per ESIID decrease
High prices started 08:30 and averaged $1,130 / MWh through the rest of the day

## Slide 21: Business Load Sunday Before Event
Day Weighted Average Dry Bulb 22.4°
Hourly Peak Total Plus Reduce 21,849 MW – 21.6 KW per ESIID
Price response increased steadily to ~4,000 MW by midnight
High prices started day at $1,200 / MWh and increased to cap around 22:45

## Slide 22: Business Load First Day of Event
Day Weighted Average Dry Bulb 13.4°
Hourly Peak Total Plus Reduce 23,455 MW – 23.2 KW per ESIID
88% of mildest day peak … 3.2 KW per ESIID decrease
Price and other response grew to ~12,000 MW during the day
High prices all day with oscillations from $1,600 - $9,000

## Slide 23: Business Load Second Day of Event
Day Weighted Average Dry Bulb 17.6°
Hourly Peak Total Plus Reduce 23,480 MW – 22.5 KW per ESIID
88% of mildest day peak … 3.9 KW per ESIID decrease
Price and other response ~12,000 MW during the day
Prices high all day - averaged $9,007

## Slide 24: Business Load Third Day of Event
Day Weighted Average Dry Bulb 28.0°
Hourly Peak Total Plus Reduce 22,494 MW – 22.3 KW per ESIID
84% of mildest day peak … 4.1 KW per ESIID decrease
Price and other response fell off to ~8,000 MW during the day
Prices high all day - averaged $9,000

## Slide 25: Business Load Fourth Day of Event
Day Weighted Average Dry Bulb 27.7°
Hourly Peak Total Plus Reduce 22,920 MW – 22.7 KW per ESIID
86% of mildest day peak … 3.7 KW per ESIID decrease
Price and other response leveled off at ~8,000 MW during the day
Prices high all day - averaged $9,015

## Slide 26: Business Load Last Day of Event
Day Weighted Average Dry Bulb 30.4°
Hourly Peak Total Plus Reduce 23,217 MW – 23.0 KW per ESIID
87% of mildest day peak … 3.4 KW per ESIID decrease
Price and other response started falling off from 8,000 MW at the beginning of the day to 6,000 MW by the end of the day
Prices averaged $8,994 until 09:00 and were back to normal at 09:30

## Slide 27: Business Load Saturday After Event
Day Weighted Average Dry Bulb 41.7°
Hourly Peak Total Plus Reduce 21,147 MW – 20.9 KW per ESIID
79% of mildest day peak … 5.5 KW per ESIID decrease
Remaining response decreased slowly all day to about 4,400 MW
No high prices all day long

## Slide 28: Business Load Saturday After Event
Day Weighted Average Dry Bulb 64.3°
For Feb 21 – 28 load reductions decrease from 4,400 MW to about 800 MW at the end of the month.
No high prices all day long

## Slide 29: Next Steps
NOIE Load response
Response from ESIIDs
  Deployed for ERS
  Deployed as Load Resources providing RRS
  Price Response (including 4CP responders)
Settlement Only Generators/Puns
Additional Subgroup break outs e.g. by Weather Zones, TDSP, etc (feedback please)

## Slide 30: Questions?
ON
OFF
craish@ercot.com 512/248-3876