## Slide 1
PG6.9 Generators in FIS stability study
Yang Zhang
ERCOT
RIWG Meeting
April 20, 2021

## Slide 2: PG6.9 Generators in FIS stability study
It is observed that some FIS stability studies turned off generators in the study area that met PG6.9 if their CODs are after the COD of the generator being studied.
PG 5.4.5 (2) requires that all operational and planned Generation Resources which have met the requirements of Section 6.9 in the area of the study shall be dispatched at full net output in at least one of the scenarios/cases evaluated by the lead TSP.

## Slide 3: PG6.9 Generators in FIS stability study
Generators should not be excluded based on COD:
  It’s very common that projects CODs change multiple times before the commissioning.
  A project is impacted by stability constraints caused by all generators in the region, regardless of their CODs.
  Excluding projects based on COD may create a situation where two projects that impact each other may never be studied together in an FIS:
    Project A finished FIS in 2020 with a COD 2023
    Project B filed FIS request in 2021 with a COD 2022

## Slide 4: PG6.9 Generators in FIS stability study
Conclusion:
  Generators modeled in the DWG cases should not be turned off, regardless of their CODs.
  Planned generators that met PG6.9 after the DWG cases being published should be modeled in the study cases if they are in the study area.
  Per PG 5.4.5 (2), if any generators in the study area are not dispatched at full output, the study report shall include the technical rationale.

## Slide 5
QUESTIONS?