## Slide 1
WMWG
May 17, 2021
Balancing Operations Planning Staff
Update on Intra-Hour Solar Forecast and SCR811

## Slide 2
Discussion Outline
Intra-Hour Solar Forecast Performance Update
Next Steps

## Slide 3: Predicted Solar Ramp Error Update
Chart: Histogram of PSSR Error (MW/5min)
| -9999 to -300 | -300 to -250 | -250 to -200 | -200 to -150 | -150 to -100 | -100 to -50 | -50 to 0 | 0 to 50 | 50 to 100 | 100 to 150 | 150 to 200 | 200 to 250 | 250 to 300 | 300 to 9999
Persistence | 48 | 54 | 89 | 115 | 154 | 282 | 748 | 875 | 315 | 186 | 111 | 79 | 43 | 47
Intra-Hour Solar Forecast | 18 | 16 | 46 | 73 | 149 | 348 | 962 | 874 | 331 | 158 | 86 | 44 | 23 | 18
STPPF | 18 | 15 | 30 | 77 | 171 | 350 | 809 | 1037 | 366 | 146 | 77 | 32 | 12 | 6
Performance Metric | Persistence (4/23 – 5/10) | Intra-Hour Solar Forecast (4/23 – 5/10) | Short-term Solar Forecast (STPPF) (4/23 – 5/10)
MAE (MW) | 79.29 | 60.12 | 57.60
MAE (MW) when 5-Min. Solar Ramp > 100 MW | 190.12 | 114.38 | 105.64
MAE (MW) when 5-Min. Solar Ramp < -100 MW | 195.40 | 109.68 | 113.03
Over Forecast
Under Forecast

## Slide 4: K8 and Max PSRR Threshold in GTBD
  - K8*5*Predicted Solar Ramp Rate (Using STPPF/IHPPF)
|PSRR| ≤ Max PSRR Threshold
Implementation of SCR811
- K8 *5* PSRR
Notes: 3/12/18 – Integral ACE Time Constant Changed from 60 min to 45 min
5/17/18 – K4 Changed from 0.3 to 0.2 and K5 Changed from 0.4 to 0.5
12/4/18 – 10:05 AM – K6 Changed from 0 to 0.5
2/12/19 – 2:15 PM – K6 changed from 0.5 to 1.0
3/12/19 – 2:10 PM – PWRR Threshold from 10 to 15 MW/min
3/19/19 – 2:15 PM – PWRR Threshold from 15 to 20 MW/min
4/01/19 – 10:00 AM – K5 changed from 0.5 to 0.4 and Max. Integral ACE Feedback changed from 250 to 150
4/24/19 – 1:15 PM – Max. Integral ACE Feedback changed from 150 to 160. PWRR Threshold changed from 20 to 25.
5/22/19 – 1:10 PM – K5 changed from 0.4 to 0.5, Max Integral ACE feedback changed from 160 to 200, PWRR Threshold changed from 25 to 30
6/17/20 – 10 AM - PWRR Calculation method changed from Direct to Interpolated
9/1/20 – 11 AM - Max Integral ACE Feedback changed from 200 to 250
9/3/20 – 3 PM - Max Integral ACE Feedback changed from 250 to 300
9/4/20 – 3 PM - Max Integral ACE Feedback changed from 300 to 250

## Slide 5: Next Steps
ERCOT will implement SCR811 during 2021 R3 between May 25 and May 27.
Initially, K8 will be set to 0 so that it will not impact GTBD calculation.
ERCOT is planning to tune K8 (K8 becomes non-zero) and potentially other GTBD parameters in the first week of June.
A market notice will be sent out prior to activation of K8 to a non-zero value.