## Slide 1: Issues Related to NPRR1080 on Capping AS Prices
Shams Siddiqi, Ph.D.
Representing Hunt Energy Network
(512) 619-3532
shams@crescentpower.net
TAC Meeting
June 23, 2021
Notes: <number>

## Slide 2: Reg/RRS: Critical Reliability Service
June 23, 2021
<number>
The rapid decay of frequency on 2/15/21 during Winter Storm Uri pointed to the critical reliability role of Responsive Reserve Service (RRS).
ERCOT grid was minutes away or a single large generator trip away from possible total blackout.
Operating Reserve Demand Curve (ORDC) is determined assuming 1 MW more of an Ancillary Service procured will result in 1 MW of avoided load lost at Value of Lost Load (VOLL) times the Loss of Load Probability (LOLP).
However, insufficient RRS to arrest frequency can result in total blackout of the grid – the unfathomable cost of a blackout is potentially the loss of thousands of lives, hundreds of thousands of MWh (depending on unknown time to recover from a blackout), and billions of dollars of economic impact.
Thus, the value of RRS is LOLP times many multiples of VOLL.
The goal of reserving enough RRS at all times to be able to arrest frequency decay resulting from the sudden loss of the two largest nuclear units makes sense.
RRS should only be deployed by frequency deviations and not released to SCED.
Notes: <number>

## Slide 3: ASPFs below SWCAP v MCPC cap
June 23, 2021
<number>
Setting RRS penalty factor at SWCAP minus $0.01 would result in DAM awarding Resources energy offers in preference to RRS awards leading to RRS insufficiency and subsequent RRS assignment.
AS assignment to a Resource that was awarded energy in DAM may cause financial harm - Protocols currently have no means of making that Resource whole.
If we modify the Protocols to allow for recovery of such financial harm, then there will be a resulting uplift charge.
Having ASPFs for Reg & RRS above SWCAP and capping AS prices at SWCAP would award Reg & RRS instead of energy in DAM.
Resource awarded RRS in DAM may have “opportunity cost” higher than SWCAP as calculated within the DAM engine – however, by design, there would be no payment above SWCAP.
This treatment is similar to the capping of energy at SWCAP under RTC where energy prices would otherwise possibly reach $11,000/MWh.
Under NPRR1080, Resources would be awarded financial energy positions in favor of essential reliability products and may incur actual financial harm whereas capping AS prices awards reliability products over energy.
Notes: <number>

## Slide 4: TAC Action Requested
June 23, 2021
<number>
While we support moving forward with NPRR1080 and OBDRR030 as an immediate step to addressing the issue of Ancillary Service prices exceeding SWCAP, we urge TAC to urgently direct ROS and WMS to investigate the following items:
Modifying RRS deployment Protocols to eliminate release to SCED thereby making RRS a purely frequency responsive service.
Modifying emergency procedures to ensure adequate RRS is maintained and restored after deployment in response to frequency events.
Setting the ASPFs for RRS and Regulation Service in the DAM at high enough values to ensure those essential reliability products are procured to the fullest extent possible prior to awarding financial energy positions. MCPCs would be capped at SWCAP.
Under RTC, modifying Ancillary Service Demand Curves (ASDCs) for RRS and Regulation Service to higher values than SWCAP and Power Balance Penalty Factor at SWCAP and capping MCPCs at SWCAP. This will ensure RRS and Regulation Service are maintained to the extent possible in order to arrest frequency decay. There is more time to address this issue than the urgent issues list above.
Notes: <number>