## Slide 1
Transient Security Assessment Tool (TSAT) Data Requirement Update
Mehdi Daryabak
July 8, 2021
ROS Meeting

## Slide 2: RRGRR021 TSAT Requirement (1)
All existing and new Generation Resources (qualifying for QSA) are required to submit TSAT UDMs by November 1, 2021
The dynamic model template serves as the vehicle for submitting dynamic models (both PSS/E and TSAT). The template supersedes the need to submit loose dyr files. In order for the same template to work for both software platforms, TSAT models should be designed to interoperate with PSS/E dyr files
If using a Conventional Synchronous or Generic Renewable template, no additional TSAT files are required as the models should automatically translate
If submitting a model that is a User-Defined Model (UDM) (as opposed to a generic or conventional model), then additional .dll and .tudm files are generally required

## Slide 3: RRGRR021 TSAT Requirement (2)
User-defined models should not use integration time step in the .dyr, .dll, or .tudm files. If a UDM needs step-size, Powertech Labs (TSAT developer) provides API (DLB_GETVAR) to developers for getting this parameter from the engine instead of hard-coding it into the dynamic files.
The .tudm and .dll files must only include the structure of the model and not any project-specific information

## Slide 4: RRGRR021 TSAT Update
Since last update (June 03, 2021), we have received one updated TSAT UDM model.
The v4.5 GE UDM (GEWTG2 model) is available in TSAT library for TSAT version 20.0.67 (or any later version). There are many instances of this model in the ERCOT network.
Powertech Labs is expected to release the TSAT v21 in July 2021. The TSAT v21 is the version that ERCOT will be switching to when it is released.

## Slide 5: RRGRR021 TSAT Update
REs should work with their OEM to make sure the OEM is developing the same exact model as the PSSE UDM. Some OEMs are only developing selected models. It is RE’s responsibility to follow up and make sure their specific models are being developed.
If TSAT UDM cannot be obtained or developed, switching to generic models for both PSSE and TSAT is one option.
If a RE has decided to switch to generic model instead of a UDM, please let us know so we can keep track of what UDMs are not going to be developed.

## Slide 6
Questions?