## Slide 1: AS Assignment
7/12/2021 WMWG

## Slide 2: AS Assignment
What is it:
ERCOT tells a generator that it will carry x MW of a type of AS service.
Does the generator receive a capacity payment:
No: AS assigned does NOT receive a capacity payment.
Generators that sell AS in the DA market receive a capacity payment. The AS offer can include the lost opportunity cost of energy prices, the risk of providing AS, and the wear and tear of moving the unit.

## Slide 3: AS Assignment
If the unit does not receive a capacity payment, how does it get compensated for holding back reserves:
It doesn’t fully get compensated.
Of the 3 RT components (LMP + ORDC + RDPA), a unit only receives LMP for URS, RRS, deployed NSRS, and undeployed DRS.
And what about combined cycles with NFRC range:
If providing RRS or regulation, a CC has to back down the range of AS plus the NFRC range. The NFRC range would get paid ORDC+RDPA, but would not receive LMP.

## Slide 4: AS Assignment
What is needed:
Protocol language to ensure that a unit is made whole to RT SPP (LMP + ORDC + RDPA) to the MW level it would have been able to generate had it not been assigned AS.
Why:
If this is not done, a unit that sells its HSL in the DA would not be able to meet that obligation and would end up owing money that it would not otherwise have owed had it not been assigned AS.
This make-whole payment is effectively is in lieu of a capacity payment.
I.E. the charge to load of the AS shows up in the make-whole as opposed to the AS charge.

## Slide 5: Current Protocol Language
6.5.9.3.3 Watch
(1) A Watch is the third of three levels of communication issued by ERCOT in anticipation of a possible Emergency Condition.
(2) ERCOT shall issue a Watch when ERCOT determines that:
(a) Conditions have developed such that additional Ancillary Services are needed in the current Operating Period;
(b) There are insufficient Ancillary Services or Energy Offers in the DAM;
6.5.7.2 Resource Limit Calculator
(3) For Generation Resources, HASL is calculated as follows:
HASL = Max (LASL, (HSLTELEM – (RRSTELEM + RUSTELEM + NSRSTELEM +NFRCTELEM)))
6.7.2 Payments for Ancillary Service Capacity Assigned in Real-Time Operations
(a) For Reg-Up, if applicable:
RTAURUAMT q, r, p, i = (-1) * 1/4 * RTAURUR q, r, p * (RTSPP p, i – RTRSVPOR – RTRDP)
(b) For RRS Service, if applicable:
RTAURRAMT q, r, p, i = (-1) * 1/4 * RTAURRR q, r, p * (RTSPP p, i – RTRSVPOR – RTRDP)
Partial solution: payment of LMP for undeployed URS & RRS.
Unit backed down from NFRC range when providing AS

## Slide 6: Necessary protocol language part 1
6.7.2 Payments for Ancillary Service Capacity Assigned in Real-Time Operations
(a) For Reg-Up, if applicable:
RTAURUAMT q, r, p, i = (-1) * 1/4 * RTAURUR q, r, p * (RTSPP p, i – RTRSVPOR – RTRDP)
(b) For RRS Service, if applicable:
RTAURRAMT q, r, p, i = (-1) * 1/4 * RTAURRR q, r, p * (RTSPP p, i – RTRSVPOR – RTRDP)
(c) For NSRS Service, if applicable:
RTAURRAMT q, r, p, i = (-1) * 1/4 * RTAURNSR q, r, p * (RTSPP p, i – RTRSVPOR – RTRDP)
(d) For NFRC range, if there was no RRS or URS responsibility prior to the assignment of AS:
RTAURRAMT q, r, p, i = (-1) * 1/4 * RTAURNFRC q, r, p * (RTSPP p, i – RTRSVPOR – RTRDP)
(e) For DRS Service, if applicable:
RTAURRAMT q, r, p, i = (-1) * 1/4 * RTADDRRR q, r, p * (RTSPP p, i – RTRSVPOR – RTRDP)
Undeployed NSRS, deployed DRS, and NFRC gets paid LMP

## Slide 7: Necessary protocol language part 2
6.7.2 Payments for Ancillary Service Capacity Assigned in Real-Time Operations
(f) For HSL – RT telemetered energy:
the generator has to pay back the marginal cost of production
Current protocols back out savings from energy not produced

## Slide 8: Necessary protocol language part 3
6.7.5 Real-Time Ancillary Service Imbalance Payment or Charge
(1) Based on the Real-Time On-Line Reliability Deployment Price Adders, Real-Time On-Line Reserve Price Adders and a Real-Time Off-Line Reserve Price Adders, ERCOT shall calculate Ancillary Service imbalance Settlement, which will make Resources indifferent to the utilization of their capacity for energy or Ancillary Service reserves, as set forth in this Section.
(2) The payment or charge to each QSE for Ancillary Service imbalance is calculated based on the price calculation set forth in paragraph (12) of Section 6.5.7.3, Security Constrained Economic Dispatch, and applied to the following amounts for each QSE:
(c) The amount of Ancillary Service Resource Responsibility for Reg-Up, RRS and Non-Spin (exempting quantities of AS Assigned in Real-Time Operations) for all Generation and Load Resources represented by the QSE for the 15-minute Settlement Interval.
…..
(7) The payment or charge to each QSE for the Ancillary Service imbalance for a given 15-minute Settlement Interval is calculated as follows:
This allows headroom to get paid RDPA+ORDC.

## Slide 9: Example for HE16 (current protocols)
This is an example for a CC (10MW HSL with 1MW of that being NFRC) that is assigned AS under current protocols.
DA TPO sale: 10 MW. (HSL=10 MW)
DA SPP = $7500

## Slide 10: Example for HE16 (current protocols)
DA TPO sale: 10 MW. (HSL=10 MW)
DA SPP = $7500
RT RRS assigned: 2 MW. [NFRC = 1 MW]
HASL = 7 MW

## Slide 11: Example for HE16 (current protocols)
DA TPO sale: 10 MW. (HSL=10 MW)
DA SPP = $7500
RT RRS assigned: 2 MW. [NFRC = 1 MW]
RT metered gen = HASL = 7 MW
SPP = $9,000 (LMP=$6000 & ORDC = $3,000 & RDPA = $0)

## Slide 12: Example for HE16 (current protocols)
DA TPO sale: 10 MW. (HSL=10 MW)
DA SPP = $7500
RT RRS assigned: 2 MW. [NFRC = 1 MW]
RT metered gen = HASL = 7 MW
SPP = $9,000 (LMP=$6000 & ORDC = $3,000 & RDPA = $0)
RT invoice: owes ERCOT $12,000
  Paid 9 MW * $6,000 + 8 MW * $3,000 = $78,000
  Pays DAM sale of 10 MW * $9,000 = $90,000
The generator incurs a 13% loss in revenue from being assigned AS.
Paid LMP: RTMG of 7mw + RRS of 2mw
Paid ORDC+RDPA: RTMG of 7mw + NFRC of 1mw