## Slide 1
NPRR 1090: ERS Winter Storm Uri Lessons Learned Changes and Other ERS Items
ERCOT Staff
July 30, 2021 DSWG Meeting

## Slide 2: NPRR 1090 items
ERS deployment instructions
ERS Contract Period renewals
Weather-Sensitive ERS Resource deployments
Scheduled Unavailability and Planned Maintenance
ERS Contract Period Availability
QSE portfolio-level event performance (1)
ERS Resource-level event performance and testing criteria
ERS Self-tests
QSE portfolio-level event performance (2)

## Slide 3: NPRR 1090 item #1: ERS deployment instructions
Proposed changes:
  At the request of ERCOT Operations, eliminating the requirement to issue a Verbal Dispatch Instruction (VDI) to deploy/recall ERS, relying solely on the Extensible Markup Language (XML) message instead.
Issues to be resolved:
  ERCOT Operations considers the requirement of issuing a VDI to deploy/recall ERS an unnecessarily complicated step to take during emergencies given the viability of relying solely on the XML message.

## Slide 4: NPRR 1090 item #2: ERS Contract Period renewals
Proposed changes:
  Modifying and clarifying language related to the beginning and end of ERS Contract Periods for ERS renewals.
Issues to be resolved:
  Language related to the renewal of ERS should make it clear that ERCOT has the flexibility to declare when exhausted ERS service types will be renewed for some or all ERS Time Periods, thus beginning a new ERS Contract Period.

## Slide 5: NPRR 1090 item #3: Weather-Sensitive ERS Resource deployments
Proposed changes:
  Removing the limit on the maximum number of deployments per ERS Contract Period.
  Removing the three-hour maximum limit per single deployment event.
  Modifying language related to the cumulative deployment obligation time requirement for Weather-Sensitive ERS Resources.
Issues to be resolved:
  The deployment rules for Weather-Sensitive ERS Resources add unnecessary complications and risks for ERCOT Operations during emergency events.
  The deployment rules for Weather-Sensitive ERS Resources are inconsistent with Non-Weather-Sensitive ERS Resources, creating unnecessary complexity for ERCOT Operations.

## Slide 6: NPRR 1090 item #4: Scheduled Unavailability and Planned Maintenance
Proposed changes:
  Eliminate scheduled unavailability for ERS Loads and planned maintenance for ERS Generators.
Current rules:
  ERS QSEs may submit scheduled unavailability or planned maintenance for an ERS Resource to exclude up to 2% of their obligated intervals during an ERS Standard Contract Term from ERS Availability and Event performance calculations if submitted at least three calendar days in advance of the requested start date.
  If ERS is instructed to deploy during an interval when an ERS Resource is on scheduled unavailability or planned maintenance, the ERS Resource is not required to deploy during that event.
  ERS Resource unavailability and maintenance can be accounted for within the 5% allowance they have to successfully meet their performance requirements for ERS Availability and Events.

## Slide 7: NPRR 1090 item #4: Scheduled Unavailability and Planned Maintenance
Issues to be resolved:
  Discrepancy between how many ERS megawatts ERCOT Operations instructs to deploy during emergencies and the amount that are actually required to deploy.
  Challenges with updating the ERCOT deployment manager due to variability of when scheduled unavailability and planned maintenance submissions are received and the duration of such submissions.
  Misalignment between the actual amount of ERS megawatts required to deploy and the amount used to calculate the Real-Time On-Line Reliability Deployment Price Adder.
  Because ERS Resources and portfolios can be large in size, the three-day notice requirement is a reliability risk for ERCOT during emergencies.
  ERS QSEs should be able to account for any issues their ERS Resources may encounter within the 5% performance allowance for ERS Availability and Events.

## Slide 8: NPRR 1090 item #5: ERS Contract Period Availability
Proposed changes:
  Modifying language related to short ERS Contract Period availability calculations for ERS Resources to account for all cases in which a short Contract Period can occur.
  Modifying the formula for the ratio of Availability Factor Hours to include all awarded hours in the ERS SCT.
Issues to be resolved:
  The current language does not account for all cases in which ERS Resources participating in a short ERS Contract Period should be eligible to have a reduced threshold apply to their availability performance requirements for the shortened ERS Contract Period. The proposed changes will allow all cases for a short ERS Contract Period to be accounted for.

## Slide 9: NPRR 1090 item #6: QSE portfolio-level event performance
Proposed changes:
  Removing the requirement to reduce the time-weighting factor for intervals by 25% after an ERS Resource has been deployed for 8-hours.
Issues to be resolved:
  The requirement to reduce the time-weighting factor for intervals by 25% after 8-hours of deployment add unnecessary complexity to event performance calculations and should have been removed when NPRR 451 was approved in 2012, which limited maximum deployment times for an ERS Resource to 12 hours.

## Slide 10: NPRR 1090 item #7: ERS Resource-level event performance and testing criteria
Proposed changes:
  Removing event performance criteria language for ERS Resources related to the first full interval of an ERS deployment event.
  Modifying and clarifying language related to successful performance during ERS deployment events to satisfy annual testing requirements.
Issues to be resolved:
  Cleanup: Performance during the first full interval of an event is not necessary to include in the event performance criteria language for an ERS Resource, but rather should be added as a clarification to the criteria that will satisfy annual testing requirements for an ERS Resource.

## Slide 11: NPRR 1090 item #8: ERS Self-tests
Proposed changes:
  Removing language related to testing ERS Generators for failing self-tests.
Issues to be resolved:
  Cleanup: All language related to ERS self-tests should have been removed when self-tests were eliminated as part of NPRR 1060.

## Slide 12: NPRR 1090 item #9: QSE portfolio-level event performance
Proposed changes:
  Modifying QSE-level event interval performance to also include capacity weighting.
Issues to be resolved:
  Capacity weighting was unintentionally left out of QSE-level event performance calculations, leading to inconsistencies with similar performance calculations that are done at the end of the Standard Contract Term.
  Not accounting for capacity weighting can also lead to unintended issues with performance calculations. For example:
    ERS deployment event has 30 intervals: QSE has 29 intervals of 200MW obligation and one interval of 1MW obligation -- QSE performance for the last interval with 1MW obligation should not be weighted equally with the other 29 intervals.

## Slide 13: Timeline
DSWG 07/30/21
PRS Language Consideration 08/12/21
WMS 09/01/21
PRS Impact Analysis Review 09/16/21
TAC Consideration 09/29/21
Board Consideration 10/12/21
PUC Consideration TBD
Effective date (Dec21-Mar22 SCT)* 12/01/21
*Changes to Section 3.14.3.3 (Weather-Sensitive deployment rules) are intended to become effective upon system implementation

## Slide 14: Questions?
ON
OFF
Contact ERS@ercot.com with additional questions