## Slide 1
Operational Reserves Update
Jeff Billo
TAC
July 28, 2021

## Slide 2: Background
At the June 30, 2021 Special TAC meeting, ERCOT announced changes in Ancillary Services quantities effective July 12 through August 31 based on recent operating conditions.
  At that meeting TAC also approved OBDRR031 which changed Non-Spinning Reserve Service (Non-Spin) Deployment.
Based on stakeholder feedback and further discussion, ERCOT proposes to make an additional change to Ancillary Service quantities for September through December.

## Slide 3: Proposed Change For September-December 2021
Procure additional Non-Spin such that Regulation Up, Non-Spin and RRS, less RRS expected to be provided by Load Resources (CLR and NCLR), is equal to 6500 MW.
  i.e.: Regulation Up + Non-Spin + RRS – (RRS expected to be provided by Load Resources) = 6500 MW
What is not changing:
  Continue to procure a floor of 2800 MW of RRS over peak hours.
  The minimum 6500 MW sum of upward Ancillary Services as described above will be procured in all hours.
  An additional up to 1000 MW of Non-Spin will be procured on days identified as having the potential for high variability in the weather forecast.
See accompanying spreadsheet for Ancillary Service quantity details by month.

## Slide 4: Next Steps
ERCOT requests stakeholders to provide comments on the proposed change by Noon on August 3.
ERCOT will send a market notice in early August to inform the market of the September-December Ancillary Service quantities.
ERCOT has begun the process of considering changes for the 2022 Methodologies for Determining Ancillary Services and will bring initial thoughts on changes to future stakeholder meetings.

## Slide 5: Questions?