## Slide 1
Operational Reserves and Ancillary Services Update
Jeff Billo
TAC
August 27, 2021

## Slide 2: Background
At the July 28, 2021 TAC meeting, ERCOT proposed changes in Ancillary Services quantities for September through December based on recent operating conditions.
TAC requested information regarding the need for the additional operating reserves and related pricing impacts.
  This presentation (slides 6-9) contains some initial information on the need for additional operating reserves.
  ERCOT is providing a separate presentation on the pricing impacts.
Since the July 28 TAC meeting, there have been related stakeholder meeting discussions:
  August 11, PDCWG: Initial discussion on 2022 Ancillary Services Methodology.
  August 20, WMWG: Discussion on 2022 Ancillary Services Methodology, presentation on forecast variability identification process, and presentation on pricing impacts from RUC and ancillary services changes.

## Slide 3: Stakeholder Feedback
ERCOT asked for stakeholder feedback on the proposed changes by August 3.
  Feedback received is posted on the July 28 TAC meeting page.
Based on feedback received from stakeholders, ERCOT took the following actions:
  Starting September 1, on days identified as having the potential for high forecast variability, ERCOT will only procure additional Non-Spin (up to 1000 MW) for hours ERCOT determines are high-risk rather than procuring the additional Non-Spin for all 24 hours.
  ERCOT is considering changing the methodology for determining Ancillary Service quantities for 2022. These discussions have begun at PDCWG and WMWG.
  ERCOT is investigating changes necessary to allow Non-Controllable Load Resource participation in Non-Spin.

## Slide 4: Summary of Feedback
Eliminate the RUC offer floor.
Consider impacts to prices and costs to consumers.
Request ERCOT provide stakeholders with studies showing technical reasons for recent operational reserve changes.
Concerns about the amount of additional reserves for all hours of the day and all times of the year.
Disagree with continued use of RUC process and amount of capacity committed through RUC process.
Consider modifying DAM process to eliminate voluntary participation.
Consider greater participation of Load Resources in Ancillary Services. Also, don’t exclude Load Resources from reserve calculations.

## Slide 5: A Note on Load Resources
Reliability Objective | How do Load Resources help to achieve this objective?
Ensure sufficient physical responsive capability (PRC) to prevent system from entering emergency conditions during peak hours. | Load Resources participate in Responsive Reserve Service, thus contributing directly to PRC. The additional 500 MW of RRS procured over peak hours since July 12 has been primarily supplied by Load Resources.
Ensure generators with long start up times are online and available to meet unexpected net load forecast or intra-day forced outage changes. | This objective is met through the RUC process and through Non-Spin. Load Resources do not currently contribute through either of these mechanisms.

## Slide 6: 2021 ERCOT Methodologies for Determining Minimum Ancillary Service Requirements
Excerpts from Non-Spin Requirement Section:
  Non-Spin may be deployed to replace loss of generating capacity, to compensate for Load forecast and/or forecast uncertainty on days in which large amounts of reserve are not available online, to address the risk of net load ramp, or when there is a limited amount of capacity available for Security-Constrained Economic Dispatch (SCED).
  Historically, the need for Non-Spin has occurred during hot weather, during cold weather, during unexpected changes in weather or following large unit trips to replenish reserves.
  The periods when load is increasing and wind is decreasing requires other generation resources to increase output or come online quickly to compensate for the sudden net load increases. As a result, net load ramp risk should be accounted for in the determination of Non-Spin requirements. While net load forecast analysis may cover reserves required for forecast uncertainty, it may not necessarily cover exposure to the loss of generation and net load ramp risk. Due to this risk, it may be necessary for ERCOT to have additional reserves available during high risk using a variable percentile to protect against forecast uncertainty.

## Slide 7: Non-Spin Sufficiency for 3-Hour Ahead Net Load Forecast Error and Thermal Forced Outages
June 1 through August 15, 2021 sufficiency of hourly Non-Spin requirement to cover the daily maximum 3-hour ahead net load forecast error (NLFE) and the additional thermal generation forced outages since midnight for that hour

## Slide 8: Non-Spin Sufficiency for 6-Hour Ahead Net Load Forecast Error and Thermal Forced Outages
June 1 through August 15, 2021 sufficiency of hourly Non-Spin requirement to cover the 6-hour ahead net load forecast error (NLFE) and the additional thermal generation forced outages since midnight for that hour.
Negative value represents that there were times during the day when the hourly non-spin requirement was less than the 6-Hour-Ahead Net Load Forecast Error and the additional thermal forced outage since midnight.
Non-Spin Requirement minus NLFE and Forced Outages

## Slide 9: Non-Spin Sufficiency for 6-Hour Ahead Net Load Forecast Error and Thermal Forced Outages for Peak Hours
June 1 through August 15, 2021 sufficiency of hourly Non-Spin requirement to cover HE15-HE22 6-hour ahead net load forecast error (NLFE) and the additional thermal generation forced outages since midnight for that hour.
Negative value represents that there were times during peak hours when the hourly non-spin requirement was less than the 6-Hour-Ahead Net Load Forecast Error and the additional thermal forced outage since midnight.
Non-Spin Requirement minus NLFE and Forced Outages

## Slide 10: Questions?