## Slide 1
Proposed Change to Steady-State Transmission Planning Load Forecast Boundary Threshold
John Bernecker
Manager, Transmission Planning Assessment

## Slide 2: Boundary Threshold Overview
As required by Planning Guide Section 3.1.7, ERCOT compares its internally developed forecast to the aggregated forecasts of the TSPs (by weather zone) and applies the following process:
  In zones where ERCOT forecast is higher, use the ERCOT forecast distributed to each substation consistent with the TSP load allocations by substation
  In zones where TSP forecast is higher than ERCOT forecast, but below the ERCOT forecast plus a boundary threshold, use the TSP forecast
  In zones where TSP forecast is greater than the ERCOT forecast plus the boundary threshold, reduce the TSP forecast to match the ERCOT forecast plus the boundary threshold
ERCOT also incorporates new customer requests (based on contracts executed between customers and the TSPs) into the forecast independently of the boundary threshold analysis
The boundary threshold is currently 5% except for the Far West zone (7.5%)
  Far West zone was increased in late 2018 to allow more proactive development of transmission to meet the needs of oil and gas customers in the Permian Basin

## Slide 3: Boundary Threshold Overview
The boundary threshold process for the Regional Transmission Plan (RTP) is depicted in this chart:

## Slide 4: Boundary Threshold Observations
In the 2021 Regional Transmission Plan (RTP), the demand forecasts for six of the eight weather zones were limited by the boundary threshold.
In the final year (2027) of the 2021 RTP, the TSP-developed forecasts for the six bounded zones ranged from 6.8% to 11.2% above the ERCOT-developed forecast.
For that year in the RTP, bounding these six zones resulted in a reduction of demand of approximately 2,800 MW.

## Slide 5: Boundary Threshold Proposal
Increasing the boundary threshold provides the TSPs more flexibility to account for the needs of fast-growing areas on their systems.
  Such a change appears increasingly needed as areas of Texas experience significant population growth and as increasing numbers of large consumers (such as new data centers) propose new facilities with accelerated development timelines.
Increasing the boundary threshold to 7.5% would be a reasonable initial step to better account for the changing needs of the grid.

## Slide 6: Request for TAC Recommendation
At the September 23, 2021 Open Meeting the PUC directed ERCOT to pursue an increase in the boundary threshold to 7.5% for all weather zones.
Planning Guide Section 3.1.7(f) requires that ERCOT-proposed revisions to the boundary threshold be recommended by TAC and approved by the ERCOT Board.
ERCOT respectfully requests that TAC recommend that the boundary threshold be increased to 7.5% for all weather zones.