## Slide 1: Wholesale Market Working Group Report to WMS
David Detelich
Murali Sithuraj
October 6, 2021
From September 22 WMWG Meeting

## Slide 2: 2022 ERCOT Ancillary Service Methodology
ERCOT presented the proposed methodology for setting the 2022 AS quantities
Regulation
  ERCOT is not proposing any change to the methodology used to compute the minimum Regulation Service requirements for 2022.
  Solar Adjustment Tables track incremental MWs of Regulation needed to account for additional variability per 1000 MW increase in installed solar capacity.
  Regulation up exhaustion during some intervals in HE18 to HE21 in June/July were mainly due to larger solar ramps that were not fully accounted in GTBD
RRS
  A floor of 2800 MW will be applied to RRS quantities during the peak.
  The additional RRS has directly impact ERCOT’s PRC during the peak hours.
  This change has effectively helped increase ERCOT’s operating margin during hours with higher net load.

## Slide 3: 2022 ERCOT Ancillary Service Methodology
Non-Spin
  ERCOT is proposing the following changes to the methodology used to compute minimum Non-Spin requirements in 2022
    Update the hourly net load forecast uncertainty calculation to use
      the 6 Hours-Ahead net load forecast, and
      the highest 5-min net load within the hour
    Change percentile coverage to vary between 85th and 95th . The applicable coverage for any hour will continue to be based on risk of net load up ramp in the hour
    Build a table that tracks historical intra-day variations in thermal resource availabilities due to Forced Outages and use it to incrementally increase Non-Spin quantities.
  ERCOT will continue the practice of monitoring the weather near Real Time and may procure up to an additional 1,000 MW of Non-Spin for Operating Hours that are identified as having an increased potential of high forecast variability that may cause a higher net load during these hours.
  The Resulting quantities are not quite as high as the 6,500 MW method, although some hours are at or exceed that level
ERCOT will present more information at the October 25th WMWG meeting

## Slide 4: Impacts of AS Methodology Discussion
Possible limitations on RRS carried on Energy Storage Resources – WMWG Action Item
  ERCOT has selected a vendor for a study on RRS
  Included in the scope is possible limits on RRS PFR by technology
Impacts on prices and unit commitment
  Should NSRS quantities be reflected in ORDC calculation?
  Does the methodology reduce the incentive for self commitment and thus increased RUC will continue?
  Update the LOLP calculation or other market mechanisms (out of scope)
  Can the impact on DAM and RTM prices be analyzed?

## Slide 5: Load Forecast Performance
ERCOT presented an update on the load forecasting process
  Weather data inputs to the load forecasting models has been changed to use the most extreme weather forecasts
  This produces more conservative load forecasts per directive
  MAPE is not overly affected
  Peak load has been under forecast for most days in August and September
Load forecasting department is responsible for creating the Forecast Variability Report and for reviewing the various wind and solar forecasts to quantify the risk associated with each
ERCOT would like to know what reporting and statistics would be beneficial for the market participants

## Slide 6: Review of Forecast Variability
Beginning Sep 1, 2021, ERCOT has updated the Forecast Variability report for the Current Day + 3 to include separate variability assessments for peak and off-peak hours.
ERCOT is considering if the step to determine whether additional Non-Spin quantities are needed can be delayed by one day.
  This will allow ERCOT to use the updated forecast from 2 days prior to the operating day. Uncertainties in the forecasts generally reduce closer to the operating day.
  However, this will also reduce the time between when the updated Non-Spin quantities are posted and when the DAM execution is kicked off.
Comments from stakeholders
  This is a third layer of conservatism
  This process does not consider the base amount of non-spin
  The additional 1,000 MW of NSRS seems arbitrary

## Slide 7: Other Reports
Review of the RUC instructions
  Review of the September RUC instructions posted
  Cause continues to be committed capacity is short of the 6,500 MW reserves target
Solar Forecast Performance in Summer 2021
  ERCOT analyzed the causes of the solar over forecasting issue
  The over-forecast bias in the hourly solar forecast during Summer 2021 was mostly driven by inaccurate future availability and/or capability information for certain resources in the solar forecast models.
    New units that are still in the commissioning process are not updating the outage schedule to account for the capability
    Certain resources are demonstrating a systematic reduction in their overall capability.
  ERCOT is working with the resources and QSE’s
  ERCOT is working with vendor on model updates

## Slide 8: NPRR 1091 Changes to Address Market Impacts of Additional Non-Spin Procurement
Not discussed at the WMWG meeting
Would like direction from WMS

## Slide 9: NPRR 1092 Remove RUC Offer Floor
Not discussed at the WMWG meeting
Would like direction from WMS
Do we take out the RUC Opt-Out provision?
  Can this be behavioral and therefore not require a system change?
Will these changes have impact on self commitment?
  Is there analysis that can be performed to show what the impact will be?
  Should other provisions be included?
What impact does the PUC projects on market design have on making changes like this?
  Are ORDC changes part of what the PUCT is looking at under project 52373 and thus out of scope?

## Slide 10: NPRR1084 Improvements to Reporting of Resource Outages and Derates
ERCOT was not ready to discuss the recently filed comments
They are preparing comments
Will take up again at next meeting

## Slide 11: Next meeting
October 25
Any questions?