## Slide 1: Congestion Management Working Group
Katie Rich, Chair
Andy Nguyen, Vice Chair
OCTOBER 6, 2021

## Slide 2: TAC Emergency Conditions Item No. 51/86
Review constraint management process during EEA3: How much generation was curtailed for congestion including GTCs during EEA3?
ERCOT reported the current procedures document when ERCOT would move to a 15-minute rating or constrain to a single contingency during EEA. These are contained in:
Section 7.2, EEA Implementation Checklist of the Shift Supervisor Procedures
Section 7.2, Congestion Management during EEA Levels of the Transmission and Security Desk Procedure
The NSA Inactive and Active Constraint reports posted on MIS give the market visibility into which constraints are impacted
CMWG considers this action item complete

## Slide 3: OBDRR 026, Change Shadow Price Caps to Curves and Remove Shift Factor Threshold
ERCOT provided additional analysis to incorporate historical shadow price caps and loading levels to demonstrate the operation risk of the portion of the transmission demand curve proposal where constraint loading is > 100% and <= 102% or <= 105%
The results showed most of the constraints (over the three years selected) were short in duration and were mainly irresolvable constraints (with a maximum shadow price of $2000)
There would be 139 new constraining elements with the transmission demand curve revisions
There was no resolution at CMWG following this discussion, and many market participants continue to question the viability of this proposal, so it is now appropriate for WMS to take up for a vote

## Slide 4: Improving Efficient Control of GTCs
ERCOT introduced the Not-to-Exceed (NTE) method
Under this concept, Intermittent Renewable Resources (IRRs) behind a binding GTC with a considerable impact should not exceed their SCED Base Point when the NTE is activated
ERCOT presented draft NPRR and SCR language that would charge a QSE for an IRR a Base Point Deviation Charge if the metered generation is more than 5% above its Adjusted Aggregated Base point and a flag for those IRRs that have received a Base Point below the HDL used by SCED or if the IRR has been instructed not to exceed its Base Point
ERCOT is requesting feedback and will work towards filing an NPRR and SCR

## Slide 5: Improving the CRR Auction Model
A stakeholder presented concerns about the current long-term auction models
The goal of the proposed solutions is to ensure the CRR auction has the most accurate expectation of system conditions (outages and derates) included in the auction window
One possible solution would include an estimated end date for NOMCR submissions, requiring TSPs to submit a NOMCR to bring the de-rated line back to its original/updated rate, and including a flag that designs a line outage as temporary
The alternative solution would use expected line ratings including a higher rating for scheduled line upgrades and submitting NOMCRs as soon as practicable
Next steps include getting feedback on the first proposed solution at the next CMWG meeting

## Slide 6: SCR 816, CRR Auction Bid Credit Enhancement
ERCOT presented an alternative to this SCR by posting auction results and changing the system parameters to realign the timing of data being sent from CRR to the Credit Monitoring and Management System (CMM)
ERCOT has determined during testing that a code change will be required to fully implement the earlier credit release
It is appropriate for WMS to take a vote on this SCR

## Slide 7: Congestion at the Cap
As a follow-up the August meeting, ERCOT will came back with a scenario of the distribution of shift factors associated with the 7700 MW not dispatched as well as the impact of a higher Power Balance Penalty Curve (PBPC).
By re-running the scenario with a PBPC capped at $2001, most resources had LMPs close to the cap but also experienced reduced base points
The results showed that an increase of the PBPC cap can reduce the under-generation MW under the scenario (from 7700 to 1000 MW)
While ERCOT completed the analysis, they are not preparing a proposal on this topic at this time

## Slide 8: Next Meeting: October 18
Improving the CRR Auction Model
RUCs for Congestion

## Slide 9: Questions?